## Slide 1: 8D Report for BFX-AT100 TV Screen shake
Prepared By: PQE/Rachel
Reviewed By: QA/Toney
Ben Trinh
Date: 2023-Dec-22

## Slide 2
Establish the Team
D1
  Operation leader: David Yin
  QA leader: CB Lin
PM: An Tran
PQE: Toney Tu, Rachel
TE: Mark Wu
PE : Jack Han/Micheal
RD: Tom / Cooper
Team Leader
Team Member
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 3
D2
Description the Problem
Issue Description ( 5W2H) | 
When | 2023/05/27
Who | ALT customer
Where | SK networks warehouse, Anseong, Korea.
What | ALT customer feedback that they found out 1/1000pcs has TV screen shake. Defect rate: 1/1000 = 1000 DPPM
Why | Follow SoC (P/N: 002.02753.005. DC: 2223, LC: D20220605, Vendor: AMLOGIC)
How | TV screen shake
How many | Total 1pcs (Defect rate: 1/1000 = 1000 DPPM) as below table.
No | Description Issue | S/N | MAC | Fail rate
1 | TV screen shake | 2149688001202301080266 | BCF4D4F82447 | 1000 DPPM

## Slide 4
D3
Containment Action
1. BFX-AT100 the TV screen shake this issue can not cover by test program on FATP.
2. From 14/June/2023 to now. Fii applies new test program into production to cover this issue. (Owner: TE Jones ,status: Done 06/14).
Notes: 5.26891E-07 4.96855E-07

## Slide 5
TV screen shake
TV screen OK
Note: Please view video sample.
1. Background Information
On 27/May/2023, ALT customer feedback that they found out 1/1000pcs has TV screen shake.
Defect rate: 1/1000 = 1000 DPPM
Fail symptom: TV screen shake issue
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 6
1. Retest NG sample at OBA station.
2. Re-Test OBA + FATP Verify Result
Summary: The fail symptom same as customer feedback.
- Retest NG sample at FT, FT1 station  Pass normally.
 FATP station can’t cover this issue
TV screen shake
2. Upgrade again factory FW and test NG sample at FT, FT1 station, the result as below:
No. | Station | Result
1 | FT | Pass
2 | FT1 | Pass
Screen shake
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 7
3. System level
1. Recheck production data record.
2. Recheck test log
Dot level
T level
No# | Station | Status
1 | UK | Pass
2 | FT (test HDMI video noise) | Pass
3 | FT1(test HDMI ) | Pass
4 | RC | Pass
5 | RC1 | Pass
6 | RC2 | Pass
Summary:
- Recheck production data record and test log  Did not find out any abnormal.
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 8
1. Check Visual inspection and take X-ray NG sample, result as below:
4. Board level - 1
Summary:
- Check visual inspection and take X-ray Result: No abnormality
Item | Top side | Bottom side | Result
Visual inspection |  |  | No abnormality
Item | SoC | eMMC | HDMI Connector | Filter | Result
X-ray |  |  |  |  | No abnormality
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 9
2. Measure impedance /VF on board HDMI connector of NG sample and compare with OK sample, result as table below:
5. Board level - 2
Summary: Did not find out abnormal with impedance of NG sample
Impedance/VF measurement on board HDMI Connector |  |  |  |  |  | 
Pin No | Pin Name | Description | NG sample |  | OK sample | 
 |  |  | Impedance (Ω) | VF | Impedance (Ω) | VF
1 | TX2+ | HDMI TMDS data2 negative output | 3.15M | 0.68 | 3.2M | 0.68
2 | TX2_shield | System Ground | 0 | 0 | 0 | 0
3 | TX2- | HDMI TMDS data2 positive output | 3.15M | 0.67 | 3.2M | 0.68
4 | TX1+ | HDMI TMDS data1 positive output | 3.15M | 0.67 | 3.2M | 0.68
5 | TX1_shield | System Ground | 0 | 0 | 0 | 0
6 | TX1- | HDMI TMDS data1 negative output | 3.15M | 0.64 | 3.2M | 0.68
7 | TX0+ | HDMI TMDS data0 positive output | 3.15M | 0.68 | 3.2M | 0.68
8 | TX0_shield | System Ground | 0 | 0 | 0 | 0
9 | TX0- | HDMI TMDS data0 negative output | 3.15M | 0.67 | 3.2M | 0.68
10 | TXC+ | HDMI TMDS clock positive output | 3.15M | 0.67 | 3.2M | 0.68
11 | TXC_shield | System Ground | 0 | 0 | 0 | 0
12 | TXC- | HDMI TMDS clock negative output | 3.1M | 0.68 | 3.2M | 0.68
13 | CEC | General purpose input/output bank H signal 3 | 2.0M | 0.69 | 2.2M | 0.69
14 | NC | Not Connect | NA | NA | NA | NA
15 | SCL | General purpose input/output bank H signal 1 | 1.03M | 0.6 | 1.2M | 0.62
16 | SDA | General purpose input/output bank H signal 0 | 1M | 0.6 | 1.01M | 0.61
17 | GND | System Ground | 0 | 0 | 0 | 0
18 | 5V | HDMI_PW | 1.0M | 0.49 | 1.2M | 0.55
19 | HPD | General purpose input/output bank H signal 2 | 109.6K | 0.69 | 110K | 0.69
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 10
3. Change component of HDMI block and retest screen TV. :
- Change new FIL1401, FIL1402, J1401.
Result: Fail. This issue not follow FIL1401, FIL1402, J1401 component.
- Change new SoC
 Result: Pass. This issue follow SoC component.
6. Board level - 3
Summary:
- This issue follow SoC (P/N: 002.02753.005, DC: 2223, LC: D20220605, Vendor: AMLOGIC) material have issue.
TV screen OK
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 11
1. Removed SoC and measure HDMI block pin, result as table below:
7. Component level - 1
Summary: Measure impedance/VF HDMI pins of NG SoC  Did not find out any abnormality
SoC-U1 HDMI pin impedance measurement |  |  |  |  | 
SoC_PIN NAME | Description | OK SoC Sample |  | NG SoC sample | 
 |  | Impedance | VF | Impedance | VF
C43 | HDMI TMDS data2 negative output | 7.4MΩ | 0.76 | 7.32MΩ | 0.765
C45 | HDMI TMDS data2 positive output | 7.42MΩ | 0.76 | 7.32MΩ | 0.765
E45 | HDMI TMDS data1 positive output | 7.41MΩ | 0.76 | 7.35MΩ | 0.765
G43 | HDMI TMDS data1 negative output | 7.42MΩ | 0.76 | 7.34MΩ | 0.764
J41 | HDMI TMDS data0 positive output | 7.42MΩ | 0.76 | 7.23MΩ | 0.764
J43 | HDMI TMDS data0 negative output | 7.41MΩ | 0.76 | 7.32MΩ | 0.764
L43 | HDMI TMDS clock positive output | 7.42MΩ | 0.76 | 7.32MΩ | 0.763
L45 | HDMI TMDS clock negative output | 7.45MΩ | 0.76 | 7.38MΩ | 0.763
N41 | General purpose input/output bank H signal 1 | 2.52MΩ | 0.71 | 2.756MΩ | 0.721
N43 | General purpose input/output bank H signal 3 | 2.64MΩ | 0.75 | 2.791MΩ | 0.744
R43 | General purpose input/output bank H signal 0 | 2.49MΩ | 0.71 | 2.760MΩ | 0.721
R45 | General purpose input/output bank H signal 2 | 2.61MΩ | 0.74 | 2.763MΩ | 0.729
AG45 | General purpose input/output bank H signal 4 | 2.91MΩ | 0.78 | 3.256MΩ | 0.788
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 12
2. Reball and do a swap verification SoC
8. Component level - 2
Summary:
- As analyzed above this issue follow U1-SoC( P/N: 002.2753.005, DC: 2223, LC: D20220605, Vendor: AMLOGIC ) component.
Check Screen HDMI | 1 | 2 | 3
OK board + OK SoC | OK | OK | OK
NG board + NG SoC | NG | NG | NG
OK board + NG SoC | NG | NG | NG
NG broad + OK SoC | OK | OK | OK
D4
Root Cause Analysis
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 13
As base analysis:
Occur cause: Follow SoC (P/N: 002.02753.005, DC: 2223, LC: D20220605, Vendor: AMLOGIC)
have material issue.
Escape cause: FATP can’t cover TV screen shake issue.
D4
Conclusion Root Cause
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 14
- RD improves the test program at FT1 station to cover screen shake issue.
(Done, RD Jerry improved test program and sent to factory for verification)
- TE Jones used NG unit which detected by customer to verify new test program 5times, result as table below:
Test times | Result
1 | Fail
2 | Fail
3 | Fail
4 | Fail
5 | Fail
SHK_VD Check video screen shake failure at FT1 station
Verification result
Summary: As the verification result, new test program can cover screen shake issue. Therefore, Fii applies new test program into production to cover this issue. (Owner: TE Jones ,status: Done 06/14).
1. Update new test program
D5
Corrective Action (Short term)
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 15
Fii Action:
Short term:
Verify new test program by NG sample which can cover this issue on FATP and from 14/Jun/2023 to now. Apply new test program have check shake item. 14/Jun/2023 Closed
Long term:
- Send the NG SoC material to AMLOGIC vendor futher analyze. Owner: SQE Naomi .Status: Closed
- Fii will keeping monitor for this issue on FATP. Status: On-going
D5
Corrective Action (Fii Action)
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 16
Amlogic vendor action:
1. The chip passed visual inspection and SAT.
2. The chip could bootup normally and duplicated dynamic image shake when VDDEE voltage was between 0.815V to 0.84V in Socket board.
3. The chip failed FT with function failure caused by chip encryption. The chip was not observed Pin Open/Short.
4. Through the RD analysis, the shake phenomenon was caused by VPU module abnormal
Conclusion:
- Based on FA result, the shake screen caused by VPU error is the only one case based on the Amlogic's RMA history records.
Amlogic recommends keeping monitor due to the low DPPM(<50dppm).
- Amlogic vendor hope that ALT customer will support decryption the SoC for amlogic vendor to further analysis.
- Request Amlogic vendor update new test plan to cover issue.
D5
Corrective Action (Amlogic Action)
Notes: 5.26891E-07 4.96855E-07