## Slide 1
BFX-AT100 (T99X171.00)
USB Not Recognize Failure Report
Prepared by: PE – Nguyen Nhat Nam
Reviewed by: Michael
Date: May 25th 2022

## Slide 2
Description of Problems
ALT customer brought 1pcs USB did not recognize (SN of NG product: 38D57AD806A5) to Vietnam for further analyzing on 05.04.2022..
Issue Description
USB not recognized
USB plugged in product
USB recognized

## Slide 3
Containment
OBA environment verification  USB did not recognized
Open housing checking.
Baking PCBA with 70oC in 2 days.
Recheck OBA environment verification  USB did not recognized  OBA can cover 100% this issue.
Take X-ray and VI PCBA  Did not find out any abnormal.
Recheck OBA, Take X-ray and VI PCBA

## Slide 4
- Check SFIS data record test log is normal, USB function working normal ( USB function test at FT station ).
1. Check Customer feedback unit production test log.
Summary:
- Didn’t find out any abnormal related to USB function.
Log test USB Pass
Failure Analysis – 1

## Slide 5
Failure Analysis – 2
Retest USB didn’t recognize on all test machines at FT station:
2. Retest USB didn’t recognize unit at FT station
Test Machine Name | Result
L10T99FT001 | Fail
L10T99FT002 | Fail
L10T99FT003 | Fail
L10T99FT004 | Fail
Summary: .
- Test program can cover this issue 100% at FT station.
USB test Fail
USB test Pass

## Slide 6
3. Measure Power Supply
Measure power supply of USB block of NG sample and OK sample, result as below:
- Power supply of USB block has abnormal
Summary: Check power supply of USB block (U902) found out the output voltage gradually decreases and then increases again (from 5V decrease to 3,1V and increases 5V again).
Power supply of USB abnormal
Failure Analysis – 3
Voltage measurement |  |  | 
Location | Voltage power spec(±5% VCC) | Ok sample | NG sample
L301 (VDDCPU - 0.8V) | (0.76-0.84)V | Pass | Pass
L302 (VDD_EE - 0.8V) | (0.76-0.84)V | Pass | Pass
L303 (P1V2 - 1.2V) | (1.14-1.26)V | Pass | Pass
L304 (P3V3 - 3.3V) | (3.135-3.465)V | Pass | Pass
R324 (P1V8 - 1.8V) | (1.71-1.89)V | Pass | Pass
R325 (P2V5 - 2.5V) | (2.375-2.625)V | Pass | Pass
C908 (USB_5V) | (4.75-5.25)V | Pass | Fail

## Slide 7
Failure Analysis – 4
Remove then measure impedance & voltage diode of U902 of NG sample and OK sample, result as table below:
Summary: Impedance & voltage diode measure U902 of USB block found out abnormal at pin 5 – ILIM.
No# | Pin Name | Pin Description | OK sample |  | U69 NG sample | 
 |  |  | Impedance (Ω) | VF voltage (VD) | Impedance (Ω) | VF voltage (VD)
1 | 1 - VIN | Input Power Supply. | 2.745M | 0.548 | 2.701M | 0.545
2 | 2 - GND | Ground. Connect GND to exposed pad. | 0 | 0 | 0 | 0
3 | 3 - EN/ | Chip Enable/Chip Shutdown. Pull the pin high to enable IC; Pull the pin low to shutdown IC. Do not let the pin floating. | 3.055M | 0.621 | 3.016M | 0.613
4 | 4 - | Fault Flag. Open-Drain Output. | 2.739M | 0.548 | 2.69M | 0.542
5 | 5 - ILIM | Use external resistor to set current-limit; recommended 12.75kΩ≦RILIM≦235kΩ | 3.066M | 0.618 | ∞ | ∞
6 | 6 - VOUT | Switch Output. | 2.752M | 0.589 | 2.69M | 0.582
No# | Pin Name | Pin Description | OK sample |  | U69 NG sample | 
 |  |  | Impedance (Ω) | VF voltage (VD) | Impedance (Ω) | VF voltage (VD)
1 | 1 - VIN | Input Power Supply. | 2.745M | 0.548 | 2.701M | 0.545
2 | 2 - GND | Ground. Connect GND to exposed pad. | 0 | 0 | 0 | 0
3 |  | Chip Enable/Chip Shutdown. Pull the pin high to enable IC; Pull the pin low to shutdown IC. Do not let the pin floating. | 3.055M | 0.621 | 3.016M | 0.613
4 |  | Fault Flag. Open-Drain Output. | 2.739M | 0.548 | 2.69M | 0.542
5 | 5 - ILIM | Use external resistor to set current-limit; recommended 12.75kΩ≦RILIM≦235kΩ | 3.066M | 0.618 | ∞ | ∞
6 | 6 - VOUT | Switch Output. | 2.752M | 0.589 | 2.69M | 0.582
4. Measure Impedance & Voltage Diode of U902

## Slide 8
5. Swap power supply IC (U902) of USB block
U902 swap verification
- Swap verification between NG U902 and OK U902, result as table below:
USB did not recognize | 1 | 2 | 3 | 4 | 5
OK board + OK U902 | OK | OK | OK | OK | OK
NG board + NG U902 | NG | NG | NG | NG | NG
OK board + NG U902 | NG | NG | NG | NG | NG
NG broad + OK U902 | OK | OK | OK | OK | OK
Failure Analysis – 5
- Measure output voltage of U902 (C908)  Voltage stable ~ 5V
Summary:
- Measure output voltage of U902 (C908)  Voltage stable ~ 5V
 As analysis above this issue follow U902 ( P/N: 033.00336.005 ) component (Vendor: FITI – Date code: 2139).

## Slide 9
Conclusion
As analysis above this issue follow U902 ( P/N: 033.00336.005 ) component (Vendor: FITI – Date code: 2139).
Send NG material and report to SQE: Mr. Ha. Done: 05/23/2022.
Need SQE send NG component to FITI vendor for further analysis. Due date: 06/01. Owner: SQE: Mr. Ha
See an attachment below.