## Slide 1
K18X001.00 FFC AMP Cable
Analysis Report
Prepared by: PE- Phuong
Date: 2022/05/29

## Slide 2
Background Information
- On 05/05/2022, ALT customer complaint 1pcs FFC cable not working.
- Failure status: Product no sound
1. Issue Description
Failure information:
Fox_P/N | Cus_P/N | Vendor | ERROR CAUSE
376.00039.005 | 183005-15089 | P-TWO | FFC AMP cable not working
Background Information

## Slide 3
Visual Inspection, X-Ray FFC AMP
Summary:
- Visual inspection and X-ray didn’t find out abnormally
Visual inspection
- Visual inspection FFC AMP cable , didn’t see any abnormal
Take X-ray
- X-ray FFC AMP cable didn’t find broken,.. issue
Visual inspection FFC AMP cable
X-ray FFC AMP cable

## Slide 4
FFC AMP cable checking
Summary:
- FFC AMP cable 2 points not connection FFC AMP cable NG.
1. Measure FFC AMP cable.
-Measure connection of 2 points of FFC AMP cable compared with FFC AMP cable OK
 Result as table below.
Measure connection of 2 points of FFC AMP cable
FFC AMP cable measurement |  |  | 
Pin Name | Value( Ω)-OK sample | Value( Ω)- Sample 1 | Result
1- A113X_USB_DM | 0.2 Ω | ∞ | F
2- A113X_USB_DP | 0.2 Ω | ∞ | F
3- GND | 0.2 Ω | ∞ | F
4-AMP_PWM_OFF | 0.2 Ω | ∞ | F
5-AMP_Reset | 0.2 Ω | ∞ | F
6- CTRL_A113X | 0.2 Ω | ∞ | F
7- AMP_I2C_SDA | 0.2 Ω | ∞ | F
8-AMP_I2C_SCL | 0.2 Ω | ∞ | F
9-GND | 0.2 Ω | ∞ | F
10-AMP_LRCK | 0.2 Ω | ∞ | F
11-AMP_BCK | 0.2 Ω | ∞ | F
12-AMP_DATA | 0.2 Ω | ∞ | F
13-GND | 0.2 Ω | ∞ | F
14-AMP_MCLK | 0.2 Ω | ∞ | F
15-GND | 0.2 Ω | ∞ | F
1
1
NG
A point
B point

## Slide 5
FFC AMP Cable Coverage
Summary:
- NG FFC AMP cable can cover 100% on FATP
1. At test station on line
- FFC AMP cable is connection between K18X001T00 main board and 96.1531T00_AMP board, use FFC AMP cable NG assemble into OK product to test AMP version at FT1, FT2 stations,
2. Test AMP version by hand
- Re test 3 times AMP version by hand, using command “adb shell fac get_version “  check AMP version always fail( boot up of AMP board fail )
No # | 1 | 2 | 3
Sample 1 | Fail | Fail | Fail
Remark | Check AMP board version fail |  | 
Assemble to verify FFC AMP cable
Result
FFC AMP cable
FFC AMP cable
Log test fail at FT1 station

## Slide 6
Conclusion
As analysis FFC AMP cable 2 points not connection
NG FFC AMP cable can cover 100% at FT1 station( check version AMP), FT2 station( check version AMP and sound function)..
Send material and report to SQE:Mr. Sy. Done: 2022/06/01.
SQE send FFC AMP cable_376.00039.005 component to P-TWO vendor for further analysis. Due date: 2022/06/03. Owner: SQE Mr. Sy.
2022/06/03 – P-TWO vendor feedback FA report. Pls check on next sheet.

## Slide 7
Conclusion