## Slide 1
BFX-UA300 (K18X001.00) RMA
LED Not Working Report
Prepared by: Pham Huy Thuc
Approved by: Michael
Date: Aug 13th 2022

## Slide 2
D1. Establish the Team
PE: Michael, Thuc
ME: Cheng Lun, Wen Thai
PM: Ben Zheng, An Tran
PD: Ruan Wen Yong
QA: Ken, Rachel
TE: Mark Wu, Allan Pham
IE: Hai Ly, Heng Ruan
Foxconn
  MFG Director: David Yin
  QA Manager : CB Lin, Toney
Team Leader
Team Member

## Slide 3
D2. Description
- On 30/06/2022, ALT customer complaint 1pcs has LED not working at Customer SW.
- Failure status: Power LED indicator no light when plugging power supply.
1. Issue Description
Failure information:
NO# | FXC_SN | Cus_SN | MAC | Symptom | Production Date
1 | YWR0IKB | 2149695001202201006480 | A8934AFEBBD5 | Power LED indicator no light | 04/12/2022
OK sample
NG sample

## Slide 4
D3: Containment
Visual Inspection  Both top & bot side of defect unit are normal.
Take X-ray D22 location Did not find out abnormal.
1. Take X-ray and VI PCBA both Top & Bot side of NG sample LED no light
D22 – Power LED indication
In front of LED board
X-ray D22 location

## Slide 5
D3. Containment
Check FATP data record: NG product tested pass at FATP
Summary: NG product didn’t have abnormal on FATP.
2. Check FATP data record

## Slide 6
D4. Root Cause
Check log test is normal
1. Check SOP define and log test at FATP
Summary: LED function tested pass at FT1 station. OP check LED light follow SOP and test FT1 program define.
Result pass normal.
FT1
...
...
Test plan FT1 station
All LED On Pass at FT1
Check LED light follow SOP define is normal.
OP check LED light follow SOP and test program define, then OP confirm follow the result see it.

## Slide 7
D4. Root Cause
2. Measure Impedance and Voltage of D22 location.
Measure impedance of D22 location  No abnormality
Measure voltage of D22 location  Have abnormality as table below:
Location | Impedance (Ω) |  | Voltage (V) | 
 | NG sample | Ok sample | NG sample | Ok sample
LED_Red | 3.32M | 3.3M | 0V | 3.17V
LED_Green | 3.3M | 3.31M | 0V | 2.31V
LED_Blue | 3.31M | 3.3M | 0V | 2.23V
LED_PWR | 5.4M | 5.52M | 4.99V | 4.99V
Summary: Check power supply of D22 found out the output voltage abnormal at Pin1 (LED_Red), Pin2 (LED_Green), Pin 3 ( LED_Blue) .
LED Schematic

## Slide 8: D4. Root Cause
Swap verification between D22 NG sample and D22 OK sample, result as table below:
Test Time Power LED Swap | 1 | 2 | 3 | 4 | 5
OK board + OK D22 | OK | OK | OK | OK | OK
NG board + NG D22 | NG | NG | NG | NG | NG
OK board + NG D22 | NG | NG | NG | NG | NG
NG broad + OK D22 | OK | OK | OK | OK | OK
Summary:
- Swap D22 OK into NG board and retest 5 times  Result Pass 5/5 times.
- As analysis above this issue follow D22 ( P/N:123.00701.005 ) component.
3. Swap verification LED.

## Slide 9: D4. Root Cause
As analysis above this issue follow D22 ( P/N: 123.00701.005 ) component.
See FAR of D22_NG LED in attachment file below.
Root cause D22 no light : X-ray D22: The gold wire of crack position is broken. “ R G B color light presentation OPEN no light ”.
4. Conclusion Root cause.

## Slide 10
Conclusion
Summary for root cause
Root cause:
This issue happen when product Power LED indicator no light when plugging power supply.
As an analysis above D22 ( P/N:123.00701.005 ) component issue “ R G B color light presentation OPEN no light ”.
Root cause Occurrence :
1. May cause from vendor LED incoming material ( Auto test and tapping station ).
2. And may cause Fii On line process from SMT to FATP can make D22 crack/ brocken.
Root cause Escape:
1. That time ( 12-Apr ), production line did not check LED by the auto testing program.
2. OP check LED by visual inspection at FT1 station may be he did not check carefully and passed to next test
station.

## Slide 11
Conclusion
Corrective action
Action from LED vendor:
Request Everlight vendor provide corrective action for 2 risk station : Auto EL test and Tapping .
Due date: 2022/08/20

## Slide 12
Conclusion
Corrective action
Action from Fii production line:
- Apply auto check LED at FT1 station for test all LED light function . Done: 2022/04/23
- Fii will keep monitoring this issue on FATP.
FT1 test Fixture auto check all LED