## Slide 1
BFX-UA300
RGMII CLK/RXData measurement

## Slide 2: Outline
Measure point
NG and Good PCBA waveform compare
SOC delay window compare
Conclusion

## Slide 3: Measure point
RX data and clock of RGMII near SOC side.
  Suggested by Synaptics for checking end of PHY IC to SOC.
SOC side: R372: RXD0, R376: RXC
PHY side: R813 pull-high for RX delay resistor.

## Slide 4: NG and Good PCBA waveform compare(1/4)
No.1 NG IC rework onto good PCBA
  External RX delay is 0ns
  No.1 NG IC+Good PCBA: Data & clock has 167ps shift (Has CRC error)
  OK IC+Good PCBA: Data & clock has 132ps shift (No CRC error)
NO.1 NG IC+Good PCBA
OK IC+Good PCBA

## Slide 5: NG and Good PCBA waveform compare(2/4)
No.2 NG IC rework onto good PCBA
  External RX delay is 0ns
  NO.2 NG IC+Good PCBA: Data & clock has 442ps shift (Has CRC error)
  OK IC+Good PCBA Data & clock has 132ps shift (No CRC error)
NO.2 NG IC+Good PCBA
OK IC+Good PCBA

## Slide 6: NG and Good PCBA waveform compare(3/4)
No.1 NG IC rework onto good PCBA
  External RX delay is 2ns
  NO.1 NG IC+Good PCBA: Data & clock has 1.733ns shift (Has CRC error)
  OK IC+Good PCBA Data & clock has 1.848ns shift (Has CRC error)
NO.2 NG IC+Good PCBA
OK IC+Good PCBA

## Slide 7: NG and Good PCBA waveform compare(4/4)
No.2 NG IC rework onto good PCBA
  External RX delay is 2ns
  No.2 NG IC+Good PCBA: Data & clock has 1.879ns shift (Has CRC error)
  OK IC+Good PCBA Data & clock has 1.848ns shift (Has CRC error)
No.2 NG IC+Good PCBA
OK IC+Good PCBA

## Slide 8: SOC delay window compare
External RX delay | PHY IC condition | SOC Delay window
0 ns | #1 NG PHY IC | 0x06~0xB0
 | #2 NG PHY IC | 0x1E~0xAA
 | OK PHY IC | 0x00~0xB0
When RX delay is 0ns, and try to fine tune delay window on SOC delay register.
The results are:
#1 NG PHY IC Delay window is 0x06~0xB0
#2 NG PHY IC Delay window is 0x1E~0xAA
OK PHY IC Delay window is 0x00~0xB0
When RX delay is 2ns, found the CRC always error.
Try to fine tune SOC delay register, the CRC always error.
So the SOC delay register cannot fix CRC error.
Conclusion:
External RX delay suggests not to add by pull high resistor.
External RX delay | PHY IC condition | SOC Delay window
2 ns | #1 NG PHY IC | Always CRC error
 | #2 NG PHY IC | Always CRC error
 | OK PHY IC | Always CRC error

## Slide 9
Both NG PHY ICs delay waveforms are similar with OK PHY IC.
NG PHY ICs delay window is narrower than OK PHY IC.
NG PHY IC is 0x1E~0xAA(narrowest). OK PHY IC is 0x00~0xB0.
If we use delay time of only 2 NG PHY ICs to cover all PHY ICs, it seems that the sampling quantity is not enough. We still need to investigate more NG PHY ICs to fine reasonable delay value.
Next step:
Add CRC test item on FATP to collect more SOC delay window.
Will use the middle SOC delay window value to check more PHY IC and SOC.
Conclusion