## Slide 1
VN-JBD-ME
05/08/2022
K18X001.00 Strain Gauge Testing
Report

## Slide 2
K18X001.00 strain gauge report
Strain gage testing stations :
PCBA Trolley
BT Test
FFC Cable Assembly
Screw PCBA & Heatsink
Srew Housing
Verify Process:
+ Step 1 : At PCBA Trolley
+ Step 2 : At test BT
+ Step 3 : FFC Cable Assembly
+ Step 4 : Screw PCBA &Heatsink
+ Step 5 : Screw Housing
Station | PCBA Assembly
Sensor Q’ty | 2
Location Test | U1 (BGA)
Experiment Location:
U1 (BGA)
Sensor 1
Sensor2
PCBA Test sample

## Slide 3
Strain Gage Parameters:
Test Date-Time:05/08/2022
Hardware Type : cDAQ
Board Thickness(mm):1.6mm
Gage FACTOR:2.1
Gage TYPE: One axis
Nominal Resistance： 120.00 Ohm
Criteria Limit :
Following the data strain standard, conduct inspections of high-risk operations of PCBA was affected by strain gauge.
(Standard strain gauge value in the range: -400~400 uE.)
K18X001.00 strain gauge report
Strain gauge
Sensor
Test data
Fig 1
The thickness of RGW PCB

## Slide 4
Result: Measured values are within the standard of control-> PASS
Max Diagonal Value(uE):
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | SENSOR 2 | U1 | -7 | 400 | Pass
No.2 | SENSOR 1 | U1 | 70 | 400 | Pass
Station : PCBA Trolley
Step 1 : At PCBA Trolley
TRAY Trolley

## Slide 5
Station : PCBA Trolley
Image Sensor 1
Image Sensor 2
Type 1 : At PCBA Trolley

## Slide 6
Station : Test BT Station
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | SENSOR 2 | U1 | -35 | 400 | Pass
No.2 | SENSOR 1 | U1 | 51 | 400 | Pass
Max Diagonal Value(uE):
Type 2 : At test BT station
Result: Measured values are within the standard of control-> PASS

## Slide 7
Station : Test BT
Image Sensor 1
Image Sensor 2
Type 2 : At test BT station

## Slide 8
Max Diagonal Value(uE):
Station : FFC Cable Assembly
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | SENSOR 2 | U1 | -16 | 400 | Pass
No.2 | SENSOR 1 | U1 | -3 | 400 | Pass
Type 3 : At FFC Cable Assembly
Result: Measured values are within the standard of control-> PASS

## Slide 9
Image Sensor 1
Image Sensor 2
Type 3 : At FFC Cable Assembly
Station : FFC Cable Assembly

## Slide 10
Station : Screw PCBA &Heatsink
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | SENSOR 1 | U1 | 14 | 400 | Pass
No.2 | SENSOR 2 | U1 | 56 | 400 | Pass
Max Diagonal Value(uE):
Type 4 : At Screw PCBA &Heatsink
Result: Measured values are within the standard of control-> PASS

## Slide 11
Image Sensor 1
Image Sensor 2
Station : Screw PCBA &Heatsink
Type 4 : At Screw PCBA &Heatsink

## Slide 12
Station : Screw Housing
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | SENSOR 1 | U1 | 49 | 400 | Pass
No.2 | SENSOR 2 | U1 | 54 | 400 | Pass
Max Diagonal Value(uE):
Type 5 : At Screw Housing
Result: Measured values are within the standard of control-> PASS

## Slide 13
Station : Screw Housing
Image Sensor 1
Image Sensor 2
Type 5 : At Screw Housing

## Slide 14
Especially Testing item : Drop or bending the PCBA to deform
IPC9704表格 |  |  |  |  | 
编号 | 元件名 | 位置 | 应变最大值(uE) | Limit (uE) | 结果
No.1 | sensor A | U1 | 2180 | 400 | Fail
No.2 | sensor B | U1 | 1527 | 400 | Fail
Max Diagonal Value(uE):
Result: Measured values are over specifications> Fail
Note: Simulate the impact of the force to deform the PCBA or test the PCBA to drop which has the risk of cracking the BGA U1 location and the product cannot test normally.

## Slide 15
Image Sensor 1
Image Sensor 2
Result: Measured values are over specifications> Fail
Especially Testing item : Drop or bending the PCBA to deform

## Slide 16
K18X001.00 Strain gauge report
Result Strain Gauge Test Stations :
At PCBA Trolley :Pass
At test BT :Pass
FFC Cable Assembly :Pass
Screw PCBA &Heatsink :Pass
Screw Housing :Pass
Conclusion: PCBA transfer and assembly follow normal process does not find risk of BGA U1 being cracked