## Slide 1: T-project RFP
Date:2021/2/23

## Slide 2: Revision history
Revision | Content
V9 | Revised based on ALT email and Mantis on 2/20
V10 | Added the supply confirmation and the organization ranking

## Slide 3: 1. Company Introduction

## Slide 4
Foxconn Confidential & Proprietary
Foxconn Organization
(Fii)

## Slide 5
Foxconn Confidential & Proprietary
Automated Unmanned
Factories
Foxconn Industrial Internet (Fii) Company introduction
Countries
Employees
Patents
Professionals
2013
2015
2017
2019
2014
2016
2018
2020
Fii concept is born
Set up a project team to prepare for industrial internet
Fii announced to build an “Industrial Internet Ecosystem”
Fii platform at Beijing Industrial Internet Alliance Conference
Foxconn becomes the governing unit of “Alliance of Industrial Internet”(AII) , “china mobile IoT alliance“ and customization industry alliance
Fii listed on A share on Shanghai Stock Exchange
Fii selected as 1 of 16 World Economic Forum’s (WEF)advanced manufacturing “lighthouses” factories.
Fii invested LUSTER, a machine vision company, and Digiwin, a digital solution provider, aiming to further ecology and expand capacity scope in Industrial Internet.
1.2.1. General Information
1.2.2. Business History

## Slide 6
Foxconn Confidential & Proprietary
Brazil: Manaus / Sao Paulo
Mexico : Guadalajara / Giuded Juarez
Nanning / Long-Hua /
Song-Jiang / Guanlan /
Hang-Zhou / Chong-Qing
USA : San Jose / Santa Clara / Houston
China － 6 branches
North America － 3 branches
1.2.3. Fii major business sectors: FG Group Branch

## Slide 7
Foxconn Confidential & Proprietary
Products
Services
Wifi/ LTE/ AP
STB
TV Conference
PND
BTS
OTT
Server
ATS/ PDU/ BBU
xDSL/ Modem
IDC device
Home Gateway
Switch/ Router/ Smart Gateway
IP Phone/ Radio
Storage Controller/ JBOD/ SSD
Rack
Containerized Data Center
Integration
Server
Filter
4G/ Fiber
Smart Life
Data Center
Smart Factory
Mobile Broadband
Smart City
Smart Home
IoT/ IoE
Internet +
1.2.3. Fii major business sectors

## Slide 8
1.2.4. Manpower/organization composition for T-project
PM/Sales/SW/HW
Kevin Liu/Peter Lan
BU Head, 25yr/27yr
Tiffanie Lai
Sales,9yr
Henry Chiou
RD PM,5yr
Rick Chen
R&D head, 28yr
Jacky Chiang
Software RDPL/ 19yr
Vincent Tung
Sales/PM head,21yr
River Wong
Chief Engineer, 18yr
Jim Chen
Senior Engineer,15yr
Jason Ling
Senior Engineer,12yr
Jerry Lin
Senior Engineer,15yr
Bcan Yeh
Senior Engineer,14yr
Sam Yang
Senior Engineer,4yr
Peter Chen
Junior Engineer,3yr
Brent Choi
Junior Engineer,1yr
Catherine Chen
Senior Engineer,6yr
Tom Lee
HW Lead/ 20yr
Fu-Chiang
Senior Engineer,14yr
Kerwin Chen
SW Lead/ 18yr
Sean Chiang
Hardware RDPL/ 19yr
Premium
Advance
Intermediate
Beginner

## Slide 9
Charge Tseng
ME leader,20yr
Ace Liu
Senior engineer,5yr
Kenji Chen
HWQA leader, 18yr
Tommy Chen
Senior engineer, 13yr
Leif Lin
Senior engineer, 12yr
Andy Qin
Layout leader,16yr
Ming Rong
Senior engineer, 6yr
Enya
Senior engineer, 7yr
Allen Chang
Package leader, 16yr
Lydia Liu
Senior engineer, 4yr
Jason Kung
Compliance leader, 19yr
Jonah Lee
Senior Engineer, 16yr
Wen Chao
Senior engineer, 8yr
ME
Layout
Compliance
Package
1.2.4. Manpower/organization composition for T-project
HW QA
Wilson Kao
SQA leader,20yr
James Kuo
Senior engineer,20yr
Bryan Yang
Senior engineer,12yr
Beca Ding
Junior Engineer,2yr
D.A. Wei
Senior engineer,8yr
SQA
Premium
Advance
Intermediate
Beginner

## Slide 10
1.2.4. Manpower/organization composition for T-project
David Yin
MFG site manager,16yr
Ben Trinh
MFG Lead, 12yr
Bi
CFT NPI PM, 10yr
Nelly
CFT MP PM, 2yr
Lam Chu
PM lead, 11yr
CFT team from VN Factory
Premium
Advance
Intermediate
Beginner

## Slide 11
2019
2018
Reference link: http://www.fii-foxconn.com/static/file/%E9%95%BF%E5%9B%BE.jpg
Reference link: http://www.fii-foxconn.com/static/file/032919_content.pdf
1.2.5. Business status for the last two years (sales, operating profit, net profit, etc.)

## Slide 12
Foxconn Confidential & Proprietary
1.2.6. Credit Evaluation sheet
2017-2018
Trusted Service Certificate of Industrial Internet Platform
2017 Excellent Application Case of Industrial Internet
2018 Excellent Industrial Internet Platform
One of 2018 China's Top 50 Big-Data Enterprises
2018 Pilot Demonstration Enterprise of Industrial Internet Platform Solution
2018 Intelligent Manufacturing Pilot Demonstration Enterprise
Enterprise of Industrial Internet Ecological Supply Resource Pool in Guangdong
Tianjin Smart Manufacturing and Industrial Internet Supply & Service Organization (First Batch) Platform Service Provider
The First Batch of Industrial Internet Application Benchmarking Units in Guangdong
TOP 10 out of China 50 Best Industrial Internet Enterprises
2017-2018 China Best 100 Internet Of Things
2018 TOP 15 in China Industrial Internet Platform Vitality List
2018 China Golden Great Wall Award for Smart Manufacturing
2018 Pilot Demonstration Project of Manufacturing “Entrepreneurship & Innovation” Platform
2019
Lights-off Factory Shortlisted as one of the “Manufacturing Lighthouses Network” by World Economic Forum
2019 Excellent Solution of Industrial Internet APP
2019 Most Valuable brand A-share Company
One of 50 Smartest companies of the Year of 2019
2019 Tech-innovation Pioneer of A-share Listed Companies
Fii Cloud rated as one of Top 10 Cross-industry Industrial Internet Platform by MIIT in 2019 Charitable Contribution Award of A-share Listed Companies
2019 One-stop Precision Cutting Tool APP crowned the First China Industrial Internet Contest
2019 GBA Branded company Award with Five-star rating in CSR index
2019 Fii Included in the Three major indexes of HSSUS
2020
Fii Ranks 27 out of Top 500 Market Valued Listed Companies in the Year of 2019
2020 Rated as one of the “5G+Industrial Internet” Demonstrative Pilot Program by DIIT of Guangdong Province
2020 Fii Cloud Rated as one of Top 30 Notable Industrial Internet Platform of the Year
2020 Fii’s Board Rated as The Best Board of Directors
2020 Pioneer & One of Ten Excellent Solution in New Infrastructure and Industrial Internet
2020 Zhanlu Award-Most Dynamic Platform
2020 Top 100 Solution Provider in Industrial Internet
2020 Tool MicroCloud Rated as IoT Demonstrative Program by MIIT
2020 5G Industry Application and Demonstrative Program
2020 Rated as “Smart Manufacturing Demonstrative Pilot Program” by by DIIT of Guangdong Province
2020 Added to Top 100 Dynamic Enterprise Index
2020 Fii Included in the Three major indexes of HSSUS
2020 One of Top 50 Promising Enterprises of New Infrastructure in China
2020 Top 500 of New Economy in China
2020 One of Most Respectable Listed Companies in Shenzhen
2020 One of Top 100 Valuable Enterprises
Reference : http://www.fii-foxconn.com/#/En/Home/About

## Slide 13: 1.3. ALT and Foxconn person in charge (main contact window)
Title | Name | Email
Sales/PM Head | Vincent | vincent.tung@foxconn.com
Sales | Tiffanie | tiffanie.ti.lai@fii-foxconn.com
RD PM | Henry | henry.chiou@mail.foxconn.com
R&D Head | Rick | rick.sj.chen@fii-foxconn.com
Software RDPL | Jacky | jacky.chiang@fii-foxconn.com
Hardware RDPL | Sean | sean.hy.chiang@fii-foxconn.com
Layout Leader | Andy | andy.x.qin@mail.foxconn.com
HWQA Leader | Kenji | kenji.hh.chen@mail.foxconn.com
SQA Leader | Wilson | wilson.fc.kao@fii-foxconn.com
ME Leader | Charge | charge.kc.tseng@mail.foxconn.com
Compliance Leader | Jason | jason.hj.kung@fii-foxconn.com
Package Leader | Allen | allen.wm.chang@fii-foxconn.com
MFG Lead | Ben | ben.trinh@fii-foxconn.com

## Slide 14: 3. List of Core Parts

## Slide 15
Please be noted 90% of parts are over 10WKs. The attached list doesn’t consider MLCC.
Compatible evaluation suggested parts
Part Name | No. 1 parts company | No. 2 parts company
IC DDR4 SDRAM 8Gb | Samsung | Hynix
IC DDR4 SDRAM 4Gb | Samsung | Hynix
3. List of Core Parts
Part Name | MPN | Parts manufacturer | Reason for core parts
IC MPU 1.8/3.3V SMD FCBGA393 GP | S905X4-J | Amlogic | 1,2
IC PER 3.3V BLUETOOTH | RTL8761BTV-CG | Realtek | 2
IC DDR4 SDRAM 8Gb | K4A8G165WC-BCWE | Samsung | 2
IC DDR4 SDRAM 4Gb | K4A4G165WE-BCWE | Samsung | 2
IC eMMC 16GB | KLMAG1JETD-B041 | Samsung | 2
DSP | CX20921 | Conexant | 2
AMP | AD82128 | ESMT | 2

## Slide 16: 4. Propose equipment technology and characteristics

## Slide 17: 4.2.1 Equipment Model Name
ALT check

## Slide 18
Left Panel
S905X4
SoC
DDR4
SDRAM
1G*2+512MB*2
32bits
eMMC
Flash
16GB
8bits
Crystal
24MHz
Front Panel
Reset IC
Rear Panel
HDMI
Connector
(HDMI2.1)
TMDS/DDC_I2C/CEC/HPD
DC Jack
Power Block
DC-DC
LDO
LDO
12V
VCC_3.3V
VDD_EE
VDD_CPU
VCC_3.3V
DDR4_1.2V
VCC_1.8V
eMMC_VDDQ
VCC_3.3V
USB 2.0
USB TX/RX/D+/D-
SPDIF
Optical Connector
AI Speaker
Voice LED
Power on/off button
BT5.0
IC
UART
PCB
Antenna *1
PCM
SPDIF Interface
RJ45
Connector
Power Switch
12V
CH UP/Down
Vol. Up/Down
MIC
On/Off
Speaker
4Ω, 3W
Class D Amp
I2S
GPIO
GPIO
GPIO
GPIO
RST
GPIO
GPIO
GPIO
I2C
IR receiver
GPIO/IR IN
CX20921
Voice Processor
DAC + DSP
MIC L IN
MIC R IN
Serial Flash
SPI
Crystal
24MHz
I2S
I2C
Data
CLK
Crystal
20MHz
Ethernet TX/RX
Internet LED
Power LED
IR Blaster
GPIO/IR out
4.2.2 Structure and form of proposed equipment-block diagram
LDO
VCC_3.3V
DDR4_2.5V
5V

## Slide 19: 4.2.2 System power block and power consumption chart (Maximum 11.65W)
Test Condition:
4K60Hz HDMI output, Wow Fish 3D Game (referred from AML S905X4 AH212 Power Consumption Test Report )
Speaker = Max. volume
MP1653 (3A)
VDD_EE
0.8V/773mA
Efficiency = 92%
56mA
73.5mA
MP1653 (3A)
Efficiency = 92%
VDDCPU
1.05V/773mA
MP1657 (2A)
180mA
Efficiency = 92%
eMMC
3.3V/30mA
LDO
FP6188-18S5
1.8V/87mA
1.8V/10mA
3.3V/97mA
VDDIO_BOOT
MP1657 (2A)
83.6mA
Efficiency = 85%
DDR4*4
1.2V/711mA
LDO
FP6188-18S5
AVDD18
1.8V/172mA
Voice
Processor
3.3V/49mA
3.3V/172mA
LDO
FP6188-25S5
2.5V/72mA
3.3V/72mA
BT
3.3V/38.5mA
Class-D
AMP
Efficiency = 80%
4 ohm
/3W
3.75W/
312.5mA
12V/
970.7mA/
11.65W
MP1657 (2A)
LED x3
15mA
USB2.0
500mA
HDMI
65mA
S/PDIF
5mA
265mA
Efficiency = 92%
3.3V/603mA
VDDIO_3V3
3.3V/144mA
VDDQ

## Slide 20: 4.2.2 System power block and power consumption chart (Normal 8.39W)
Test Condition:
4K60Hz HDMI output, AV1_4K_60fps
Streaming from PC, Eth on, wifi off (referred from AML S905X4 AH212 Power Consumption Test Report )
Speaker = 70% volume
MP1653 (3A)
VDD_EE
Efficiency = 90%
25.5mA
MP1653 (3A)
Efficiency = 90%
VDDCPU
0.841V/327mA
MP1657 (2A)
157.2mA
Efficiency = 91%
eMMC
3.3V/24mA
LDO
FP6188-18S5
1.8V/70mA
1.8V/10mA
3.3V/80mA
VDDIO_BOOT
MP1657 (2A)
86.8mA
Efficiency = 84%
DDR4*4
1.2V/729mA
LDO
FP6188-18S5
AVDD18
1.8V/168mA
Voice
Processor
3.3V/49mA
3.3V/168mA
LDO
FP6188-25S5
2.5V/30mA
3.3V/30mA
BT
3.3V/38.5mA
Class-D
AMP
Efficiency = 80%
4 ohm
/2.1W
2.625W/
218.8mA
12V/
699.5mA/
8.39W
MP1657 (2A)
LED x3
15mA
USB2.0
300mA
HDMI
5mA
S/PDIF
5mA
148.8mA
Efficiency = 91%
3.3V/520mA
VDDIO_3V3
3.3V/131mA
VDDQ
0.8V/844mA
62.5mA

## Slide 21
S905X4
SoC
Speaker
4Ω, 3W
Class D Amp
CX20921
MIC L IN
MIC R IN
Data
CLK
I2C
I2C
DOUT
DIN
AEC reference
DATA
DIN
Playback Audio
LRCK
BCLK
LRCK
BCLK
LRCK
BCLK
DATA
LRCK
BCLK
DATA
LRCK
BCLK
Voice Process
4.2.2 Structure and form of proposed equipment-MIC & SPK Signal Flow Block Diagram

## Slide 22
4.2.2 Structure and form of proposed equipment- Layout placement

## Slide 23: 4.2.3 Equipment components (including detailed photos)
4K OTT Board
Highlight
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Wi-Fi 2.4/5GHz 2T2R Connection | Support 802.11 ac/a/b/g/n Data rate up to 866Mbps
Power adapter | 100~240VAC input, 5V/2A DC output
23
Chipset | Memory
AML S905X4 Quad-Core Cortex-A55 ARM Mali-G31 MP2, 850MHz | 2 GB DDR3 8 GB eMMC flash
Interface | Features
-HDMI 2.1 @ 4Kp60 output x1, HDCP 2.2 -USB 3.0 Type A x1 -RJ-45 x1; 10Mbps / 100Mbps -Optical S/PDIF x 1 -IR receiver x 1 -LED for power on/off indication -DC jack for 5V @ 2A DC input | Main stream box for HEVC/4K video HLS/MS Smooth Streaming/MPEG-DASH, HDR 10/ HLG/Dolby Vision Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade
Networking | Remote Control
Wi-Fi 802.11 ac/a/b/g/n 2x2 dual band 10/100 Base-T Ethernet Bluetooth 5.0 w/ BLE | BT5.0 or IR based RCU
Operating System | 
Android 11 Widevine Level 1/PlayReady DRM support | 
Technical Specification
Fii have kicked off several 4K OTT projects based on S905X4.
Notes: 1. 一組 S/PDIF
2. 兩組 USB
3. 一組 Composite
23

## Slide 24
Google Apps
3rd Party Apps
OTT Apps
Activity Manager
Voice Assistant Activity
Linear Service
Genie Apps
Bound Apps
Unbound Apps
Android Applications
KT Operator Tier App
ExoPlayer / Media Framework
KT TV Core
Android Framework
HW Control
Media CAS API
UCEMS Client
SW Client
Base Libraries
KT Voice Assistant Service
SoC Media SDK
(Libraries)
KT CAS
(Libraries)
Android Media / System
and other Services
Android Native
(Libraries)
Linux Kernel (SoC SDK)
Drivers
Modules
…
DRM Lib
SecureOS
HAL (Audio, Graphics, Network, …etc)
Service
Firmware
4.3.1. S/W function block diagram and function description for each block

## Slide 25
Android Media Framework Architecture
Application Framework
At the application framework level is application code that utilizes android.media APIs to interact with the multimedia hardware.
Binder IPC
The Binder IPC proxies facilitate communication over process boundaries.
Native Multimedia Framework
At the native level, Android provides a multimedia framework that utilizes the Stagefright engine for audio and video recording and playback.
OpenMAX Integration Layer (IL)
The OpenMAX IL provides a standardized way for Stagefright to recognize and use AML hardware-based multimedia codecs called components.
AML provide an OpenMAX plugin named libstagefrighthw.so.
This plugin links Stagefright with AML’s codec components, which is implemented according to the OpenMAX IL component standard.
AML
AML
4.3.1. S/W function block diagram and function description for each block

## Slide 26
Android Version-up and OTA Upgrade Flow
OTA Preparation
Generate OTA file
Upload to OTA Server
Build/Release new version
SDS Client Start
Connect to OTA Server
Check version
Download and store OTA file
Reboot to recovery
Execute commands to update files in recovery
OTA Process finish
Need to upgrade
Up to date
Reboot to normal system image
Google Project Treble:
In Android 8.0 and higher, a new stable vendor interface provides access to the hardware-specific parts of Android, so device makers can deliver new Android releases simply by updating the Android OS framework—without additional work required from the silicon manufacturers
OTA Upgrade Flow
4.3.1. S/W function block diagram and function description for each block

## Slide 27
Incremental OTA
The same update flow with standard OTA
Maybe 1/10 or less OTA file size than standard OTA
Incremental OTA files: applied to specific FW only
e.g. OTA_13: applied to FW 1, upgrade to FW 3
OTA_23: applied to FW 2, upgrade to FW 3
+
=
FW 1
OTA_13
FW 3
FW 2
OTA_23
FW 3
+
=
Apply wrong incremental OTA file may cause the device unusable
FW 2
OTA_13
+
X
=
4.3.1. S/W function block diagram and function description for each block

## Slide 28
Build
environment
Unsigned images
Signing tools
secure boot key
(HW root key)
Result
Signed images
Start
Bootloader
Verify signature of boot image (HW root key)
Bootloader
Start to run image
Bootloader
Stop to run image
OK
Fail
Signing flow of secure boot
Verification flow of secure boot
Hash+signature
Security certification (recognized lab)
Amlogic S905X4: Pass certification in Riscure lab
Signing tools
The image signing tools would be provided by Amlogic
Secure Image Signing and Secure Boot Flow
4.3.1. S/W function block diagram and function description for each block

## Slide 29
If there is no response after sending a DHCP message, the retransmission interval should follow the criteria below.
  When the Discover/Offer is not received, the discover message is transmitted at '0, 4, 8, 16, 32 seconds' for the first minute, and at a certain period (15 seconds) after 1 minute. However, the period may be changed by requesting a service.
  When Request/ACK is not received, the request message is transmitted in 0, 1, 2, 2 seconds and then the discover message is transmitted.
  When ACK is not received at T1 Time (1/2 time point), a request message is transmitted in 4, 8, 16, 32 seconds and then waits until the next T2 Time.
  When ACK is not received at T2 Time (7/8 of the release time), the request message is transmitted in 4, 8, 16, and 32 seconds, and then the discover message is transmitted after waiting until the next lease time.
IP Address Setting (DHCP)
CLIENT
DHCP SERVER
1
2
3
4
5
6
STATE
INITIALIZATION
RENEWING
Discover
Offer
Request
Ack
Request
Ack
EXTEND ADDRESS LEASE
1/2 OF LEASE
7/8 OF LEASE
7
8
Request
Ack
4.3.1. S/W function block diagram and function description for each block

## Slide 30
Google Far Field Voice Pipeline
It must design an audio HAL that meets Google far field speech requirements.
A secured audio device source, AUDIO_DEVICE_IN_ECHO_REFERENCE from Android Framework, is used to pipe secured loopback audio sources such as app content player (YouTube) and external inputs (HDMI-in).
4.3.1. S/W function block diagram and function description for each block
Design consideration and conflict: Current MIC input data passes through the Conexant for Giga Genie but Google FFV design doesn’t require extra Conexant chip, so it needs Google/ Amlogic to discuss with KT for how to enable dual FFV feature.

## Slide 31
4.3.2 List of OpenSource SW licenses
Items | License
Android | Android Apache License 2.0 for userspace software, GNU GPL v2 for the Linux kernel
ffmpeg | GNU GPLv2,GPLv3
exfat | GNU GPLv2
libtiff | BSD-like license
ntfs-3g | GNU GPLv2

## Slide 32: 4.4 Function and performance – S905X4 Benchmark Test Report
Project | SC2_S905X4_AH212 Android Q |  | 
Firmware Version | http://firmware.myamlogic.com/shanghai/image/android/Android-Q/Android_TV/patchbuild/2020-08-24/ohm- |  | 
 | userdebug-android32-kernel64-GTVS-57/ |  | 
 | http://firmware.myamlogic.com/shanghai/image/android/Android-Q/Android_TV/patchbuild/2020-08-26/ohm- |  | 
 | userdebug-android32-kernel64-GTVS-61/ |  | 
Type |  |  | 2020/8/27
Benchmark |  | Project | SC2-S905X4
 |  | Hardware Spec | AH212+2G Memory
 |  | Software Spec | Android Q
 |  | CPU MAX | 2.0GHz
 |  | GPU MAX | 846MHz
 |  | DDR Frequency | DDR4 1584MHz
 |  | System Spec. | 32bit
 |  | Screen Resolution | 3840*2160
 |  | Time | 1st
Antutu v8 | Total Score |  | 95323
 | CPU | Total | 35508
 |  | CPU Mathematical | 4931
 |  | CPU Common | 7401
 |  | CPU Multi-Core | 23176
 | GPU | Total | 10820
 |  | Terracotta | out of memory
 |  | Coastline | 3161
 |  | Refinery | 7659
 | Memory | Total | 33272
 |  | RAM Access | 17582
 |  | ROM APP IO | 1332
 |  | ROM Sequential Read | 2803
 |  | ROM Sequential Write | 675
 |  | ROM Random Access | 10880
 | UX | Total | 15723
 |  | Data Security | 3806
 |  | Data Processing | 4677
 |  | Image Processing | 2441
 |  | User Experience | 4799

## Slide 33: 4.5.3 Features and excellence of the proposed solution
Main stream box for HEVC/4K video
HLS/MS Smooth Streaming/MPEG-DASH,
HDR 10/ Dolby Vision
Google casting support
BT Voice control
Preload apps for TV services
Over-The-Air image upgrade
Netflix NTS certificated
4.5.4 Eco friendly functions and technologies
Passive standby mode under 1W

## Slide 34
ISO9001
OHS600651
ISO50001
ISO140001
TL9000
SA8000
ISO14064
ESD
4.6.1 certification and patents

## Slide 35
There are 188 OTT & Smart speaker related patents (including invention patent, utility model patent and design patent)
Below is the latest 10 patent list and the complete information please refer to the attachment
4.6.1 certification and patents

## Slide 36
Reliability
Mechanical Test
Vibration Test Random (Op)
Shock test (Op)
Label Adhesion Test
Abrasion Resistance of Label Test
Logo/Printing Abrasion Test
Package Test
Temperature and Humidity Test
Static Compression Test
Random Vibration Test
Free Fall Drop Packaged
Fix Displacement Vibration Test
Reliability Standard:
IEC60068 for Environmental
ISTA-2A for Package test
3rd Party Lab.: Orange color
High Temperature & Humidity Test (Op)
Operational Temperature Range
Power on/of f with Temp.
Quicky Power on/off Test
RDT Test
MTBF Prediction
HALT Test
Non-operating drop test
Salt Spray Test
Connector Life Test
Button Life Test
Climatic Test
Thermal Profile test
Cold / Hot Start Test
Continuation of temperature cycle
EDVT
Temperature and humidity cycles test
HWQA Reliability Test Items
4.6.2 Reports of testing institutions

## Slide 37
Verify the hardware design by exposure of the product to wider temp & voltage margining.
Temperature Margin: Min Op. Temp – 5’C ~ Max Op. Temp + 5’C
Voltage Margin DC: All Power Rail +/- 5%
Voltage Margin AC: 90VAC /47Hz & 264VAC / 63Hz
EDVT
HWQA Capabilities – EDVT
Electrical Design Verification Test
Power Cycle Box
DAQ
IXIA
Power Supply
EDVT Lab
4.6.2 Reports of testing institutions

## Slide 38
Mechanical Design Verification Test
ＭＤＶＴ
MDVT
HWQA Capabilities – MDVT
Thermal Chamber
Shock Tester
Drop Tester
MDVT is comprised of dynamic (mechanical) and environmental tests. These combination of op. and non-op. tests.
Thermal Profile Measurement
Environmental Test – High/Low Temp/Hum., Altitude, UV, Rain, Dust, Salt spread…etc.
Mechanical Test - Vib & Shock, Drop, button life, cable..etc
Package Test – ISTA-2A, 3A
Product Reliability: MTBF Prediction/ demo., thermal shock…etc.
Test to failed – HALT, HASS
Env. Chambers
Thermal Shock
HALT
Vib. Test for Rack
4.6.2 Reports of testing institutions

## Slide 39
SI
HWQA Capabilities - SI Meas.
Signal Integrity Measurement
A dedicated team to work on a set of measures of the quality of an high-speed electrical signal.
IEEE802.3 10M/100M/1G/10G/2.5G/5G/40G/100G/400G Compliance Test
SFP+/QSFP+/QSFP+100 Compliance Test
DDR I/ II/ III/IV/IVLE Signal Test
UDB3.1/HDMI/PCIe/SATA
DC/DC, AC/DC, PoE
Clock Phase Noise
….etc.
Keysight 86100D
400G SI Test
DPO71604C
Keysight 86100D
MSO72304DX
Keysight N6705C
4.6.2 Reports of testing institutions

## Slide 40
SI
MDVT
EDVT
Test
Standards
IEC 60068-2 MIL-STD NEBS GR-63 CORE Telcordia SR-332 ISO7779 ISTA – 2A
IEEE 802.3
SFF-8431
JEDEC 79-4A
HWQA Test
4.6.2 Reports of testing institutions

## Slide 41
(1) General chamber:
(2) Altitude chamber:
(3) Thermal shock:
(4) Earthquake (zone 4 level):
(5) Dust & water protection (IP65):
(8) Salt fog test: 5% salt, 35℃
(6) Package test machine:
(7) Wind loading test: 61.2 m/s (wind level 17: strongest typhoon)
(9) Solar test:1120 w/m2, 55 ℃
HWQA Capabilities
4.6.2 Reports of testing institutions

## Slide 42
Anechoic Chamber
Inner Dimension : 2 m(L)×2 (W)×2m(H)
Background Noise : < 15dBA
Cut-off Frequency : 125 Hz
Anechoic Box
Inner Dimension : 0.6 m(L)×0.58 (W)×0.85(H)
Background Noise : < 25dBA
Cut-off Frequency : 120 Hz
Listening Room
Inner Dimension : 7 m(L)×6 (W)×3(H)
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than ETSI test room
Acoustic Test Equipment
4.6.2 Reports of testing institutions

## Slide 43
Speaker & Microphone Test equipment
B&K 4955 / 4191
GRAS 26AM/ 40HL
Microphone Calibrator
B&K 4231 / GRAS 42AB
B&K Nexus
Conditioning Amplifier
APx585
Power Amplifier
KMT DC3
SCAmp
Audio Test Amplifier
Soundcheck listen with RME soundcard
GRAS 12AA Microphone power module with Gain
GRAS 44AA
Mouth Simulator
B&K 4227
Mouth Simulator
Acoustic Test Equipment
Head Acoustics ACQUA
(Speech Quality
Analysis System)
Head Acoustics MFE VI.1
(Analog Front-end)
Head Acoustics MFE VIII
(VoIP SIP Ref. GW)
Head Acoustics
HMS II.3 HATS
B&K 4128c
HATS
4.6.2 Reports of testing institutions
Notes: — Adobe Audition (Cool Edit): It is a tool to generate, edit, and output various audio signals for Electro-Acoustics testing.

## Slide 44
Speaker test Items
Sound pressure level
Frequency response
Phase
Total harmonic distortion
Total harmonic distortion with noise
SNR
Power Amplifier
Microphone Pre-amplifier
Speaker
Microphone
APx585
Anechoic Chamber
Speaker & Microphone(Analog & Digital) Test
Anechoic Chamber
Analog or Digital(PDM) microphone
Record
Microphone test Items:
Frequency response
Sensitivity
Polar plots(Directivity)
Linearity
Noise floor
4.6.2 Reports of testing institutions

## Slide 45
B&K Nexus Conditioning Amplifier
Measure frequency range from 20Hz to 20KHz
Measure the sound pressure level with “A-weighting “ which approximates the response of the human ear to sounds of medium intensity
Test Items
  Sound Pressure Level
  Low-level measurement
  FFT and Real Time analysis
Acoustic Noise Test
Apx 585
Head Acoustics MFE VI.1
(Analog Front-end)
4.6.2 Reports of testing institutions

## Slide 46
Amazon ALEXA voice service test Items
Wake-word False Rejection Rate
Response Accuracy Rate (RAR)
Wake-word Detection Delay (Latency)
Wake-word False Alarm Rate (FAR)
Power Amplifier
KMT DC3
Inner Dimension : 7 m(L)×6 (W)×3(H) (larger than ETSI request 3.5 m(L)×4 (W)×2.5(H))
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than ETSI test room
Amazon ALEXA voice service test (Background noise simulation)
4.6.2 Reports of testing institutions

## Slide 47
Google ART Lab setup requirements
Listening chamber (meet the requirements of ETSI 202-396-1)
Background noise system(Canton xl plus noise speaker*4 & power amplifier KMT DC3 )
Simulated users(HEAD ACQUA Acoustic HATS 、B&K mouth simulator)
Calibration and control system (Listen Inc SoundCheck version 17)
Google ART test Items
Wake-word False Rejection Rate
Response Accuracy Rate (RAR)
Wake-word Detection Delay (Latency)
Wake-word False Alarm Rate (FAR)
Power Amplifier
KMT DC3
Inner Dimension : 7 m(L)×6 (W)×3(H)
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than test room(ETSI 202-396-1)
Google ART Test Equipment & item
Listen Inc SoundCheck version 17 with Mac OS
4.6.2 Reports of testing institutions

## Slide 48: OTT Box Test Environment
Internet
AP
HDMI
Composite
Component
OTT Box
Ethernet
Ethernet
WiFi
802.11 b/g/n/ac
WEP/WPA/WPA2
Remote
Controller
TV Sets
Sony, Panasonic, Toshiba, Sharp ...
Speakers
Dolby AV Receiver
Subjective Test
Peripheral Test
Objective Test
Audio Analyzer
- AP APX585 & AP2722
HDMI Protocol/CEC Analyzer
- Quantum Data 980 / 882E
Picture Analyzer
- Video Clarity ClearView
Digital Serial Analyzer
- TEK DSA71604B
Video Streaming
Traffic Jitter/Delay/ Drop
- Shunra Storm
Ethernet
4.6.2 Reports of testing institutions

## Slide 49
CTS Test (Compatibility Test Suite)
Internet
Wireless
Base Station
The CTS is an automated testing suite
The CTS runs on a desktop machine and executes test cases directly on attached devices or an emulator
4.6.2 Reports of testing institutions

## Slide 50: 5. Supply Records

## Slide 51
Fii works with worldwide 1st Tier Brand companies: Google, Amazon, Roku, Technicolor for worldwide carriers.
Over 15 million STB (CATV, Satellite) delivered per year
Over 30 million OTT(IPTV) delivered per year
5.1. STB supply performance of domestic and foreign paid broadcasting (IPTV/CATV/Satellite)

## Slide 52: 6. Technical Support

## Slide 53: 6. Technical Support-SW Development System
 | Source Code Control | Bug Tracking System | Android App Developer | Project Management
Foxconn Internal |  |  |  | 
Work with Customers/Chip Vendors |  |  |  | 
Git Server
Git Server

## Slide 54: 6. Technical Support-SW
Jacky Chiang
SW Manager
Kerwin Chen
SW Lead
River Wong
Android BSP- Audio HAL/drivers, system integration
Jim Chen
Android BSP- BT, system integration
Jason Ling
Android BSP-xTS
Brent Choi
Android BSP-FAE
Jerry Lin
Android BSP-OTA, Manufacturing Test
Bcan Yeh
Android BSP-Diagnostic, System Integration
Sam Yang
Android BSP-IO interface drivers, System Integration
Peter Chen
Android BSP-power management

## Slide 55
Sean Chiang
HW Manager
Tom Lee
HW Lead
Fu-Chiang Yang
HW Baseband - Audio, Video, Thermal, Power system, RCU
Catherine Chen
HW RF - BT, ANT, BQB certification
Charge Tseng
ME leader
Ace Liu
ME
Andy Qin
Layout leader
Ming Rong
Main board layout
Enya
Subboard layout
Allen Chang
Package leader
Lydia Liu
Package design
Jason Kung
Compliance lead
Jonah Lee
EMC test debug
Wen Chao
EMC test
6. Technical Support-HW/Layout/ME/Package/Compliance

## Slide 56
Wilson Kao
SQA leader
James Kuo
Dolby Cert., SIT
Bryan Yang
ATV CTS cert., SIT
Beca Ding
ATV CTS cert., SIT
D.A. Wei
Google FFV ART testing
Kenji Chen
HWQA leader
Tommy Chen
Reliability, mechanical
Leif Lin
Package test
6. Technical Support-HWQA/ SQA

## Slide 57
6. Technical Support- Reliability Test Plan
HWQA Reliability Test Items
Reliability
Mechanical Test
Vibration Test Random (Op)
Shock test (Op)
Label Adhesion Test
Abrasion Resistance of Label Test
Logo/Printing Abrasion Test
Package Test
Temperature and Humidity Test
Static Compression Test
Random Vibration Test
Free Fall Drop Packaged
Fix Displacement Vibration Test
Reliability Standard:
IEC60068 for Environmental
ISTA-2A for Package test
3rd Party Lab.: Orange color
High Temperature & Humidity Test (Op)
Operational Temperature Range
Power on/of f with Temp.
Quicky Power on/off Test
RDT Test
MTBF Prediction
HALT Test
Non-operating drop test
Salt Spray Test
Connector Life Test
Button Life Test
Climatic Test
Thermal Profile test
Cold / Hot Start Test
Continuation of temperature cycle
EDVT
Temperature and humidity cycles test

## Slide 58
Verify the hardware design by exposure of the product to wider temp & voltage margining.
Temperature Margin: Min Op. Temp – 5’C ~ Max Op. Temp + 5’C
Voltage Margin DC: All Power Rail +/- 5%
Voltage Margin AC: 90VAC /47Hz & 264VAC / 63Hz
EDVT
HWQA Capabilities – EDVT
Electrical Design Verification Test
Power Cycle Box
DAQ
IXIA
Power Supply
EDVT Lab
6. Technical Support

## Slide 59
Mechanical Design Verification Test
ＭＤＶＴ
MDVT
HWQA Capabilities – MDVT
Thermal Chamber
Shock Tester
Drop Tester
MDVT is comprised of dynamic (mechanical) and environmental tests. These combination of op. and non-op. tests.
Thermal Profile Measurement
Environmental Test – High/Low Temp/Hum., Altitude, UV, Rain, Dust, Salt spread…etc.
Mechanical Test - Vib & Shock, Drop, button life, cable..etc
Package Test – ISTA-2A, 3A
Product Reliability: MTBF Prediction/ demo., thermal shock…etc.
Test to failed – HALT, HASS
Env. Chambers
Thermal Shock
HALT
Vib. Test for Rack
6. Technical Support

## Slide 60
SI
HWQA Capabilities - SI Meas.
Signal Integrity Measurement
A dedicated team to work on a set of measures of the quality of an high-speed electrical signal.
IEEE802.3 10M/100M/1G/10G/2.5G/5G/40G/100G/400G Compliance Test
SFP+/QSFP+/QSFP+100 Compliance Test
DDR I/ II/ III/IV/IVLE Signal Test
UDB3.1/HDMI/PCIe/SATA
DC/DC, AC/DC, PoE
Clock Phase Noise
….etc.
Keysight 86100D
400G SI Test
DPO71604C
Keysight 86100D
MSO72304DX
Keysight N6705C
6. Technical Support

## Slide 61
SI
MDVT
EDVT
Test
Standards
IEC 60068-2 MIL-STD NEBS GR-63 CORE Telcordia SR-332 ISO7779 ISTA – 2A
IEEE 802.3
SFF-8431
JEDEC 79-4A
HWQA Test
6. Technical Support

## Slide 62
(1) General chamber:
(2) Altitude chamber:
(3) Thermal shock:
(4) Earthquake (zone 4 level):
(5) Dust & water protection (IP65):
(8) Salt fog test: 5% salt, 35℃
(6) Package test machine:
(7) Wind loading test: 61.2 m/s (wind level 17: strongest typhoon)
(9) Solar test:1120 w/m2, 55 ℃
HWQA Capabilities
6. Technical Support

## Slide 63
Anechoic Chamber
Inner Dimension : 2 m(L)×2 (W)×2m(H)
Background Noise : < 15dBA
Cut-off Frequency : 125 Hz
Anechoic Box
Inner Dimension : 0.6 m(L)×0.58 (W)×0.85(H)
Background Noise : < 25dBA
Cut-off Frequency : 120 Hz
Listening Room
Inner Dimension : 7 m(L)×6 (W)×3(H)
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than ETSI test room
Acoustic Test Equipment
6. Technical Support

## Slide 64
Speaker & Microphone Test equipment
B&K 4955 / 4191
GRAS 26AM/ 40HL
Microphone Calibrator
B&K 4231 / GRAS 42AB
B&K Nexus
Conditioning Amplifier
APx585
Power Amplifier
KMT DC3
SCAmp
Audio Test Amplifier
Soundcheck listen with RME soundcard
GRAS 12AA Microphone power module with Gain
GRAS 44AA
Mouth Simulator
B&K 4227
Mouth Simulator
Acoustic Test Equipment
Head Acoustics ACQUA
(Speech Quality
Analysis System)
Head Acoustics MFE VI.1
(Analog Front-end)
Head Acoustics MFE VIII
(VoIP SIP Ref. GW)
Head Acoustics
HMS II.3 HATS
B&K 4128c
HATS
6. Technical Support
Notes: — Adobe Audition (Cool Edit): It is a tool to generate, edit, and output various audio signals for Electro-Acoustics testing.

## Slide 65
Speaker test Items
Sound pressure level
Frequency response
Phase
Total harmonic distortion
Total harmonic distortion with noise
SNR
Power Amplifier
Microphone Pre-amplifier
Speaker
Microphone
APx585
Anechoic Chamber
Speaker & Microphone(Analog & Digital) Test
Anechoic Chamber
Analog or Digital(PDM) microphone
Record
Microphone test Items:
Frequency response
Sensitivity
Polar plots(Directivity)
Linearity
Noise floor
6. Technical Support

## Slide 66
B&K Nexus Conditioning Amplifier
Measure frequency range from 20Hz to 20KHz
Measure the sound pressure level with “A-weighting “ which approximates the response of the human ear to sounds of medium intensity
Test Items
  Sound Pressure Level
  Low-level measurement
  FFT and Real Time analysis
Acoustic Noise Test
Apx 585
Head Acoustics MFE VI.1
(Analog Front-end)
6. Technical Support

## Slide 67
Amazon ALEXA voice service test Items
Wake-word False Rejection Rate
Response Accuracy Rate (RAR)
Wake-word Detection Delay (Latency)
Wake-word False Alarm Rate (FAR)
Power Amplifier
KMT DC3
Inner Dimension : 7 m(L)×6 (W)×3(H) (larger than ETSI request 3.5 m(L)×4 (W)×2.5(H))
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than ETSI test room
Amazon ALEXA voice service test (Background noise simulation)
6. Technical Support

## Slide 68
Google ART Lab setup requirements
Listening chamber (meet the requirements of ETSI 202-396-1)
Background noise system(Canton xl plus noise speaker*4 & power amplifier KMT DC3 )
Simulated users(HEAD ACQUA Acoustic HATS 、B&K mouth simulator)
Calibration and control system (Listen Inc SoundCheck version 17)
Google ART test Items
Wake-word False Rejection Rate
Response Accuracy Rate (RAR)
Wake-word Detection Delay (Latency)
Wake-word False Alarm Rate (FAR)
Power Amplifier
KMT DC3
Inner Dimension : 7 m(L)×6 (W)×3(H)
Background Noise : < 30dBA
Reverberation time between 0.2 s and 0.7s
Bigger than test room(ETSI 202-396-1)
Google ART Test Equipment & item
Listen Inc SoundCheck version 17 with Mac OS
6. Technical Support

## Slide 69: OTT Box Test Environment
Internet
AP
HDMI
Composite
Component
OTT Box
Ethernet
Ethernet
WiFi
802.11 b/g/n/ac
WEP/WPA/WPA2
Remote
Controller
TV Sets
Sony, Panasonic, Toshiba, Sharp ...
Speakers
Dolby AV Receiver
Subjective Test
Peripheral Test
Objective Test
Audio Analyzer
- AP APX585 & AP2722
HDMI Protocol/CEC Analyzer
- Quantum Data 980 / 882E
Picture Analyzer
- Video Clarity ClearView
Digital Serial Analyzer
- TEK DSA71604B
Video Streaming
Traffic Jitter/Delay/ Drop
- Shunra Storm
Ethernet
6. Technical Support

## Slide 70
CTS Test (Compatibility Test Suite)
Internet
Wireless
Base Station
The CTS is an automated testing suite
The CTS runs on a desktop machine and executes test cases directly on attached devices or an emulator
6. Technical Support

## Slide 71: 7. Development Ability

## Slide 72
7.1.1 Android TV OS based UHD STB development experiences-
Android Platform Function & CTS Test Experience
Phone
&
Tablet
Tablet
Gingerbread
2.3
Honeycomb
3.2
Ice Cream
Sandwich
4.0
Jelly Bean
4.1 / 4.2
Phone
&
OTT Box
OTT Box
KitKat
4.4
Tablet
Lollipop
5.1
OTT Box
OTT BOX
Marshmallow
6.0
Nougat
7.1
Android TV
Android TV
Oreo
8.0
OTT BOX
Android TV
Android TV
OTT BOX
Pie
9.0
OTT BOX
Android TV
Android 10

## Slide 73
7.1.2 Model name of developed products-Android TV CTS Certification Experience
We already got Android TV CTS certifications for Android OTT/STB products. Below is product list we ever made in Android portal website.
There are many other projects get CTS under customer’s name done by Foxconn and not listed here below
Customer | Device | Device Type | Model Name | Launched OS Ver. | Launch Date | Upgraded OS Ver.
TBC |  | Hybrid STB(DVB-C) | TATV_8000 | Android TV 9 | Jun. 2020 | Android TV 11 (released in Q4)
SKB/ALT |  | IPTV STB | BFX-UH200 | AOSP 9 | Nov. 2019 | N/A
SKB/ALT |  | IPTV STB | BFX-AT100 | Android TV 9 | Jul. 2019 | Android TV 10
Flnet |  | OTT Box | ba201 | Android TV 7 | Jun. 2018 | N/A
PCCW |  | OTT Box | hk101 | Android TV 7 | May. 2018 | Android TV 9
CJ Hello Vision |  | OTT Box | kr101 | Android TV 7 | Nov. 2017 | Android TV 8
Flnet |  | OTT Box | ba101 | Android TV 6 | Jan. 2017 | Android TV 7

## Slide 74
Google GMS TEST & pre-CERTIFICATION for Android TV
1.CTS test – to verify device’s compatibility.
2.CTS Verifier – to verify device’s compatibility that can not be automated.
3.GTS – to verify device’s Google GMS compatibility.
4.VTS/CTS-GSI – to verify compliance to Treble architecture
5.STS – to verify device is updated with latest security patches
6. TV Test Suite (TVTS) –to verify Android TV device’s compatibility.
7.Smoke Tests – tests cover the following functionalities
8.Function test – to verify device’s functions, like network、video player、USB port…
-Audio
-Youtube
-Play Movies
-Play Games
-Remote Controls
-Voice Search
-Companion App
-Voice Actions
-Accessories
-Cast
-Standby, etc.
-Boot-up
-Launcher
-HDMI CEC
-HDMI ARC
-Component Input
-Optical Audio Out
-Restricted Profile
-Client ID check
-Serial number check
-Games
-Apps
7.4.1 xTS certification

## Slide 75
7.4.2 Netflix authentication
We have experiences to get NTS Certifications for Android TV OTT box products.
Below is Netflix certification letter for reference.

## Slide 76
7.4.2 Netflix authentication -Netflix Certification Steps
Customer needs to ask for Netflix’s permission to allow the product to enter Netflix certification.
If Netflix agrees to certificate the product. Then create a project in Netflix partner portal and fill the product related information. Also apply RAE test equipment from Netflix.
Send final product devices and RCU(Remote Control Unit) to Netflix. The Netflix logo on RCU has to meet Netflix’s requirements.
If Dolby Vision need to be supported, the product needs to pass Dolby Vision Certification first.
Pass Android TV CTS Certification.
Start internal NTS testing until all of NTS test items are passed.
Submit F/W image to Netflix to certify your device. If any critical issues fail, fix them and repeat Step 6.
Until all critical issues are fixed or Netflix agrees exemption on failed items, Netflix will give a Certification Pass Report to allow F/W image deployment.

## Slide 77
7.4.2 Netflix authentication -Netflix Certification Steps Flow

## Slide 78
Subjective / Objective / Peripheral / Video Streaming
Picture Quality Testing / AV Sync
EDID / HDCP / CEC / Hot Plug Pulse
7.4.2 Netflix authentication - Fii Netflix NTS Testing Capability

## Slide 79
Full set design review process
  SCH Lib, PCB footprint, Datasheet cross check
  Power Plan chart, Power circuit feasibility check
  Power on/off Sequence check
  Reset Circuit Feasibility Study
  Fuse component selection check
  Thermal/PI/SI/ME Simulation
  Crystal Circuit, Memory Circuit feasibility study
  Layout Guideline/Rule Check list review
  High Speed Bus/RF layout impedance check
  EMC/Safty components check, Design for EMC rule check
  MTBF Prediction, De-rating Factor Check for Key components
  DFMEA, DFM analysis
7.5.1 Design/development ability to secure STB quality stability
Design review and Design rule checklist help to reduce development period for quick time to market.

## Slide 80
SI Simulation: Allegro SigXplorer
- HDMI 2.0
- USB 3.1
- SATA 1.0/2.0/3.0
- DDR I,II,III,IV
- PCI Express
PI Simulation : Allegro Sygrity
Voltage Drop on Power Distribution and Interconnect
Circuit Design Simulation : Cadence Pspice
PCB Impedance Simulation : SI9000
RF Simulation :
1.Microwave Office
2.Advance Design System (RF Circuit /EM-wave simulation)
3.AppCAD (Tx/Rx Link budget evaluation
7.5.1 Design/development ability to secure STB quality stability

## Slide 81
Comprehensive DVT Test Items and Test Plan Database
  EMC/Safety, Regulatory test items
  HW test items
    PWR accuracy/ripple, PWR on Sequence
    Reset Timing and Sequence
    Inrush Current
    Clock accuracy/drift ,Signal Timing Measurement
    Performance test report (Front End Tuner, Wifi, Bluetooth, RF4CE, A/V…)
    Compliance test report (Ethernet 10/100/1000base-T, USB, HDMI, SATA, Dolby…)
  Mechanical and Reliability test items
    Hot/Cold Start, Hot/Cold Run-in
    Thermal/Humidity Shock, HALT test
    On/Off Test
    Drop/Vibration/Impact….
Full DVT test ensure product design quality..
7.5.1 Design/development ability to secure STB quality stability

## Slide 82
Tektronix TDS Series
- USB 2.0/3.0/3.1
- HDMI 1.4/2.0/2.1
- 802.3
- DDR1,2,3,4
- SATA 1.0/2.0/3.0
- PCI Express
High-Speed SI Measurement
7.5.1 Design/development ability to secure STB quality stability

## Slide 83
8.1 (Post) Stabilization of supply and demand to respond to coronavirus
  FXN is the working leading manufacturing company with many projects running. Thus there are many common parts to leverage to reduce the supply risk.
8.2 Initial delivery schedule and quantity:
  Please refer to schedule and ALT check MP quantity.
8.3 Year/half/quarter/monthly production quantity
  More than 4M pieces per month. Fii could adjust the capacity to meet customer long term demand.
8.5 Inventory holding and production plan to respond to unexpected demand (the level of monthly safety stock holding of contract volume (%) )
  Strategy procurement for long lead time parts
8. Delivery and Support

## Slide 84
8.4 Supply confirmation letter from major core parts maker
8. Delivery and Support
Item | File | Remark
Main Chip |  | Amlogic provides the supply confirmation letter
BT chip |  | Distributor GMI replied by email and the certificate of distribution in Chinese for reference. (no English version)
HW AEC |  | Synaptics replied by email confirmation
Memory |  | Distributor YOSUN replied by email and attached the certificate of distribution.

## Slide 85: 9. Project Organization and Structure

## Slide 86
Kevin Liu/Peter Lan
BU Head, 25yr/27yr
Tiffanie Lai
Sales,9yr
Henry Chiou
RD PM,5yr
Rick Chen
R&D head, 28yr
Jacky Chiang
Software RDPL/ 19yr
Vincent Tung
Sales/PM head,21yr
River Wong
Chief Engineer, 18yr
Jim Chen
Senior Engineer,15yr
Jason Ling
Senior Engineer,12yr
Jerry Lin
Senior Engineer,15yr
Bcan Yeh
Senior Engineer,14yr
Sam Yang
Senior Engineer,4yr
Peter Chen
Junior Engineer,3yr
Brent Choi
Junior Engineer,1yr
Catherine Chen
Senior Engineer,6yr
Tom Lee
HW Lead/ 20yr
Fu-Chiang
Senior Engineer,14yr
Kerwin Chen
SW Lead/ 18yr
Sean Chiang
Hardware RDPL/ 19yr
9.Project Organization structure PM/Sales/SW/HW

## Slide 87
Charge Tseng
ME leader,20yr
Ace Liu
Senior engineer,5yr
Kenji Chen
HWQA leader, 18yr
Tommy Chen
Senior engineer, 13yr
Leif Lin
Senior engineer, 12yr
Andy Qin
Layout leader,16yr
Ming Rong
Senior engineer, 6yr
Enya
Senior engineer, 7yr
Allen Chang
Package leader, 16yr
Lydia Liu
Senior engineer, 4yr
Jason Kung
Compliance leader, 19yr
Jonah Lee
Senior Engineer, 16yr
Wen Chao
Senior engineer, 8yr
ME
Layout
Compliance
Package
HW QA
Wilson Kao
SQA leader,20yr
James Kuo
Senior engineer,20yr
Bryan Yang
Senior engineer,12yr
Beca Ding
Junior Engineer,2yr
D.A. Wei
Senior engineer,8yr
SQA
9.Project Organization structure-
ME/ Layout/ Compliance/ Package/ HWQA/ SQA

## Slide 88
David Yin
MFG site manager,16yr
Ben Trinh
MFG Lead, 14yr
Bi
CFT NPI PM, 10yr
Nelly
CFT MP PM, 2yr
Lam Chu
PM lead, 11yr
CFT team from VN Factory
9.Project Organization structure- CFT team from VN factory

## Slide 89: 10. Quality assurance
10.1. Quality guarantee (free A/S) period of the proposed equipment Write at least 24 pieces, in 6-month increments (Example: 24 months/30 months/36 months, etc.)
  Normally 24months warranty for hardware device.
  However, it’s also possible to support 30months or 36months based on customer requirement with different business model.

## Slide 90: 11. Additional suggestions

## Slide 91
Device Management
OTA
Management
App
Management
User Behavior Analytics
Notification
Center
AD
Management
Device Management
  Device profiling, control and status
OTA Management
  Device grouping, incremental mode
App Management
  App installation, ordering, video recommendation
User Behavior Analytics
  Device related statistics – members, active users, device map, RCU button clicks
  Apps related statistics – App ranking(usage, watching, clicks), installation ranking, hour distribution
Notification Center
  Promotion/emergency notification messages
Advertising Management
  AD schedule
Dashboard UI
ACS System
11.1. Proposal STB-based differentiated service
ACS system supports operator to manage devices, OTA FW upgrade, notification, promotion, understand subscribers behavior and preference, which can lower A/S maintenance manpower.
ACS System – ATV platform Back-end System

## Slide 92
Foxconn Confidential & Proprietary
11.1. Proposal STB-based differentiated service :
For OTT Operators to understand user preference.
For next generation product planning
For new services planning
Online Status
Android Version
FW Version
HDMI Input Status
Language
Network Type
TV Brand
Model
Why ACS (Auto Configuration System)

## Slide 93
Foxconn Confidential & Proprietary
11.1. Proposal STB-based differentiated service: What can you get from ACS System
New Member Bar Chart
Location Ranking
Watching Hours
Accumulated App Clicks
App Usage Comparison
App Usage in 24 Hours
Active User Ratio
App Installation Ratio
ACS System

## Slide 94
Foxconn Confidential & Proprietary
11.1. Proposal STB-based differentiated service : ACS Functions
Device Grouping
Configuration Provisioning
Remote Screen Capture/Reboot
BT RCU Info & Un-Pairing
HDMI Output Control
Device Status Reporting
Debug/Log Collection
Firmware Upload
Group Scheduling
FW Download Progress
User/System Force Update
FW Update History
Online Status
FW Version
TV Brand
Network Type
Screen Resolution
Sound/CEC/ Language
HDMI Input Config.
Device Info Importing
Account Management
Role-Based Access Control
Bandwidth Conf.
Connection Conf.
Member Stats
Member Device Distribution
App Usage Stats
App Installation Ranking
RCU Buttons Profiling
Advanced Search
Statistics Report
Device Mgmt.
OTA
Mgmt.
Device Profiling
UBA
Admin Mgmt.
App
Mgmt.
APK File Upload
App Installation
App Icons Ordering
App Notification Center
B+ Recommendation
PS: 1. ACS: Auto Configuration System
2. OTA: Over The Air 3. UBA: User Behavior Analysis

## Slide 95
  Android TV OTT/STB roadmap
2017
2018
2019
2020
2021
2022
Dongle
OTT Box
Hybrid STB
OTT+AI Speaker
/Soundbar
BANDOTT
SANDWICH
Now E
Viewing
t.Gateway
Dongle
Far Field Mic
AirStick
SMB400
DVB-C STB
M
N
O
P
10
11
Smart3
Near Field Voice
IPTV STB
ISDB-T/S STB
8K OTT
TV Input Framework
4K AV1 OTT
AI Speaker
AI Soundbar
4K AV1 OTT
Amlogic S905X4
AV1 decoding
WiFi 6
4K AV1 Dongle
SoC: Amlogic S905Y4
AV1 decoding
AV1 Video Decoding
11.2. Future Product Plan (Road Map)

## Slide 96
Device Management
OTA
Management
App
Management
User Behavior Analytics
Notification
Center
AD
Management
Device Management
  Device profiling, control and status
OTA Management
  Device grouping, incremental mode
App Management
  App installation, ordering, video recommendation
User Behavior Analytics
  Device related statistics – members, active users, device map, RCU button clicks
  Apps related statistics – App ranking(usage, watching, clicks), installation ranking, hour distribution
Notification Center
  Promotion/emergency notification messages
Advertising Management
  AD schedule
Dashboard UI
ACS System
11.3 Additional provision function of the proposer to
improve the convenience of service use
ACS system supports operator to manage devices, OTA FW upgrade, notification, promotion, understand subscribers behavior and preference, which can lower A/S maintenance manpower.
ACS System – ATV platform Back-end System

## Slide 97
As stated in 1.2.1 Fii owns intelligent factories that applied the up-to-date technology for unmanned factory practice which could reduce the production cost.
11.4. Technology/function applied to lower CAPEX/OPEX
Automated Unmanned
Factories
Countries
Employees
Patents
Professionals