## Slide 1: Unit Line Inspector Measurement Guide <Bako2120>
1
Audio R&D Lab.
2021. 05. 27

## Slide 2: ▣ Unit Line Inspector Measurement Guide
※ System Components
Item | Description
 | Type BK2120A Speaker & Receiver Test Unit DAQ Module DIO Board ICP Amplifier Power Amplifier
 | Coupler (Cabinet) Close Type, each for Left & Right (Built-in Microphone Sensor & Cable)
 | Type BS1123 Test Program BK1090 Sound Card COM1  RS-232C 17” LCD-Monitor
Cables & Accessories | Power Cable RS232 Cable Stereo Audio Cables (55-jack to BNC) BNC to Clip

## Slide 3: ▣ Unit Line Inspector Measurement Guide
※ Measurement Environment
To BK2120 Input
Test Coupler
Microphone
Unit

## Slide 4
※ Measurement
▣ Unit Line Inspector Measurement Guide
Insert Unit to JIG & connect cable(5sec)
Measurement(10sec)
Judgement

## Slide 5
※ Frequency Response Criteria
Testing range:
- Woofer: F0 ~ 10KHz
- Full range: F0 ~ 20KHz
Reference graph: Golden sample’s FR graph(provided by supplier)
Pass/Fail Criteria: Within +/- 3dB from reference graph
Testing sweep time: 5sec
▣ Unit Line Inspector Measurement Guide
Red Graph: Reference Graph
Upper Graph: +3dB(Upper limit)
Lower Graph: - 3dB(Lower limit)