## Slide 1
Acoustic chamber production capability

## Slide 2
Production capability of acoustic chamber test
Acoustic chamber evaluation 10,000PCS/MONTH |  |  |  |  |  |  |  |  |  | 
Capability Target | 500 | Day/M | 26 | M_output | 10400 | Equipment Utilization |  |  |  | 
Station | Test time | Ping on | Load/unload | Total test time | Production HR/day | Target FPR | CT | Required acoustic chamber number | Current acoustic chamber number | Current production capability
FT2 | 950.00 | 40 | 25 | 1015 | 18.00 | 90% | 104.98 | 10 | 1 | 52
FT2: Audio acoustic chamber test
Ping on: Product power on/off time
Load/unload: OP operation time
FPR: First pass rate
Current product capability (per day) = (3600/1015) * 18 * FRP * Chamber number * 0.9 = 51.712
The target capability is 500 per day, Therefore, we need *10 chambers to meet the requirement.

## Slide 3
Detailed test items and time of FT2 test station
Test items | Test frequency points |  |  |  |  |  |  |  |  | Test time (sec)
Left speaker FR | 100Hz | 400Hz | 800Hz | 1KHz | 4KHz | 8KHz | 12KHz | 15KHz | 18KHz | 108
Left speaker THD |  |  |  |  |  |  |  |  |  | 
Left speaker Balance | 1KHz |  |  |  |  |  |  |  |  | 12
Middle speaker FR | 100Hz | 400Hz | 800Hz | 1KHz | 4KHz | 8KHz | 12KHz | 15KHz | 18KHz | 108
Middle speaker THD |  |  |  |  |  |  |  |  |  | 
Middle speaker Balance | 1KHz |  |  |  |  |  |  |  |  | 12
Right speaker FR | 100Hz | 400Hz | 800Hz | 1KHz | 4KHz | 8KHz | 12KHz | 15KHz | 18KHz | 108
Right speaker THD |  |  |  |  |  |  |  |  |  | 
Right speaker Balance | 1KHz |  |  |  |  |  |  |  |  | 12
Mic1 sensitivity | 20Hz | 100Hz | 500Hz | 1KHz | 10KHz | 24KHz |  |  |  | 120
Mic2 sensitivity | 20Hz | 100Hz | 500Hz | 1KHz | 10KHz | 24KHz |  |  |  | 120
Mic3 sensitivity | 20Hz | 100Hz | 500Hz | 1KHz | 10KHz | 24KHz |  |  |  | 120
Mic4 sensitivity | 20Hz | 100Hz | 500Hz | 1KHz | 10KHz | 24KHz |  |  |  | 120
Mic1 Isolation | 1KHz |  |  |  |  |  |  |  |  | 20
Mic2 Isolation | 1KHz |  |  |  |  |  |  |  |  | 20
Mic3 Isolation | 1KHz |  |  |  |  |  |  |  |  | 20
Mic4 Isolation | 1KHz |  |  |  |  |  |  |  |  | 20
 |  |  |  |  |  |  |  | Sub-total |  | 920
 |  |  |  |  |  |  |  | DUT connection test |  | 30
 |  |  |  |  |  |  |  | Total |  | 950
The function of calculating the test time of each test item has not been built into the DVT2 version of the test software, and only has total test time.
The test time of each test items is estimated by the vendor, not the actual test result