## Slide 1
Prepared by : PE Long
Date : 2023/06/26
BFX-AT100 TV screen shake
FA Report

## Slide 2
Issue Description ( 5W2H) | 
When | 2023/05/27
Who | ALT customer
Where | SK networks warehouse, Anseong, Korea.
What | ALT customer feedback that they found out 1/1000pcs has TV screen shake. Defect rate: 1/1000 = 1000 DPPM
Why | Suspect SoC material (P/N: 002.02753.005. DC: 2223, Vendor: AMLOGIC)
How | TV screen shake
How many | Total 1pcs (Defect rate: 1/1000 = 1000 DPPM) as below table.
No | Description Issue | S/N | MAC | Fail rate
1 | TV screen shake | 2149688001202301080266 | BCF4D4F82447 | 1000 DPPM
Problems description
#1
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 3
Problems description
TV screen shake pictures
#2
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 4
Containment
Recheck production data record.
- This unit passed all station normally, no found any abnormal.
2. Recheck test log
No# | Station | Status
1 | UK | PASS
2 | FT (test HDMI video noise) | PASS
3 | FT1(test HDMI ) | PASS
4 | RC | PASS
5 | RC1 | PASS
6 | RC2 | PASS
Summary:
- Recheck production data record and test log  Did not find out any abnormal.
#3
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 5
#4
1. Upgrade again factory FW and retest NG sample at FT, FT1 station, the result as below:
Root cause analysis
Summary: The fail symptom same as customer feedback and FATP station can’t cover this issue.
TV screen shake at OBA station
2. Retest NG sample at OBA station.
No. | Station | Result
1 | FT | Pass
2 | FT1 | Pass
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 6
3. Check Visual inspection and take X-ray NG sample, result as below:
Root cause analysis
Summary:
- Check visual inspection and take X-ray  Result: No abnormality
Item | Top side | Bottom side | Result
Visual inspection |  |  | No abnormality
Item | SoC | eMMC | HDMI Connector | Filter | Result
X-ray |  |  |  |  | No abnormality
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 7
4. Measure impedance /VF on board HDMI connector of NG sample and compare with OK sample, result as table below:
Root cause analysis
Summary: Did not find out abnormal with impedance of NG sample
Impedance/VF measurement on board HDMI Connector |  |  |  |  |  | 
Pin No | Pin Name | Description | NG sample |  | OK sample | 
 |  |  | Impedance (Ω) | VF | Impedance (Ω) | VF
1 | TX2+ | HDMI TMDS data2 negative output | 3.15M | 0.68 | 3.2M | 0.68
2 | TX2_shield | System Ground | 0 | 0 | 0 | 0
3 | TX2- | HDMI TMDS data2 positive output | 3.15M | 0.67 | 3.2M | 0.68
4 | TX1+ | HDMI TMDS data1 positive output | 3.15M | 0.67 | 3.2M | 0.68
5 | TX1_shield | System Ground | 0 | 0 | 0 | 0
6 | TX1- | HDMI TMDS data1 negative output | 3.15M | 0.64 | 3.2M | 0.68
7 | TX0+ | HDMI TMDS data0 positive output | 3.15M | 0.68 | 3.2M | 0.68
8 | TX0_shield | System Ground | 0 | 0 | 0 | 0
9 | TX0- | HDMI TMDS data0 negative output | 3.15M | 0.67 | 3.2M | 0.68
10 | TXC+ | HDMI TMDS clock positive output | 3.15M | 0.67 | 3.2M | 0.68
11 | TXC_shield | System Ground | 0 | 0 | 0 | 0
12 | TXC- | HDMI TMDS clock negative output | 3.1M | 0.68 | 3.2M | 0.68
13 | CEC | General purpose input/output bank H signal 3 | 2.0M | 0.69 | 2.2M | 0.69
14 | NC | Not Connect | NA | NA | NA | NA
15 | SCL | General purpose input/output bank H signal 1 | 1.03M | 0.6 | 1.2M | 0.62
16 | SDA | General purpose input/output bank H signal 0 | 1M | 0.6 | 1.01M | 0.61
17 | GND | System Ground | 0 | 0 | 0 | 0
18 | 5V | HDMI_PW | 1.0M | 0.49 | 1.2M | 0.55
19 | HPD | General purpose input/output bank H signal 2 | 109.6K | 0.69 | 110K | 0.69
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 8
5. Change component of HDMI block:
- Change new FIL1401, FIL1402, J1401 then retest screen TV at OBA.
Result: Fail
Root cause analysis
Summary: After change new FIL1401, FIL1402, J1401 then retest Screen TV at OBA , result: screen TV still (logo booting, video) shakes.
=> Suspect SoC (P/N: 002.02753.005. DC: 2223. Vendor: AMLOGIC) has issue.
TV screen shake
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 9
6. Removed SoC and measure HDMI block pins, result as table below:
Summary: Measure impedance/VF HDMI pins of NG SoC  Did not find out any abnormality
SoC-U1 HDMI pin impedance measurement |  |  |  |  | 
SoC_PIN NAME | Description | OK SoC Sample |  | NG SoC sample | 
 |  | Impedance | VF | Impedance | VF
C43 | HDMI TMDS data2 negative output | 7.4MΩ | 0.76 | 7.32MΩ | 0.765
C45 | HDMI TMDS data2 positive output | 7.42MΩ | 0.76 | 7.32MΩ | 0.765
E45 | HDMI TMDS data1 positive output | 7.41MΩ | 0.76 | 7.35MΩ | 0.765
G43 | HDMI TMDS data1 negative output | 7.42MΩ | 0.76 | 7.34MΩ | 0.764
J41 | HDMI TMDS data0 positive output | 7.42MΩ | 0.76 | 7.23MΩ | 0.764
J43 | HDMI TMDS data0 negative output | 7.41MΩ | 0.76 | 7.32MΩ | 0.764
L43 | HDMI TMDS clock positive output | 7.42MΩ | 0.76 | 7.32MΩ | 0.763
L45 | HDMI TMDS clock negative output | 7.45MΩ | 0.76 | 7.38MΩ | 0.763
N41 | General purpose input/output bank H signal 1 | 2.52MΩ | 0.71 | 2.756MΩ | 0.721
N43 | General purpose input/output bank H signal 3 | 2.64MΩ | 0.75 | 2.791MΩ | 0.744
R43 | General purpose input/output bank H signal 0 | 2.49MΩ | 0.71 | 2.760MΩ | 0.721
R45 | General purpose input/output bank H signal 2 | 2.61MΩ | 0.74 | 2.763MΩ | 0.729
AG45 | General purpose input/output bank H signal 4 | 2.91MΩ | 0.78 | 3.256MΩ | 0.788
Root cause analysis
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 10
7. Reball and do a swap verification SoC
Summary: As analyzed above this issue follow U1-SoC( P/N: 002.2753.005, DC: 2223, LC: D20220605, Vendor: AMLOGIC ) component.
Check Screen HDMI | 1 | 2 | 3
OK board + OK SoC | OK | OK | OK
NG board + NG SoC | NG | NG | NG
OK board + NG SoC | NG | NG | NG
NG broad + OK SoC | OK | OK | OK
Root cause analysis
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 11
Root cause analysis
#4
Conclusion:
- Occur cause: Due to material issue, SoC (P/N: 002.02753.005, DC: 2223, Vendor: AMLOGIC). - Escape cause: FATP can’t cover issue.
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 12
Actions
#5
1. RD improves the test program at FT1 station to cover screen shake issue. (Done)
- TE Jones used NG unit which detected by customer to verify new test program 5time, result as table below:
Test times | Result
1 | SHK_VD Check video screen shake failure
2 | SHK_VD Check video screen shake failure
3 | SHK_VD Check video screen shake failure
4 | SHK_VD Check video screen shake failure
5 | SHK_VD Check video screen shake failure
SHK_VD Check video screen shake failure at FT1 station
Verification result
Summary: As the verification result, new test program can cover screen shake issue. Therefore, Fii applies new test program into production to cover this issue. (Owner: TE Jones , Done).
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 13
Actions
#5
2. Co-work with SQE to conduct vender material FA report. (On-going)
- SQE sends mail for vender to confirm about FA process (Due date : Jun-28)
Notes: MA5800-X7#display cable modem <MAC> detail