## Slide 1: SKB dongle RFP

## Slide 2: Revision history
V2
p.44,45: changed RCU, but still need ALT's confirmation.
p77,p.78: Add GOTA
p.83 Add Vietnam
p49/51-53: Add WiFi module spec., Flash reliability & CPU benchmark test

## Slide 3
Foxconn Confidential & Proprietary
Automated Unmanned
Factories
2.2 Company Status: Foxconn Industrial Internet (Fii) Company introduction
Countries
Employees
Patents
Professionals
2013
2015
2017
2019
2014
2016
2018
2020
Fii concept is born
Set up a project team to prepare for industrial internet
Fii announced to build an “Industrial Internet Ecosystem”
Fii platform at Beijing Industrial Internet Alliance Conference
Foxconn becomes the governing unit of “Alliance of Industrial Internet”(AII) , “china mobile IoT alliance“ and customization industry alliance
Fii listed on A share on Shanghai Stock Exchange
Fii selected as 1 of 16 World Economic Forum’s (WEF)advanced manufacturing “lighthouses” factories.
Fii invested LUSTER, a machine vision company, and Digiwin, a digital solution provider, aiming to further ecology and expand capacity scope in Industrial Internet.
1.2.1. General Information
1.2.2. Business History

## Slide 4
Foxconn Confidential & Proprietary
Brazil: Manaus / Sao Paulo
Mexico : Guadalajara / Giuded Juarez
Nanning / Long-Hua /
Song-Jiang / Guanlan /
Hang-Zhou / Chong-Qing
USA : San Jose / Santa Clara / Houston
China － 6 branches
North America － 3 branches
2.2 Company Status: Fii major business sectors: FG Group Branch

## Slide 5
Foxconn Confidential & Proprietary
Products
Services
Wifi/ LTE/ AP
STB
TV Conference
PND
BTS
OTT
Server
ATS/ PDU/ BBU
xDSL/ Modem
IDC device
Home Gateway
Switch/ Router/ Smart Gateway
IP Phone/ Radio
Storage Controller/ JBOD/ SSD
Rack
Containerized Data Center
Integration
Server
Filter
4G/ Fiber
Smart Life
Data Center
Smart Factory
Mobile Broadband
Smart City
Smart Home
IoT/ IoE
Internet +
2.2 Company Status: Fii major business sectors

## Slide 6
2.2 Company Status: Android TV Team Org(Sales and HW/SW Team)
Kevin Liu/Peter Lan
BU Head, 25yr/27yr
Vincent Tung
Sales/PM head,21yr
Rick Chen
R&D head, 28yr
Jacky Chiang
Software RDPL/ 20yr
Sean Chiang
Hardware RDPL/ 19yr
Premium
Advance
Intermediate
Beginner
15+ team member.
Target to grow to 20+ members in 2021.
TW, VN, CN, JP, KR, USA
40+ ATV team member.
Target to grow to 60+ members in 2021.
10+ ATV team member.
Target to grow to 20+ members in 2021.
200+ team member.
TW, VN, CN, JP, KR, USA
500+ RD engineers.
TW, VN, CN, JP, KR, USA

## Slide 7
Wilson Kao
SQA leader,20yr
James Kuo
Senior engineer,20yr
Bryan Yang
Senior engineer,12yr
Beca Ding
Junior Engineer,2yr
D.A. Wei
Senior engineer,8yr
Premium
Advance
Intermediate
Beginner
Charge Tseng
ME leader,20yr
Ace Liu
Senior engineer,5yr
Andy Qin
Layout leader,16yr
Ming Rong
Senior engineer, 6yr
Enya
Senior engineer, 7yr
Allen Chang
Package leader, 16yr
Lydia Liu
Senior engineer, 4yr
Aglaia Lee
Senior engineer, 5yr
Jason Kung
Compliance leader, 19yr
Jonah Lee
Senior Engineer, 16yr
Wen Chao
Senior engineer, 8yr
ME
Layout
Compliance
Package
Kenji Chen
HWQA leader, 18yr
Tommy Chen
Senior engineer, 13yr
Leif Lin
Senior engineer, 12yr
HW QA
SQA
2.2 Company Status: Android TV Team Org(Engineering Support Team)
10+ team member.
10+ team member.

## Slide 8
2.2 Company Status: Android TV Team Org(MFG)
David Yin
MFG site manager,16yr
Ben Trinh
MFG Lead, 12yr
Bi
CFT NPI PM, 10yr
Nelly
CFT MP PM, 2yr
Lam Chu
PM lead, 11yr
CFT team from VN Factory
Premium
Advance
Intermediate
Beginner

## Slide 9
STB related
WiFi related
2.2 Company Status: Patent

## Slide 10
2019
2018
Reference link: http://www.fii-foxconn.com/static/file/%E9%95%BF%E5%9B%BE.jpg
Reference link: http://www.fii-foxconn.com/static/file/032919_content.pdf
2.2 Company Status: Financial statements

## Slide 11
Foxconn Confidential & Proprietary
2.2 Company status - Subsidiary or affiliated company
(Fii)
Mother company: Honhai precision Ltd’s main business sectors
Hon Hai Precision
鴻海精密 2317.TW
AOT
榮創 3437.TW
FIH Mobile Limited
富智康 2038.HK
A
Innolux
群創 3481.TW
K
CyberTAN
建漢 3062.TW
FG
MTI
台揚 2314.TW
FG
Zhen Ding
臻鼎 4958.TW
L
ESON
乙盛 5243.TW
E
Fii 工業富聯 601138.SH
A
Foxconn Technology
鴻准 2354.TW
C
Ennoconn
樺漢 6414.TW
FG
ShunSin
訊芯 6451.TW
E
Foxsemicon
京鼎 3413.TW
C
SHARP Corporation
夏普 6753.TO
E
Asia Pacific Telecom
亞太電 3682.TW
FG
L
FIT HON TENG
鴻騰 6088.HK
L

## Slide 12
Reliability
Mechanical Test
Vibration Test Random (Op)
Shock test (Op)
Label Adhesion Test
Abrasion Resistance of Label Test
Logo/Printing Abrasion Test
Package Test
Temperature and Humidity Test
Static Compression Test
Random Vibration Test
Free Fall Drop Packaged
Fix Displacement Vibration Test
Reliability Standard:
IEC60068 for Environmental
ISTA-2A for Package test
3rd Party Lab.: Orange color
High Temperature & Humidity Test (Op)
Operational Temperature Range
Power on/of f with Temp.
Quicky Power on/off Test
RDT Test
MTBF Prediction
HALT Test
Non-operating drop test
Salt Spray Test
Connector Life Test
Button Life Test
Climatic Test
Thermal Profile test
Cold / Hot Start Test
Continuation of temperature cycle
EDVT
Temperature and humidity cycles test
HWQA Reliability Test Items
2.3 Related technology and supply performance

## Slide 13
Verify the hardware design by exposure of the product to wider temp & voltage margining.
Temperature Margin: Min Op. Temp – 5’C ~ Max Op. Temp + 5’C
Voltage Margin DC: All Power Rail +/- 5%
Voltage Margin AC: 90VAC /47Hz & 264VAC / 63Hz
EDVT
HWQA Capabilities – EDVT
Electrical Design Verification Test
Power Cycle Box
DAQ
IXIA
Power Supply
EDVT Lab
2.3 Related technology and supply performance

## Slide 14
Mechanical Design Verification Test
ＭＤＶＴ
MDVT
HWQA Capabilities – MDVT
Thermal Chamber
Shock Tester
Drop Tester
MDVT is comprised of dynamic (mechanical) and environmental tests. These combination of op. and non-op. tests.
Thermal Profile Measurement
Environmental Test – High/Low Temp/Hum., Altitude, UV, Rain, Dust, Salt spread…etc.
Mechanical Test - Vib & Shock, Drop, button life, cable..etc
Package Test – ISTA-2A, 3A
Product Reliability: MTBF Prediction/ demo., thermal shock…etc.
Test to failed – HALT, HASS
Env. Chambers
Thermal Shock
HALT
Vib. Test for Rack
2.3 Related technology and supply performance

## Slide 15
SI
HWQA Capabilities - SI Meas.
Signal Integrity Measurement
A dedicated team to work on a set of measures of the quality of an high-speed electrical signal.
IEEE802.3 10M/100M/1G/10G/2.5G/5G/40G/100G/400G Compliance Test
SFP+/QSFP+/QSFP+100 Compliance Test
DDR I/ II/ III/IV/IVLE Signal Test
UDB3.1/HDMI/PCIe/SATA
DC/DC, AC/DC, PoE
Clock Phase Noise
….etc.
Keysight 86100D
400G SI Test
DPO71604C
Keysight 86100D
MSO72304DX
Keysight N6705C
2.3 Related technology and supply performance

## Slide 16
SI
MDVT
EDVT
Test
Standards
IEC 60068-2 MIL-STD NEBS GR-63 CORE Telcordia SR-332 ISO7779 ISTA – 2A
IEEE 802.3
SFF-8431
JEDEC 79-4A
HWQA Test
2.3 Related technology and supply performance

## Slide 17
(1) General chamber:
(2) Altitude chamber:
(3) Thermal shock:
(4) Earthquake (zone 4 level):
(5) Dust & water protection (IP65):
(8) Salt fog test: 5% salt, 35℃
(6) Package test machine:
(7) Wind loading test: 61.2 m/s (wind level 17: strongest typhoon)
(9) Solar test:1120 w/m2, 55 ℃
HWQA Capabilities
2.3 Related technology and supply performance

## Slide 18: OTT Box Test Environment
Internet
AP
HDMI
Composite
Component
OTT Box
Ethernet
Ethernet
WiFi
802.11 b/g/n/ac
WEP/WPA/WPA2
Remote
Controller
TV Sets
Sony, Panasonic, Toshiba, Sharp ...
Speakers
Dolby AV Receiver
Subjective Test
Peripheral Test
Objective Test
Audio Analyzer
- AP APX585 & AP2722
HDMI Protocol/CEC Analyzer
- Quantum Data 980 / 882E
Picture Analyzer
- Video Clarity ClearView
Digital Serial Analyzer
- TEK DSA71604B
Video Streaming
Traffic Jitter/Delay/ Drop
- Shunra Storm
Ethernet
2.3 Related technology and supply performance
Notes: RCU’
DUT換成EAGLE

## Slide 19: Wi-Fi Development Process (1/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
Wi-Fi spec. review
  Transmit power
  Frequency Band
Wi-Fi solution
  Interface : SDIO
  Chipset vendor : REALTEK
Locating Antenna position in STB
  Mechanical drawing
  Simulation(HFSS)
  RF cable path
Schematic and Layout reviewed by vendor
2.3 Related technology and supply performance

## Slide 20: Design prepare
Mechanical drawing
Simulation (HFSS)
Return Loss
Efficiency
Chip antenna | 5.15G | 5.47G | 5.85G
Efficiency(%) | 63.36 | 66.20 | 63.51
* Above is reference data, need to use actual PCB to test
WIFI
module
SOC
WIFI module
Chip antenna
RF path
This picture is only for reference.
2.3 Related technology and supply performance

## Slide 21: Wi-Fi Development Process (2/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
802.11a/n/ac Spec. verification
  Transmit power measurement
  Transmitter spectral mask test
  Transmitter spectral Flatness
  Local Oscillator suppression & Center frequency tolerance
  Transmit Center Frequency Error
  Transmit Power On and Power Down Ramp
  Transmit modulation accuracy (EVM)
  Receiver minimum input level sensitivity
  Receiver maximum input level
  Adjacent channel rejection and Non-adjacent channel rejection
Chipset vendor review Conducted performance
2.3 Related technology and supply performance

## Slide 22: Conducted test
Test diagram
Test Step
DUT install RF test tool of module
Control PC connect IQxel or others equipment via Ethernet
Connect DUT and IQxel by 50 ohm cable and Ipex4 to SMA cable
Setting parameter by IQxel
Setting parameter by RF test tool and start test
Repeat step4 and step5
 | Q’ty
Control PC | 1
IQxel | 1
Ethernet cable | 1
50 ohm cable | 1
Ipex4 to SMA cable | 1
Test equipment list
2.3 Related technology and supply performance

## Slide 23: Wi-Fi Development Process (3/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
internal design target
  Frequency 5GHz: 5150 ~ 5350, 5470 ~ 5850MHz
  Directivity: ≥ +3dBi
  Efficiency: ≥ -50%
  VSWR: ≤ 2.0:1
  Return Loss : ≤ -10dB
Antenna passive test with mounting STB
  Antenna position: Simulation by using 3D antenna tool (HFSS)
  Antenna performance measurement in Anechoic chamber
Antenna 3D plot
The reason to reduce peak gain spec from +5dBi to +3dBi
Based on environment of dongle, expected to use chip antenna, but pattern design of chip antenna is fixed and the peak gain can’t be improved by adjusting antenna matching
Based on the design experience in previous project, the peak gain of chip antenna is about +3dBi
 | 5150 | 5470 | 5850
Peak gain (dBi) | 3.68 | 3.58 | 3.45
* Above is reference data, need to use actual PCB to test
Peak gain of previous project
2.3 Related technology and supply performance

## Slide 24: Antenna Test
Test Step
DUT place on test platform
Parameter setting by test tool
Generate antenna gain, efficiency, 2D and 3D plot
DUT
DUT
Antenna Anechoic chamber
2.3 Related technology and supply performance

## Slide 25: Wi-Fi Development Process (4/5)
RvR(Wi-Fi Throughput Rate vs. Range in TCP) test
  Test Spec.:
  Test condition
  - In anechoic chamber or shield room
WIFI Throughput Tx/Rx test
- In anechoic chamber
Design prepare
Conducted test
Antenna test
Radiation test
OTA test
Octobox environment setting
Please refer to radiation test page
(Suggest test criteria for next page)
2.3 Related technology and supply performance

## Slide 26: Test criteria
The following table is RvR test result using WIFI module (chipset : RTL8822CS), when the attenuation is 10dB, throughput less than 200Mpbs, so unable to meet over 270Mbps at -50dBm
* Above is reference data, need to use actual PCB to test
Suggest test criteria
Because the throughput test result is related to the SOC, Therefore, it is suggest that the test criteria as below table
2.3 Related technology and supply performance

## Slide 27: Radiation test
Actual test environment
Test diagram
5GHz (unit: 866Mbps) |  | Channel 36 | Channel 149 | Channel 161
RCU no pairing | Tx | 268 | 297 | 280
 | Rx | 256 | 256 | 257
RCU pairing | Tx | 265 | 293 | 277
 | Rx | 250 | 248 | 254
5GHz (unit: 866Mbps) |  | Channel 36 | Channel 149 | Channel 161
RCU pairing | Tx | 250 | 262 | 260
 | Rx | 236 | 256 | 237
Test Condition : RCU pairing/RCU non pairing
Test Condition : RCU pairing + Play 4K Video
* Above is reference data, need to use actual PCB to test
Shielding room size
2.34m*2.34m*2.19m
2.3 Related technology and supply performance

## Slide 28: Wi-Fi Development Process (5/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
Indoor OTA test
  Test Spec.: Min. Throughput ≥ 20Mbps @spot No
  Test condition
  - CH36 @5GHz and CH161
  - Test spot on FXN TW office
Outdoor OTA test
  Test Spec.: comparison data for reference sample
  Test condition
  - CH36 @5GHz and CH161
- Test place where is non line of sight W/O WLAN AP
MP prepare
  Mass product automation program
  Manufacturing Spec. fix
Please refer test environment and procedure to next page
2.3 Related technology and supply performance

## Slide 29: OTA test
Indoor
Test Step for Indoor and Outdoor OTA test
DUT install Iperf3 client APK
The AP is placed at the green point in the picture
The DUT is placed at the red point 1 in the picture
Start Rx test
Repeat step 3 and step 4
NLOS - Rental House Test
Live signal without neighbors’ WiFi interference
Outdoor
2.3 Related technology and supply performance

## Slide 30: Wi-Fi Manufacturing Process (1/4)
Conducted test
Radiation test
Calibration
OBA test
Wi-Fi Calibration
Wi-Fi Verification(Conducted test)
Using IQxel80 or IQM8W
Description | Unit
PC | 1
IQxel80 or IQM8W | 1
RF connector | 4
RF cable | 5
Attenuator(10dB) | 1
Ethernet cable | 3
Shielding Box(Big) | 1
Fixture | 1
2.3 Related technology and supply performance

## Slide 31: Wi-Fi Manufacturing Process (1/4)
Conducted test
Radiation test
Calibration
OBA test
Wi-Fi Calibration spec
  List up
2.3 Related technology and supply performance

## Slide 32: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
WIFI Conducted test
  Test diagram
  Test spec
802.11a/n/ac . Frequency list, Test spec, Calibration & verification or only have verification
  Transmit power measurement
  Transmitter spectral mask test
  Transmit Center Frequency Error
  Transmit Power
  Transmit modulation accuracy (EVM)
  Receiver minimum input level sensitivity
  Receiver maximum input level
2.3 Related technology and supply performance

## Slide 33: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
WIFI Conducted test
  Test diagram
  Test spec
2.3 Related technology and supply performance

## Slide 34: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
Throughput test
  Test diagram
  Test spec
2.3 Related technology and supply performance

## Slide 35: Wi-Fi Manufacturing Process (3/4)
Calibration
Conducted test
Radiation test
OBA test
WIFI Radiation test
  Test diagram
  Test spec
* ALT Comment : Please update mass production test diagram and test environment
* FXN : It’s the same with WIFI throughput test
2.3 Related technology and supply performance

## Slide 36: Wi-Fi Manufacturing Process (4/5)
Calibration
Conducted test
OBA test
Radiation test
WIFI OBA test
  Test diagram
  Test spec->Connect internet and play YouTube content
* ALT Comment : Please update mass production test diagram and test environment
2.3 Related technology and supply performance

## Slide 37
Fii works with worldwide 1st Tier Brand companies: Google, Amazon, Roku, Technicolor, Commscope, SHARP, etc for worldwide carriers.
Over 15 million STB delivered per year
Over 30 million OTT delivered per year
Over 600K ATV STB delivered per year
Operating profit is around 2%
Android TV OTT box related development experience and major supply performance/commercialization cases in the last 3 years
PCCW
Shipped 100K+
CJ HelloVision
Shipped 80K+
CCC
Shipped 200K+
TBC
Shipped 100K+
BANDOTT
Shipped 200K+
Simple H/W & S/W Spec by model, supplier, supply quantity, commercialization must be included
SKB
Shipped 1KK+
2.3 Related technology and supply performance

## Slide 38
Foxconn Confidential & Proprietary
4K OTT - BANDOTT
ID
Basic
Dimension | - 140mm(W) × 127mm(D) × 29mm(H)
Networking | Wi-Fi 802.11 ac 2T2R dual band 10/1000 Base-T Ethernet Bluetooth 4.1 w/ BLE
Power adapter | 5V/2A DC output
Technical Specification
Chipset | Memory
Quad-core 64bit ARM Cortex-A53 up to 1.5 GHz, Penta-cores Mali-450 up to 750MHz | 2 GB DDR3 8 GB eMMC flash
Interface | Features
HDMI 2.0b @ 4Kp60 output x1, HDCP 2.2 HDMI input x 2 up to 1080i resolution USB 2.0 Host Type A x1 RJ-45 x1; 10Mbps / 100Mbps | Main stream box for HEVC/4K video HLS/MS Smooth Streaming/MPEG-DASH, BT Voice control Android TV certificated Netflix NTS certificated
Multimedia | Operating System
Decode H.265 HEVC MP-10@L5.1 up to 4Kp60 H.264 AVC HP@L5.1 up to 4Kp30 VP9 profile 2 up to 4Kp60 Encode H.264 up to 1080p60 | Android 7.1 Widevine Level 1/PlayReady DRM support Dolby AC3 support
 | Remote Control
 | BT4.0 or IR based RCU

## Slide 39
Foxconn Confidential & Proprietary
4K OTT - Sandwich (Mini Box)
ID
Basic
Dimension | - 84.6mm(W) x 39.6mm(D) x 15mm(H)
Networking | Wi-Fi 802.11 ac 1T1R single band Bluetooth 4.1 w/ BLE
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240V AC input, 5V/1A DC output
Safety Certification | BSMI / NCC certification
Technical Specification
Chipset | Memory
Quad-core 64bit ARM Cortex-A53 up to 1.5 GHz, Penta-cores Mali-450 up to 750MHz | 2 GB DDR4 16 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.0b @ 4Kp60 output x1, HDCP 2.2 | Main stream box for HEVC/4K video HLS/MS Smooth Streaming/MPEG-DASH, BT Voice control Android TV certificated Netflix NTS certificated
Multimedia | Operating System
Decode H.265 HEVC MP-10@L5.1 up to 4Kp60 H.264 AVC HP@L5.1 up to 4Kp30 VP9 profile 2 up to 4Kp60 Encode H.264/H.265 up to 1080p60 | Android TV 7.1/8.0 Widevine Level 1/PlayReady DRM support
 | Remote Control
 | BT 4.2 RCU w/ voice input

## Slide 40: SKB 4K IP STB
ID illustration
Basic
Technical Specification
Chipset | Memory
S905X2 Quad-Core Cortex-A53, 16,560DMIPS ARM Mali-G31 MP2, 800MHz | 3 GB DDR4 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.1 @ 4Kp60 output x1, HDCP 2.2 USB 3.0 Host Type A x1 RJ-45 x1; 10/100/1000 Mbps IR receiver x 1 MIC input (3.5pie) x 1 RGB LED for indication DC jack for 5V @ 2A DC input | Main stream box for HEVC/4K video HLS/MPEG-DASH/HDR 10/ HLG Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade Android TV certificated
Multimedia | Operating System
Decode 4Kp75 10b H.265, VP9 Profile 2 Encode H.264/H.265 1080p60 | Android P Widevine Level 1/PlayReady DRM support Dolby AC3
 | Remote Control
 | BT w/ IR based RCU
Dimension | -95mm x 95mm x 25mm
Networking | 10/100/1000 Base-T Ethernet Bluetooth 4.2 w/ BLE
Power adapter | 100~240VAC input, 5V/2A DC output
Safety Certification | KC/HDMI/BQB

## Slide 41
Jacky Chiang
SW Manager
Kerwin Chen
SW Lead
River Wong
SW Engineer
Jim Chen
SW Engineer
Jason Ling
SW Engineer
Brent Choi
SW Engineer
Jerry Lin
SW Engineer
Bcan Yeh
SW Engineer
Sam Yang
SW Engineer
Peter Chen
SW Engineer
2.4 Development manpower: SW

## Slide 42
Sean Chiang
HW Manager
Tom Lee
HW Lead
Fu-Chiang Yang
HW Engineer
Catherine Chen
HW Engineer
Charge Tseng
ME leader
Ace Liu
ME
Andy Qin
Layout leader
Ming Rong
Main board layout
Enya
Subboard layout
Allen Chang
ID/Package leader
Lydia Liu
Package design
Aglaia Lee
ID design
Jason Kung
Compliance lead
Jonah Lee
EMC test debug
Wen Chao
EMC test
2.4 Development manpower: HW/Layout/ME/Package/Compliance

## Slide 43
Wilson Kao
SQA leader
James Kuo
Dolby Cert., SIT
Bryan Yang
ATV CTS cert., SIT
Beca Ding
ATV CTS cert., SIT
Kenji Chen
HWQA leader
Tommy Chen
Reliability, mechanical
Leif Lin
Package test
2.4 Development manpower: HWQA/ SQA

## Slide 44: OTT Dongle（S905Y4/Android11）
Dimension | - TBD
Wi-Fi 2.4/5GHz 2T2R Connection | - Support 802.11 ac/a/b/g/n - Data rate up to 866Mbps
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240VAC input, 5V/1A DC output
Safety/ Cert. | KC certification
Chipset | Memory
AML S905 Y4 Quad-Core Cortex-A35, 18,400DMIPS ARM Mali-G31 MP2, 850MHz | 2 GB DDR4 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.1 @ 4Kp60 output x1, HDCP 2.3 USB 2.0 MicroUSB for power RGB LED indicator * 1 | Main stream box for HEVC/4K video HLS/MPEG-DASH/HDR 10/ HLG Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade Android TV pre-certified Netflix NTS (optional)
Networking | Remote Control
Wi-Fi 802.11 ac/a/b/g/n 2x2 dual band Bluetooth 5.0 / BLE Ethernet AC adapter(built-in USB2.0 type-A interface) | IR/BT4.2 voice control
Multimedia | Operating System
Decode AV1 4Kp75 10b H.265, VP9 Profile 2 4kp30 H.264 Encode H.264/H.265 1080p60 | Android 11 Widevine Level 1/PlayReady DRM support Supported Codec MPEG2/ H.264/ H.265/ HDR10 (PQ)/ HLG (HLG)
Technical Specification
OTT Box ID Illustrationht
Highlight
AV1 (VP10) supported
5. HW spec

## Slide 45
45
Bluetooth button
1. Google assistant key
2. Up key
3. Down key
4. Left / Fast Backward key
5. Right / Fast Forward key
6. Enter / Play & Pause key
7. Back key
8. Home key
9. Manual key
10. Direct App key
Dongle Design
02a. Back cover
C : Black / M: Plastic / F : Polish (SPI A2)
03. USB TypeC
01a. Front cover
C : Black / M : Plastic / F : Polish (SPI A2)
LOGO
C : UV-Translucent ink/ Printing
04. HDMI
Dimensions :
93.9(W) X 32 (D) X 11.6 (H) mm
01b. Front cover
C : Black / M: Plastic / F : Texture (MT11010B)
02b. Back cover
C : Black / M: Plastic / F : Texture (MT11010B)
05. Reset button
5. HW spec
IR button
1. TV power key
2. TV volume key
3. TV input key
7. TV mute key
TBD
Need ALT to confirm IR function and key requireoment

## Slide 46
5. HW spec

## Slide 47
AC to DC
Converter
100~240Vac
Block Diagram – Adaptor (Built-in RJ45 & USB2.0)
Micro USB Conn.
With Cable
5V/1A
USB 1 to 2 Hub IC
USB2.0
USB Type A Conn.
USB2.0
Ethernet PHY
to
USB IC
USB2.0
10/100M LAN Port
TX/RX
SPI Flash
25MHz Crystal
25MHz Crystal
5. HW spec

## Slide 48
5. HW spec

## Slide 49: WiFi module AP6398SV (BCM43752): Highly Integrated 28nm WIFI 5 Combo  802.11ac + BT5.1
Module Summary: 2x2 11ax+ BT5.1
28nm design for lowest active power consumption and small size
Highly integrated with iPA/iLNA in WLBGA/FCBGA for 802.11ac
256QAM 80MHz support
Full Bluetooth 5.0 features (include 2Mbps, LE LR)
On-chip Memory Expansion
Dual BT TX enable flexible BT configuration with best RF coverage
SLNA/DLNA design to support excellent WiFi/BT coex
5. HW spec

## Slide 50: Antenna Simulation
Antenna Placement
Return Loss
Isolation
3D Pattern
Gain/ Efficiency
ANT 1_2.4G | 2.400 GHz | 2.450 GHz | 2.500 GHz
Gain(dB) | 3.07 | 3.31 | 3.57
Efficiency(%) | 62 | 65 | 66
ANT 2_2.4G | 2.400 GHz | 2.450 GHz | 2.500 GHz
Gain(dB) | 3.18 | 3.25 | 3.33
Efficiency(%) | 63 | 65 | 64
ANT 2_5G | 5.150 GHz | 5.350 GHz | 5.550 GHz | 5.850 GHz
Gain(dB) | 5.08 | 5.25 | 5.41 | 5.55
Efficiency(%) | 66 | 65 | 64 | 65
ANT 1_5G | 5.150 GHz | 5.350 GHz | 5.550 GHz | 5.850 GHz
Gain(dB) | 5.15 | 5.33 | 5.21 | 5.42
Efficiency(%) | 67 | 68 | 66 | 65
Return Loss | 2.4 GHz | 2.5 GHz | 5.150 GHz | 5.850 GHz
ANT1-S11 (dB) | -14.4 | -11.34 | -14.01 | -22.56
ANT2-S22 (dB) | -11.01 | -15.75 | -12.75 | -19.37
Isolation | 2.4 GHz | 2.5 GHz | 5.150 GHz | 5.850 GHz
S12 (dB) | -13.13 | -12.25 | -19.16 | -26.36
S21 (dB) | -13.12 | -12.25 | -19.15 | -26.36
5. HW spec

## Slide 51: eMMC Read/Write reliability (Samsung 8G eMMC)
The Daily Amount Data Size
Data Retention Test Result
5. HW spec

## Slide 52
S905Y4 Benchmark Test Report (Antutu V8)
CONFIDENTIAL
For SK BB Only
5. HW spec

## Slide 53
S905Y4 Benchmark Test Report (GFXBench 5)
CONFIDENTIAL
For SK BB Only
CONFIDENTIAL
For SK BB Only
5. HW spec

## Slide 54
Thermal Profile Test
Step 1
Define Test
Locations & Criteria
1. Key ICs, XTAL,
AL Capacitors, Housing, ...
2. Refer Thermal Simulation Data
3. Temperature
+25°C, +40°C, …
Step 2
Prepare
Test Equipments
1.IR Thermal Imager
2. Thermocouple wires rework
3. Thermal glue & accelerator
Step 3
Start
Thermal
Test
1. Attach the thermocouples on test locations
2. Test duration:
3~6 hours
Step 4
Record Test
Result
1.Record the test result @ different conditions
(+25°C, +40°C, …)
54
Thermal Profile Test
5. HW spec

## Slide 55
Environmental Test
Temp. /
Humidity
ALT/RDT Demo.
Thermal Shock
Walk-In Chamber
1.Temp & Humidity Range:
-40℃~ 80℃ 20~95%RH,1℃/min
2.Inside:290(W)*195(D)*210(H)
Thermal Shock
1.Temp. range-65℃~0℃,65 ℃ ~150℃
5 Mins per cycle
2.Inside dimension: 60(W)*50(D)*50(H)
Temp./ Humidity
1.Temp & Humidity Range:
-40℃~150℃ 10~98%RH
,Temp. Rate: 2℃/min
2.Inside 100(W)*100(D)*100(H)
Altitude
Altitude
1.Temp. range:-70℃ ~ 120℃
2.Altitude range：site level to 80K feet
3.Pressure range：101.32kpa~1kpa
4.Inside dimension: 110(W)*110(D)*110(H)
55
5. HW spec

## Slide 56: Salt Spray Test
Salt Spray Test
1. Salt: 5% , Temp.: 35C and Humidity: 85%
2. Spray Volume: 0.5-2.0ml/80sq.cm hr
3. Test time: 48 hours
5. HW spec
Notes: 56

## Slide 57
Mechanical Test - 1
Package Drop Test
1. KD-128AS
2. Drop height：35 ~ 200 cm
3. Max. load：60 kg
Random Vibration Test
1. Frequency range ：1~2.4KHz
2. Max. force：3600kgf
3. Max. acceleration：50g
4. Max. displacement：2 inches
5. Max. velocity:78 inches/sec.
6. Work space：120*120/cm
Shock Test
1. Weight: < 4.5 Kg
2. G level: 65G ~ 80G
3. Duration: 8.7 msec
4. Work space ：70 *70/cm
5. Loading :227KG
57
5. HW spec

## Slide 58
Mechanical Test - 2
Free Fall Drop
1. Height: 1.5 m, 1.2 m
2. Drop: 6 faces
Keypad Life Test
1. Press force: 50~1000 gram
2. Speed: 0.05~360 cycles/min
Road Simulator
1. Frequency: 10Hz~55Hz
2. Displacement: 0.75 mm
3. Cycle: 60 cycles
Push Pull Test
1. Force Range: < 50 Kg
2. Test Range: 1 ~ 200 m/min
3. DC Jack, USB/ HDMI, IEC...
58
5. HW spec

## Slide 59
Mechanical Test - 3
59
5. HW spec

## Slide 60: AV1 Video Decoding
AV1 video decoding is required for all new devices and product variants launching after March 31, 2021*.
Requirement applies to new Android 10 and Android 11 devices and
products.
Devices must support 60fps decode at the maximum supported decode and display resolution of the device (2K, 4K or 8K).
8.1 OS/Android Platform Android 11 Overview

## Slide 61: Android 11 features
Item | What’s New for TV?
Performance | Reduced cold start time Speeding up app starts by adding binder cache
Privacy & Security | Restrictions for Microphone access from background One-time permission option for sensitive permissions Limited package visibility only allowing apps to interact with the apps they need to
Power and Sleep Functionality | Energy saver features optimizing standby behavior Configurable wake keys CEC wake up via One-Touch-Play (for OTT)
Media decoder | Media decoder latency optimizations
Display Handling | Display API improvements for display modes, hot plugging
Silent OTA | Quiescent boot for standby OTA
Google Assistant | Google Assistant: Audio pipeline and launch path optimizations
Android TV Other application/service | Significant improvement in Accessibility App Gboard: New UI and features Building high quality Google TV experiences
8.1 OS/Android Platform Android 11 Overview

## Slide 62: GTVS Apps Changes for Android 11
8.1 OS/Android Platform Android 11 Overview

## Slide 63
CTS Test (Compatibility Test Suite)
Internet
Wireless
Base Station
The CTS is an automated testing suite
The CTS runs on a desktop machine and executes test cases directly on attached devices or an emulator
ATV xTS Certification
8.1 OS/Android Platform Android 11 Overview

## Slide 64
Google GMS TEST & pre-CERTIFICATION for Android TV
1.CTS test – to verify device’s compatibility.
2.CTS Verifier – to verify device’s compatibility that can not be automated.
3.GTS – to verify device’s Google GMS compatibility.
4.VTS/CTS-GSI – to verify compliance to Treble architecture
5.STS – to verify device is updated with latest security patches
6. TV Test Suite (TVTS) –to verify Android TV device’s compatibility.
7.Smoke Tests – tests cover the following functionalities
8.Function test – to verify device’s functions, like network、video player、USB port…
-Audio
-Youtube
-Play Movies
-Play Games
-Remote Controls
-Voice Search
-Companion App
-Voice Actions
-Accessories
-Cast
-Standby, etc.
-Boot-up
-Launcher
-HDMI CEC
-HDMI ARC
-Component Input
-Optical Audio Out
-Restricted Profile
-Client ID check
-Serial number check
-Games
-Apps
ATV xTS Certification
8.1 OS/Android Platform Android 11 Overview

## Slide 65
Processing Flow to Apply Google Security Patch
Google release security patches and corresponding STS test suite
FII to apply security patches and build the test image
Check if test image can pass corresponding STS test suite
Upload security patches to SKB Bitbucket (Git server)
8.1 OS/Android Platform Android 11 Overview

## Slide 66
From OTA Server
OTA Preparation
Generate OTA file
Upload to OTA Server
Build/Release new version
OTA Client Start
Connect to OTA Server
Check version
Download and store OTA file
Reboot to recovery
Execute commands to update files in recovery
OTA Process finish
Need to upgrade
Up to date
Reboot to normal system image
OTA Upgrade Flow
Copy OTA file to USB
Reboot to recovery
(by SW command or HW button)
Execute commands to update files in recovery
OTA Process finish
Reboot to normal system image
From USB Storage
8.1 OS/Android Platform Android 11 Overview

## Slide 67
Build
environment
Unsigned images
Signing tools
secure boot key
(HW root key)
Result
Signed images
Start
Bootloader
Verify signature of boot image (HW root key)
Bootloader
Start to run image
Bootloader
Stop to run image
OK
Fail
Signing flow of secure boot
Verification flow of secure boot
Hash+signature
Security certification (recognized lab)
Amlogic S905X4: Pass certification in Riscure lab
Signing tools
The image signing tools would be provided by Amlogic
Secure Policy – Secure Image Signing and Secure Boot Flow
8.1 OS/Android Platform Android 11 Overview

## Slide 68
Secure Policy – TEE for Encrypted Contents on Android
ARM TrustZone - ARM TrustZone is a set of security extensions added to the ARM architecture that can provide two views of the system, secure world and normal world. It provides a Trusted Execution Environment (TEE) for application. Access to certain peripherals and areas of memory can be restricted to the secure world by hardware.
Secure OS - Secure OS is a secure kernel that can be run in parallel with a full featured rich operating system such as Linux or Android on the same ARM core. It uses ARM TrustZone technology to protect trusted applications and any secure peripherals from code running in the rich OS (REE). The implementation of Amlogic Secure OS has been reviewed by ARM.
Normal World (REE)
Secure World (TEE)
DRM CA
DRM TA
CAS CA
CAS TA
TEE Supplicant
TEE Client API
TEE Internal API
TEE Driver
Storage
TEE Core
Monitor
HW Resources
Crypto/OTP/RNG
User
Privileged
CAS: Conditional Access System
DRM: Digital Rights Management
CA: Client Application
TA: Trusted Application
TEE Supplicant: a TEE daemon library
TEE Architecture Overview
8.1 OS/Android Platform Android 11 Overview

## Slide 69
Processing Flow to Include Preloaded Apps from SKB
SKB release verified Preloaded Apps to FII
FII include these Apps in code base and build the test image
FII to check if test image can pass corresponding BTS test suite
Feedback result to SKB
8.1 OS/Android Platform Android 11 Overview

## Slide 70
Customizing the Home Screen in Android Standard Launcher
1. A widget (optional) is a dynamic icon that launches an activity when selected by the user. Device manufacturers can use the widget as an entry point for custom
2. The Favorite Apps row can contain up to eight apps in the out-of-box (OOB) configuration. After completing the OOB setup, users can move, favorite, or un-favorite apps as desired.
4. App recommendations promote apps that aren't installed on the device. Device manufacturers can include a recommendations row in the Apps view that is populated dynamically by a content provider and controlled by the OEM at all times.
3. The Apps grid has a fixed width of four apps.
Slots 5–8 are reserved for Google apps.
Please let us know the favorite-apps-out-of-box-order, Apps order, if you want to show App Recommendations, please provide
name. Name of app displayed in the recommendations row.
package_name. Name of the app package to launch.
banner_uri. Location of the banner image to display on the card. The image should be (in pixels) 208 px wide x 117 px high.
data_uri. Data URI added to the intent launching the app. Required for virtual apps; optional for native apps.
is_virtual_app. Set to true for virtual apps and false for native apps.
8.1 OS/Android Platform Android 11 Overview

## Slide 71
8.2 OTT Apps - Netflix Certification
We have experiences to get NTS Certifications for Android TV OTT box products.
Below is Netflix certification letter for reference.

## Slide 72
8.2 OTT Apps - Netflix Certification Steps
Customer needs to ask for Netflix’s permission to allow the product to enter Netflix certification.
If Netflix agrees to certificate the product. Then create a project in Netflix partner portal and fill the product related information. Also apply RAE test equipment from Netflix.
Send final product devices and RCU(Remote Control Unit) to Netflix. The Netflix logo on RCU has to meet Netflix’s requirements.
If Dolby Vision need to be supported, the product needs to pass Dolby Vision Certification first.
Pass Android TV CTS Certification.
Start internal NTS testing until all of NTS test items are passed.
Submit F/W image to Netflix to certify your device. If any critical issues fail, fix them and repeat Step 6.
Until all critical issues are fixed or Netflix agrees exemption on failed items, Netflix will give a Certification Pass Report to allow F/W image deployment.
We will use Hailstorm code base provided from Amlogic to speed up Netflix certification process. So
we expected the overall certification schedule shall be within 1.5 months

## Slide 73
Subjective / Objective / Peripheral / Video Streaming
Picture Quality Testing / AV Sync
EDID / HDCP / CEC / Hot Plug Pulse
8.2 OTT Apps - Fii Netflix NTS Testing Capability

## Slide 74
8.2 OTT Apps - Amazon Prime Video Cert. Steps
FII to create project and on-boarding process and security review with Amazon
AML to provide Amazon Prime Video related patches to FII
FII apply the patches and FII’s QA run AVTS(Amazon Video Test Suite) test cycle
Fix AVTS issues during testing and restart AVTS testing
Submit our AVTS testing results and devices to Amazon
Amazon validate our integration by repeating AVTS testing
Get approval letter
Because Amlogic will provide BSP with Amazon Prime pre-certification so we expected the overall certification schedule shall be within 1.5 months

## Slide 75
RCU
ATV Box
SEARCH Key (0x0C, 0x221)
Search (CHAR_CTL: 0x08)
Mic_open (CHAR_TX: 0x0C, {codec_used})
Mic_open_error
(CHAR_CTL: 0x0C, error_code(2))
Audio_start (CHAR_CTL: 0x04)
Audio_data (CHAR_RX: Data)
.
.
.
Audio_end (CHAR_CTL: 0x00)
Mic_close (CHAR_TX: 0x0D)
Audio_data (CHAR_RX: Data)
GA Key is pressed
The user will initiate the voice search by pressing the microphone button.
The Remote will send a key event (HID: page 0x0C, value: 0x221) to the Android TV Device. It will also send a ATVV_CHAR_CTL notification (with data byte 0x08) to Android TV.
When the Android TV Device is ready to start receiving data from the Remote it will send the Mic_open() command via the ATVV_CHAR_TX characteristic (with data byte 0x0C and codec_used ).
When the Android TV Device has detected the user has stopped speaking, it will send the stop recording command to the Remote also via the ATVV_CHAR_TX characteristic (with data byte 0x0D).
Audio data will be sandwiched between ATVV_CHAR_CTL(with data byte 0x04) and ATVV_CHAR_CTL(with data byte 0x00) as the start and end of audio data respectively.
8.3 Work Flow of Google Assistant Between Box and RCU

## Slide 76
8.4 Proprietary Voice Recognition - NUGU
For integrating SKT Voice recognition - NUGU, it needs an Android App and modify android framework, Android Audio HAL and Linux Kernel Driver to support it.
We already had experience in SKB product to modify all of matters to support it. But, for the NUGU app, we need SKT to provide it because it will need to communicate with NUGU server with proprietary NUGU APIs and they already had an Android App for it.
NUGU
Voice Recognition Server
NUGU APP
Android Framework
Audio HAL
Kernel driver
NUGU APIs

## Slide 77: 8.5 Upgrade and Management - GOTA
GOTA is a Google offered service for Android TV TADA partners
  Delivers system SW update packages to end user devices using Google Infrastructure
  GOTA is about DELIVERY of OTA packages. OTA prep and packaging is supported as part of AOSP
Includes on-device component (incl in GMSCore) and GOTA server hosted in Google Cloud
Can be managed via self-service portal or via API for integration into custom IT workflows

## Slide 78: 8.5 Upgrade and Management - Why GOTA?
GOTA is FREE for Android TV TADA Partners
  EVERYTHING included (client, frontend access, and Google Cloud hosting)
GOTA is PROVEN
  More than 100 Million devices across many OEMs
  GOTA for Android TV shares server and client implementation with Android mobile
FUTURE PROOFED with ongoing feature development from Google
GOTA is a NIMBLE solution. Client side GMS Core deployed through Google Play so fixes and feature updates are not coupled to platform releases

## Slide 79
ACS System
8.5 Upgrade and Management – ACS System
ACS System – FII in-house designed ATV platform Back-end System
Device Management
OTA
Management
App
Management
User Behavior Analytics
Notification
Center
AD
Management
Device Management
  Device profiling, control and status
OTA Management
  Support GOTA
  Device grouping, incremental mode
App Management
  App installation, ordering, video recommendation
User Behavior Analytics
  Device related statistics – members, active users, device map, RCU button clicks
  Apps related statistics – App ranking(usage, watching, clicks), installation ranking, hour distribution
Notification Center
  Promotion/emergency notification messages
  TV Mail/Ticker
Advertising Management
  AD schedule
Dashboard UI
  Recent trend statistics
ACS system supports operator to manage devices, OTA FW upgrade, notification, promotion, understand subscriber's behavior and preference, which can lower A/S maintenance manpower.
ACS System

## Slide 80
Foxconn Confidential & Proprietary
For OTT Operators to understand user preference.
For next generation product planning
For new services planning
Online Status
Android Version
FW Version
HDMI Input Status
Language
Network Type
TV Brand
Model
Why ACS (Auto Configuration System)
8.5 Upgrade and Management

## Slide 81
Foxconn Confidential & Proprietary
New Member Bar Chart
Location Ranking
Watching Hours
Accumulated App Clicks
App Usage Comparison
App Usage in 24 Hours
Active User Ratio
App Installation Ratio
ACS System
8.5 Upgrade and Management

## Slide 82
Foxconn Confidential & Proprietary
Device Grouping
Configuration Provisioning
Remote Screen Capture/Reboot
BT RCU Info & Un-Pairing
HDMI Output Control
Device Status Reporting
Debug/Log Collection
Firmware Upload
Group Scheduling
FW Download Progress
User/System Force Update
FW Update History
Online Status
FW Version
TV Brand
Network Type
Screen Resolution
Sound/CEC/ Language
HDMI Input Config.
DVB-C Signal
Network Speed
Device Info Importing
Account Management
Role-Based Access Control
Bandwidth Conf.
Connection Conf.
IP Range Settings
Member Stats
Member Device Distribution
App Usage Stats
App Installation Ranking
RCU Buttons Profiling
Advanced Search
Statistics Report
Device Mgmt.
OTA
Mgmt.
Device Profiling
UBA
Admin Mgmt.
App
Mgmt.
APK File Upload
App Installation/ Removal
App Icons Ordering
App Notification Center
App Recommendation
PS: 1. ACS: Auto Configuration System
2. OTA: Over The Air 3. UBA: User Behavior Analysis
8.5 Upgrade and Management: ACS Features

## Slide 83
Manus, Brazil
PCBA, BOX Build
n
n
n
n
Santa Clara, CA
NPI, NA Hub, Engineering Service, Enclosure
San Jose, CA
NPI, Engineering Service, PCBA & BOX Build
Czech Republic
Enclosure, ATO, EU Regional DF Site
Houston, TX
ATO, North America Regional DF Site
TuCheng/HsinChu,
Taiwan
Engineering Service
JDM/ODM Design
Guanlan, China
ATO, Asia / China Regional DF Site
Long Hua, China
NPI,Repair, Engineering
Service, PCBA, Enclosure,
BOX Build, B/P
JDM/ODM Design
Song Jiang, China
Enclosure, B/P, BOX Build, NPI,
JDM/ODM Design
Chongqing, China
PCBA, BOX Build
Chennai, India
Enclosure
Bac Ning/Bac Giang, Vietnam
PCBA, BOX Build
Juarez, Mexico
PCBA, DF
Hang Zhou, China
PCBA, BOX Build
Hungary
CTO,ATO, EU Regional DF Site
Mass Production Facilities
Research & Development
n
Proposed PCBA Mfg node
n
n
Slovakia
PCBA, BOX Build
Production Subject-domestic and overseas production sites
13. Monthly mass production and quality control capability
Nanning, China
NPI,PCBA,Enclosure,Box Build
NPI,Repair, Engineering Service,
JDM/ODM Design
Bac Giang, Bac Ning, Vietnam
NPI,PCBA,Enclosure,Box Build
NPI,Repair, Engineering Service,
Notes: Manus – Box Build
Sylovras… - PCBA / Box Build

## Slide 84: Production Subject-Foxconn Vietnam Bac Giang campus
B01
B02
B03
A01
A02
A03
P06
P03
P05
P02
P01
P05A
F zone
M zone
3km
Bac Giang #1
Quang Chau IP
Bac Giang #2,#3
6 Factory buildings
5 Dormitory buildings
Land area 120,000 m2
Production area: 65,000m2
Fii : 32,500m2
10,000 employees (Fii: 4,500 employees)
Bac Giang #1
5 Factory buildings
Land area 55,000 m2
Production area: 52,000m2
2,000 employees
Bac Giang #2
(P Zone)
Total planning 12 Factory buildings
Land area 260,000m2
Q3'20- 4 Factory buildings ready (F12/F13/F16/F17)
Q4'20- 5 Factory buildings ready (F02/F03/F06/F07/M11)
Other 3 buildings under planning in Y2021/Q1
Total production area: 310,000m2 (3 Floors for each Factory building)
Bac Giang #3
(F&M Zone)
84
13. Monthly mass production and quality control capability
Notes: 84

## Slide 85: Production Subject-Foxconn Vietnam Bac Ninh campus
3km
6 Factory buildings
4 Dormitory buildings
Land area 120,000 m2
Production area: 68,400m2
Fii : 55,500m2
9,500 employees (Fii : 8500)
Bac Ninh #1
(B Zone)
2 Factory buildings
Land area 12,000 m2
Production area: 13,000m2
1,200 employees
Bac Ninh #2
(C Zone)
1 Factory building with 3 Floor
Land area: 20,000m2
Production area: 31,000m2
2,500 employees
Bac Ninh #3
(BN3)
B01
B02
B03
B04
B05
B06
C02
BN3
C03
85
13. Monthly mass production and quality control capability
Notes: 85

## Slide 86
Fii Vietnam Capacity
Over 120 SMT lines
Daily capacity over 285Kpcs
Monthly capacity over 7,500Kpcs
Expanding capacity to support more customers
Chart: 2020 Foxconn Vietnam Build Products
| Set-Top Box | Cable Modem | Wireless (Lan) | XDSL | Smart power meter | IP Camera | Door Bell | Mesh Router | MPOS | BTS/Switch | Other
 | 21239.056 | 11941.071 | 7637.103 | 7077.596 | 6707.383 | 3391.74 | 1513.562 | 1508.427 | 1156.888 | 917.167 | 1437.768
13. Monthly mass production and quality control capability
Notes: eMTA: embedded Multimedia Terminal Adapter
WeMTA
86

## Slide 87
Production factory
Direct production with factory in Vietnam
Factory Name: Funing Precision Component Co.,Ltd
13. Monthly mass production and quality control capability

## Slide 88: Maintenance-SW Development System
 | Source Code Control | Bug Tracking System | Android App Developer | Project Management
Foxconn Internal |  |  |  | 
Work with Customers/Chip Vendors |  |  |  | 
Git Server
Git Server
14. Maintenance quality management A/S capability

## Slide 89: Technical Support-SW
Jacky Chiang
SW Manager
Kerwin Chen
SW Lead
River Wong
SW Engineer
Jim Chen
SW Engineer
Jason Ling
SW Engineer
Brent Choi
SW Engineer
Jerry Lin
SW Engineer
Bcan Yeh
SW Engineer
Sam Yang
SW Engineer
Peter Chen
SW Engineer
14. Maintenance quality management A/S capability

## Slide 90
Sean Chiang
HW Manager
Tom Lee
HW Lead
Fu-Chiang Yang
HW Engineer
Catherine Chen
HW Engineer
Charge Tseng
ME leader
Ace Liu
ME
Andy Qin
Layout leader
Ming Rong
Main board layout
Enya
Subboard layout
Allen Chang
ID/Package leader
Lydia Liu
Package design
Aglaia Lee
ID design
Jason Kung
Compliance lead
Jonah Lee
EMC test debug
Wen Chao
EMC test
Technical Support-HW/Layout/ME/Package/Compliance
14. Maintenance quality management A/S capability

## Slide 91
Wilson Kao
SQA leader
James Kuo
Dolby Cert., SIT
Bryan Yang
ATV CTS cert., SIT
Beca Ding
ATV CTS cert., SIT
Kenji Chen
HWQA leader
Tommy Chen
Reliability, mechanical
Leif Lin
Package test
Technical Support-HWQA/ SQA
14. Maintenance quality management A/S capability

## Slide 92: Quality Management System
Quality management certificate
  TL9000
  ISO9001
Quality goals, performance indicators, performance management data
  Please refer to the manual
Internal audit plan, results, and corrective action data
  The audit is conducted every 6 months by team comprised of internal professionals
  Please refer to the attachment
14. Maintenance quality management A/S capability

## Slide 93
RMA specification could refer to Eagle project
14. Maintenance quality management A/S capability