## Slide 1
SWAN K18X001.00 Button issue
1
JBD-VN-ME

## Slide 2
1. Abnormal height of Ejector mask
The height of the ejector mask is 0.15~0.25mm, so that the button can not all extend out of the housing.
Gap:0.15~0.25 mm
Gap:0.15~0.25 mm

## Slide 3
2. The button offset
The button is deflected to one side, which makes it easy to get stuck.

## Slide 4
3. The button is deformed
The button is deformed, and the height of the buttons is inconsistent after assembly.
來料按鈕凹陷

## Slide 5
4. Vendor rework issue.
毛邊
毛邊
毛邊
毛邊
FII reworking
There are still burr after INKEL sorting

## Slide 6
5. Design modify Suggest
No gap after Button &Key board assembly.
The touch of the button is not good due to the influence of pulling force.
Change the gap between Button and Key board to 0.3mm

## Slide 7
5. Design modify Suggest
The button is deflected to one side after assembly.
Increase positioning pins and chamfer on top cover.
There are positioning pins on Key Board &Button
No positioning pins on Button &Top cover
Shift
Shift
Shift
Shift
Increase chamfer