## Slide 1
BlueTool Install and Test Command

## Slide 2
Ground
UART_Tx
UART_Rx
HW Rework:
Main board connects to Console board
UART_TxTXD
UART_RxRXD
GroundGND
Console board
Bottom side of Main board
Schematic

## Slide 3: NOTE
If display error message, need to
(1) DUT Reset (power off and then power on again)
(2) Re-plug in USB to TTL dongle
(3) Close BlueTool and open tool again

## Slide 4: A. Install BlueTool
Open Bluetool folder  Install ActivePerl-5.8.4.810-MSWin32-x86
Install BlueTool

## Slide 5
1

## Slide 6: B. Enable Test Mode
2. Open BlueTool
3. From the View menu, select Log Window
4. From the Transport menu, select HCI Control
DUT Power on, plug in USB within 5 second
NOTE
Page 7-9 must to complete within 30 second

## Slide 7
5. (1) In Select HCI Control Window Transport, select UART
(2) Key-in COM PORT, the same with device manager
(3) Select baud rate to 115200
(4) Cancel CTS flow control
(5) Click OK
(1)
(2)
(3)
(4)
(5)

## Slide 8: Reset
6. In the HCI Control Command Window
  Select 7.3 Host Controller & Baseband Command
  In the main body of the window, double-click Reset
  (3-1) Deliver first reset within 30 sec at DUT power on
  (3-2) wait to success message at the last line reads status = 0x0 (0, "Success")
(1)
(2)
(3-1)
Deliver first reset within 30 sec at DUT power on
(3-2)

## Slide 9: Download Firmware
7. Download Firmware
  From the Transport menu, select Download Firmware
(1)

## Slide 10
(2)
  Import  Select CYW20704A2_001.002.011.0296.0298
(3)
Cancel
(4)
Cancel
(5)
Select from burn image
(6)
Select download configuration record  Locate  Select CYW20704A2_001.002.011.0296.0298.hcd
(7)

## Slide 11
  Display Download completed and next step

## Slide 12
8. (1) After Load FW  select HCI control window  select HCI protocol active
(2) Click Reset
(3) In the log window, the last line reads status = 0x0 (0, "Success")
(1)
(2)
Reset
(3)

## Slide 13
9. Set Event Filter
Success : In the log window, the last line reads status = 0x0 (0, "Success")
10. Write Scan Enable
  Success : In the log window, the last line reads status = 0x0 (0, "Success")
Connection setup
Allow connection from devices
Do auto accept the connection with role switch disable
Inquiry and page scan enable

## Slide 14
11. Enable Test Mode
Success : In the log window, the last line reads status = 0x0 (0, "Success")

## Slide 15: C. Set Tx Carrier Frequency ARM