## Slide 1
EVT build PCBA to DVT build PCBA change history

## Slide 2
Changing the cable connector to FCC connector which will interfere with bottom cover, and the bottom cover need to be modified.
Original PCBA
Current PCBA
LED Board
Need to modify Bottom cover accordingly
Open status：Before assembling the FFC
Close status: After assembling the FFC
FCC connector

## Slide 3
Original PCBA
Current PCBA
Button Board and Mic Board
Changing the cable connector to FCC connector on the Mic board which will interfere with mic-holder-part and silicon-mic, so the mic-holder-part and silicon-mic need to be modified.
Need to modify mic-holder-part and accordingly silicon-mic
Mic holder part
Mic silicon part

## Slide 4
Original PCBA
Current PCBA
Side LED Board
Changing the cable connector to FCC connector on the Side LED Board.

## Slide 5
Original PCBA
Current PCBA
SoC Board
Changing the cable connector to FCC connector on the SoC Board and moving the position of some connectors.
3mm

## Slide 6
Original PCBA
Current PCBA
Amp Board
Moving the position of some connectors.

## Slide 7
Cable routing
Side LED Board to LED board
Original cable
Current FFC cable

## Slide 8
Cable routing
SoC Board to LED board
Original cable
Current FFC cable

## Slide 9
Cable routing
SoC Board to Button board and Mic board
Original cable
Current FFC cable

## Slide 10
Cable routing
SPK to Amp board
Original Amp board
Bottom view
SPEAKER_CORD_ASSY_LEFT
SPEAKER_CORD_ASSY_RIGHT

## Slide 11
Current Amp board
SPEAKER_CORD_ASSY_LEFT
SPEAKER_CORD_ASSY_RIGHT
Bottom view

## Slide 12
Cable assembly
OR

## Slide 13
Cable assembly
Sponge for all FFC cable