## Slide 1: Command line

## Slide 2: Console Pin Definition
Connect console
Ground
Tx
Rx
1
2
3
4
5
1
2
3
4
5
GND
GND
TX
RX
3.3V

## Slide 3: Direct Test Mode
Su
echo 0 0 0 0 > /proc/sys/kernel/printk
service call bluetooth_manager 8 // Disable BT Service
rtlbtmp
enable usb:/dev/rtkbt_dev
bt_mp_Exec 1 // enable test mode
bt_mp_Exec 0 // (HCI Reset) stop test

## Slide 4: BR/EDR continue TX test
bt_mp_SetParam 1,0;2,0x02;3,0x05;4,0x00;6,0x7F;7,0x00;9,0xA078;11,0x000000c6967e //channel 0 (2402MHz),DH5
bt_mp_SetParam 1,0;2,0x05;3,0x05;4,0x00;6,0x7F;7,0x00;9,0x3F870;11,0x000000c6967e //channel 0 (2402MHz),2DH5
bt_mp_SetParam 1,0;2,0x08;3,0x05;4,0x00;6,0x7F;7,0x00;9,0xA078;11,0x000000c6967e //channel 0 (2402MHz)，3DH5
bt_mp_SetParam 1,39;2,0x02;3,0x05;4,0x00;6,0x7F;7,0x00;9,0xA078;11,0x000000c6967e //channel 39 (2441MHz)，DH5
****************************************************
bt_mp_Exec 34 //start tx 30 for FW_packet tx
bt_mp_Exec 35 //stop tx 31 for FW_packet tx stop
When testing another set of bt_mp_SetParam, must to input stop command first
su
echo 0 0 0 0 > /proc/sys/kernel/printk
service call bluetooth_manager 8 // Disable BT Service
rtlbtmp
enable usb:/dev/rtkbt_dev
Initial Command
Enable success

## Slide 6
bt_mp_SetParam 1,0;2,0x02;3,0x05;4,0x00;6,0x7F;7,0x07;9,0xA078;11,0x000000c6967e
ChannelNumber  value range : 0~78
a
a
b
b
PacketType
c
c
PacketHeader

## Slide 7: Sigle Tone Tx Mode
bt_mp_SetParam 1,0;2,0x08;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e
//channel 0 3DH5 single tone tx mode
Bt_mp_SetParam 1,39;2,0x08;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e
//channel 39 3DH5 single tone tx mode
bt_mp_SetParam 1,78;2,0x08;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e
//channel 78 3DH5 single tone tx mode
****************************************************
bt_mp_Exec 34 //start tx
bt_mp_Exec 35 //stop tx

## Slide 8: Hopping test
bt_mp_SetParam 2,0x00;10,0x00;6,0xFF;18,0,78 // DH5
bt_mp_SetParam 2,0x05;10,0x00;6,0xFF;18,0,78 //2DH5
Bt_mp_SetParam 2,0x08;10,0x00;6,0xFF;18,0,78 // 3DH5
bt_mp_SetParam 2,0x09 // BLE
**************************************************
bt_mp_Exec 21 //start
bt_mp_Exec 0 //stop

## Slide 9: BLE5.0 TX test (1M)
bt_mp_SetParam 1,0;3,0x00;15,0xff;16,1 //channel 0 (2402MHz)，BLE
bt_mp_SetParam 1,19;3,0x00;15,0xff;16,1 //channel 19 (2421MHz)，BLE
bt_mp_SetParam 1,39;3,0x00;15,0xff;16,1 //channel 39 (2441MHz)，BLE
********************************************
bt_mp_Exec 22 //LE TX TEST
bt_mp_Exec 24 //LE TEST END

## Slide 10: BLE5.0 TX test (2M)
bt_mp_SetParam 1,0;3,0x00;15,0xff;16,2 //channel 0 (2402MHz)，BLE
bt_mp_SetParam 1,19;3,0x00;15,0xff;16,2 //channel 19 (2421MHz)，BLE
bt_mp_SetParam 1,39;3,0x00;15,0xff;16,2 //channel 39 (2441MHz)，BLE
********************************************
bt_mp_Exec 22 //LE TX TEST
bt_mp_Exec 24 //LE TEST END

## Slide 11: BLE TX test _ ch0－39 */ 2,0x09=PRBS9
bt_mp_SetParam 1,0;2,0x09;3,0x30;4,0x00;7,0x00;15,0x25 //channel 0 (2402MHz)，BLE
bt_mp_SetParam 1,19;2,0x09;3,0x30;4,0x00;7,0x00;15,0x25 //channel 19 (2421MHz)，BLE
bt_mp_SetParam 1,39;2,0x09;3,0x30;4,0x00;7,0x00;15,0x25 //channel 39 (2441MHz)，BLE
********************************************
bt_mp_Exec 36 //start tx
bt_mp_Exec 37 //stop tx

## Slide 12: BLE Single Tone
bt_mp_SetParam 1,0;2,0x09;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e //channel 0 BLE single tone tx mode
bt_mp_SetParam 1,19;2,0x09;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e //channel 19 BLE single tone tx mode
bt_mp_SetParam 1,39;2,0x09;3,0x00;6,0xFF;7,0x00;9,0x3FFFF;11,0x000000c6967e //channel 39 BLE single tone tx mode
****************************************************
bt_mp_Exec 36 //start LE tx
bt_mp_Exec 37 //stop LE tx

## Slide 13: RX test / by No-Signaling /PRBS9 payload_type
bt_mp_SetParam 1,0;2,0x00;3,0x07;6,0xFF;9,0x33820;11,0x000000c6967e //channel 0,DH1
bt_mp_SetParam 1,39;2,0x02;3,0x07;6,0xFF;9,0xA078;11,0x000000c6967e //channel 39,DH5
bt_mp_SetParam 1,39;2,0x05;3,0x07;6,0xFF;9,0x3F870;11,0x000000c6967e //channel 39,2DH5
bt_mp_SetParam 1,78;2,0x08;3,0x07;6,0xFF;9,0xA078;11,0x000000c6967e //channel 78,3DH5
bt_mp_Exec 32 //start rx
bt_mp_Report 3
//Report Received Result /format RxRssi,RXBits,RxCounts,RxErrorBits/ “bt_mp_Report 3” should be executed every 1s.
bt_mp_Exec 33 //stop rx

## Slide 14: BLE RX test /Measure the DUT BLE Rx sensitivity
bt_mp_SetParam 1,0;3,0x07 //ch0,Payload Type:PRBS9
bt_mp_SetParam 1,0;2,0x09;3,0x07 //ch0,Payload Type:PRBS9
bt_mp_Exec 23 //Run LE_RX_DUT_test
bt_mp_Exec 24 //LE_RX_DUT_Test_End; stop LE packet RX and to obtain the receive packet count
k
bt_mp_Report 11 //Rx RxCounts
--------------------------------------------------------------------------------------------------------------------------------------------------------------------
bt_mp_SetParam 1,0;2,0x09;3,0x07

## Slide 15: Adjust Tx Power By Command
Get TX power level
bt_mp_Exec 38
bt_mp_Report 17
Set TX power level to ram: Default (1M=0x3C);(2M=0x43);(3M=0x43),(BLE=0x3C)
bt_mp_SetParam 18,0x3C,0x43,0x43,0x3C,0x3C;
bt_mp_Exec 51
BT 1M
BT 2M
BT 3M
LE 1M
LE 2M
BT1M
BT2M
LE1M
BT3M
LE2M
Notice: If DUT restart and need to set power value again

## Slide 16: Tx Power Table