## Slide 1
[AI2 MAX Soundbar STB]
Standby Mode definition(Active Standby vs Passive Standby)
Organization
R&D Lab. 2
Version
0.1
Issued Date
2021.05.21

## Slide 2
Revision History
Version | Date | Description | Owner
0.1 | 2021/05/21 | 1st Draft version | Lonnie Kim

## Slide 3
Active & Passive Standby

## Slide 4
Active Standby Condition
HDMI output OFF
Ethernet ON
FFV MIC ON
BT ON
A113X ON
AMP IC:
1) Below Register OFF
through I2C
- SHDN(Shut down)
- PWM

## Slide 5
Passive Standby Condition(Phase 1): Under 2W
HDMI output OFF
Ethernet ON
FFV MIC Sleep Mode
BT Sleep Mode
A113X OFF
AMP IC OFF
(A113X & AMP: appendix)

## Slide 6
APPENDIX

## Slide 7
APPENDIX(Will apply Mass production)
A113X OFF
AMP IC OFF
Using “CTRL_A113X(J813 pin6)
 CTRL_A113X connected to 5V_EN
(VS550 can control Audio Amp block’s power)
 Enable Audio Amp Block
> 5V_EN : High
> I2C Control(initialize)
 Disable Audio Amp Block
> I2C Control(Off)
> 5V_EN : Low

## Slide 8
Thank you.