## Slide 1
The rib height of the received sample is 12mm, but the dimension in 3D is 10mm. The speaker will interference with bottom cover so that it can not be assembled.
Housing sample
3D on March 30th
Assembly issue
Bottom cover
Speaker
Interference

## Slide 2
Housing sample
3D on March 30th
Assembly issue
Heatspreader for DVT3
Bottom cover
SoC board
The SoC board can not touch the fix-boss with Heatspreader for DVT3.