## Slide 1: Audio Routing for BT Sink mode
FII: River

## Slide 2: Background Connect BT mobile (SWAN in BT sink mode) Android Original Design
Android Framework
Audio Flinger
AudioTrack
BT Mobile
AUDIO_STREAM_MUSIC
BT Stack
Android Framework
Audio Flinger
AudioTrack
BT Mobile
YouTube
AudioTrack
AUDIO_STREAM_MUSIC
BT Stack
Play YouTube
AUDIO_STREAM_MUSIC
BT sink is paused because of receiving AudioFocus_LOSS from YouTube playing.
Request AudioFocus

## Slide 3: Background Connect BT mobile (SWAN in BT sink mode) Original Issue: BT sink is paused by HOME UI
Android Framework
Audio Flinger
AudioTrack
BT Mobile
AUDIO_STREAM_MUSIC
BT Stack
Android Framework
Audio Flinger
AudioTrack
BT Mobile
HOME UI
AUDIO_STREAM_MUSIC
BT Stack
Enter Home UI
BT sink is paused because of receiving AudioFocus_LOSS from HOME UI showing up (Ex. User press HOME key of RCU).
Request AudioFocus

## Slide 4: Jira BTVSBOX510 SK asks for the same implement as AI2
AI2’s Behavior:
BT audio is continuing playing.
Mute other streams when YouTube or other APPs are playing.
Modify BT sink to ignore AudioFocus_LOSS event to avoid being paused while HOME UI gets AudioFocus.
Google Assistant is not supported in AI2 AOSP, so it can not test.

## Slide 5
Android Framework
AudioPolicyManager
Audio Flinger
BT Stack
AudioTrack
BT Mobile
YouTube
AudioTrack
Only BT stream will be output
handleSKBStreamAndDevice()
AUDIO_STREAM_MUSIC
AUDIO_STREAM_NUGU
How AI2 implements it:
1.AI2 set BT AudioTrack to AUDIO_STREAM_NUGU.
2.AI2 uses handleSKBStreamAndDevice() to mute other streams (OTH=>NUGU) by monitoring
STARTING_OUTPUT and STOPPING_OUTPUT events. 3.BT sink ignore AudioFocus_LOSS to keep playing.
Ignore AudioFoucs_LOSS
HOME UI
Request AudioFocus
Ai2 Implementation

## Slide 6: Questions
handleSKBStreamAndDevice() is removed by SPTEK, it seems to handle Streams mute/unmute in BroadcastReceiver of AudioService. Could you explain your current design? And advise how we should handle this BT sink case to co-work with you?
We found SPTEK add code in BroadcastReceiver of AudioService to handle “bt_sink” event, do we need to send intent to notify you that BT sink mode is enabled? But it seems does not check bt_sink is enabled or not in handling other events. Who will be in charge of handle BT sink enabled case in other events?
BT Mobile input audio is set to AUDIO_STREAM_NUGU, is it right? It will share NUGU volume curve. If it is wrong, will you add anther Audio Stream type for it?
How to handle Google Assistant(AUDIO_STREAM_MUSIC) when in BT sink mode case? Do you have any suggestion?

## Slide 7: BT sink + Google Assistant
Android Framework
AudioPolicy
Audio Flinger
BT Stack
AudioTrack
BT Mobile
YouTube
AudioTrack
Only Google Assistant will be output
AUDIO_STREAM_MUSIC
Google Assistant
AudioTrack
AUDIO_STREAM_MUSIC
Ignore AudioFoucs
abandonAudioFoucs by GA