## Slide 1: Audio Routing for BT Sink mode 1.NUGU end to resume BT sink 2.Google Assistant vs. NUGU
FII: River

## Slide 2: Background BT Sink restarts after NUGU end Original Google Design
Android Framework
Audio Flinger
NUGU Start
BT Mobile
Google BT Sink
AvrcpService
“pause”
AudioFocus_Loss_Transient
Request
AudioFocus
Android Framework
Audio Flinger
NUGU
End
BT Mobile
Google BT Sink
AvrcpService
“play”
AudioFocus_Gain
BT Stack
BT Stack
BT sink is current AudioFocus
before NUGU start

## Slide 3: Background Issue happens when Other Apps get AudioFocus
Android Framework
Audio Flinger
NUGU Start
BT Mobile
Google BT Sink
AvrcpService
AudioFocus_Loss_Transient
Request
AudioFocus
BT Stack
YouTube
Youtube is current AudioFocus
before NUGU start
Android Framework
Audio Flinger
NUGU
End
BT Mobile
Google BT Sink
AvrcpService
AudioFocus_Gain
BT Stack
YouTube
Mute by “bt_sink”

## Slide 4: BT Sink does not restart after NUGU end
Android Framework
Audio Flinger
NUGU Start
BT Mobile
SptekBluetooth
AvrcpService
“pause”
NUGU_BT_CTRL_REQUEST
?APP
Android Framework
Audio Flinger
NUGU Stop
BT Mobile
BT Stack
SptekBluetooth
AvrcpService
No NUGU_BT_CTRL_REQUEST
?APP
YouTube
BT Stack
YouTube
YouTube is current AudioFocus
before NUGU start

## Slide 5: Google Assistant vs. NUGU
We can not always output Google Assistant TTS to Speaker as the same as NUGU, because in pass-through mode, MUSIC stream volume is set to 32 level and is NOT adjustable. So if we output Google Assistant to Speaker in pass-through mode, Assistant audio will be very loud.
So, we will let Google Assistant output to the same device as BTV/YouTube

## Slide 6: Google Assistant vs. NUGU
BTV/Youtube is forced to MAX 32 level in pass-through mode.
Android Framework
NUGU
AudioTrack
AUDIO_STREAM_NUGU
stream_
volume.xml
for NUGU
Android Framework
Google Assistant App
AudioTrack
AUDIO_STREAM_MUSIC
stream_
volume.xml
for BTV/Youtube
NUGU has it’s own volume curve and is not set to
Max volume in pass-through mode.
Max Level 32