## Slide 1
5014SGLH6-ES-L2-TR
异物分析報告
Foreign body analysis report
Prepared: Vic
Approved: Herry
Date: 2023/3/23

## Slide 2
D1 Establish Team Approach
Champion (主要負責人員) :
Team Leader (FRB主席) : 宋小春—xiao chun Song
Team Member (成員)
生产(production)---刘平珍
品管(Quality control)---邹振元
設計(design)---罗禅
资材(material)---刘玉海
製工(fabricator)---李 強
Team UP meeting (會議發起):
 When (時間) : 2023-3-18
 Where (地點) : 公司會議室

## Slide 3
1. Who：Foxconn(越南)
2. Which：5014SGLH6-ES-L2-TR
3. When：2023.3.18
4. Where：客戶端抽檢工站(Client sampling station)
5. What： Plug無法插到位,不良1PC；具體如下圖所示（The Plug can not be inserted in place, and the 1PC is not good. The details are shown in the following figure）：
D2 Description Problem

## Slide 4
D3 Root Cause & Findings
3.1 工艺图排查，风险工站确认
3.1 Process drawing check and risk station confirmation
经对制程组装过程进行确认，可确定此为风险工站
After confirming the assembly process of the manufacturing process, it can be determined that this is a risk station

## Slide 5
D3 Root Cause & Findings
3.2 异物产生工站确认
3.2 Confirmation of foreign body production station
对组装过程确认，可确定此为异物产生工站
To confirm the assembly process, it can be determined that this is the foreign body generating station

## Slide 6
D3 Root Cause & Findings
3.3 异物产生真因确认
3.3 Confirmation of the true cause of foreign bodies
小结；
summary;
1、经过确认公头内圆环为测试机台的探头铜环，测试探头长时间测试使用，出现损伤。
1. After confirming that the inner ring of the male head is the probe copper ring of the testing machine, the test probe has been tested for a long time, resulting in damage.
2、经过确认生技保养记录，此测试探头使用次数达到6万次，经长时间使用，导致磨损/损伤，测试时探头铜环脱落留在DC内。
2. After confirming the production technology maintenance record, the test probe has been used for 60,000 times, which leads to wear/damage after a long time of use. During the test, the probe copper ring falls off and stays in DC.
功能测试探头
Functional test probe
确认为测试探头铜环
Confirm as test probe copper ring

## Slide 7
4.1 增加测试探头的使用寿命管控（调整为5万次），以此防止测试探头使用次数过多，导致铜环脱落。
4.1 Increase the service life control of the test probe (adjust to 50,000 times) to prevent the copper ring from falling off due to excessive use of the test probe.
---責 任 人（Responsible person）：李強
---完成時間（Completion time）：2023/03/23
4.2 将此不良异常，制作为“不良看板”，进行内部宣导，并悬挂于生产现场警惕作业人员，随时检查测试探头的磨损/损伤情况。
4.2 Make the bad anomaly as "bad Kanban" for internal promotion, and hang it on the production site to alert operators and check the wear/damage of the test probe at any time.
---責 任 人（Responsible person）：Arvin
---完成時間（Completion time）：2023/03/20
D4 Corrective Action