## Slide 1
May 9th 2020
ALT S905X3 OTT Stick Proposal

## Slide 2: Reference Project 1
Dimension | - 97.2mm x 45.5mm x 17.48mm
Wi-Fi 2.4G 1T1R Connection | - Support 11N single band 1T1R - Data rate up to 150Mbps
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240VAC input, 5V/1A DC output
Safety Certification | 
OTT Box ID
Highlight
Technical Specification
Chipset | Memory
AML S805Y Quad core ARM Cortex-A53 CPU up to 1.5GHz Penta-core ARM Mali-450 GPU up to 750MHz+ | 1 GB DDR3 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.0b @ 1080p60 output x1, HDCP 2.2 RJ-45x1; 10Mpbs/100Mpbs LED for power on/off indication Micro-USB for 5V @ 1A DC input | Main stream box for HEVC Full HD video HLS/MS Smooth Streaming/MPEG-DASH, Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade Android TV certificated Netflix NTS certificated
Networking | Remote Control
10/100 Base-T Ethernet Wi-Fi 11n single band 1T1R Bluetooth 4.2 w/ BLE | BT4.2 RCU w/ voice input (with 4 hot keys)
Multimedia | Operating System
Decode H.265 HEVC MP-10@L4.1 up tp 1080P60 H.264 AVC HP@L4.2 up to 1080P30 VP9 profile-2 up to 1080P60 Encode H.264 up to 1080p30 | Android 9.0 Widevine Level 1/PlayReady DRM support
Confidential

## Slide 3: Reference Project 2
OTT Box ID Illustration
Highlight
Technical Specification
Dimension | T: 11.1mm; W: 30mm; L: 70.2mm
Wi-Fi | Wi-Fi 802.11 ac/a/b/g/n 1x1 dual band
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | DC 5V 1.2A
Safety/ Cert. | 
3
Chipset | Memory
AML S912-J Android 7.1 | 2 GB DDR4 16 GB eMMC flash
Interface | Features
HDMI 2.0b @ 4K2Kp60 output x1, HDCP 2.2 LED for power on/off indication Micro USB for DC input | Main stream box for HEVC/4K2K video Super smooth streaming, 4K 60fps decoding Google casting support Voice control
Networking | Remote Control
Wi-Fi 802.11 ac/a/b/g/n 1x1 dual band 10/100 Base-T Ethernet ( via adapter ) Bluetooth 4.1 w/ BLE | BT 4.0
Multimedia | Operating System
Decode H.265 HEVC MP-10@L5.1 4K2Kp60 H.264 AVC HP@L5.1 up to 4K2Kp30 VP9 profile 2 4K2Kp60 Dolby Vision and HDR10 support | Android TV WideVine level 1/Playready DRM support
Notes: 1. 一組 S/PDIF
2. 兩組 USB
3. 一組 Composite
3

## Slide 4
Reference Project 3
ID
Basic
Dimension | - 84.6mm(W) x 39.6mm(D) x 15mm(H)
Networking | Wi-Fi 802.11 ac 1T1R single band Bluetooth 4.1 w/ BLE
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240V AC input, 5V/1A DC output
Safety Certification | 
Technical Specification
Chipset | Memory
AML S905D Quad-Core Cortex-A53, 18,400DMIPS ARM Mali-G31 MP2, 850MHz | 1 /2 GB DDR4 (Optional) 8 /16 GB eMMC flash (MLC type) (Optional)
Interface | Features
HDMI 2.0b @ 4Kp60 output x1, HDCP 2.2 RJ-45 x1; 10Mbps / 100Mbps through PSU (option) | Main stream box for HEVC/4K video HLS/MS Smooth Streaming/MPEG-DASH, BT Voice control Android TV certificated Netflix NTS certificated (Optional)
Multimedia | Operating System
Decode H.265 HEVC MP-10@L5.1 up to 4Kp75 H.264 AVC HP@L5.1 up to 4Kp30 VP9 profile 2 up to 4Kp60 Encode H.264/H.265 up to 1080p60 | Android TV 9.0 Widevine Level 1/PlayReady DRM support
 | Remote Control
 | BT 4.2 RCU w/ voice input

## Slide 5: Reference 4: BANDOTT Smart Home Gateway Spec
OTT Box ID
Highlight
Technical Specification
Dimension / Weight | - 140× 127 × 29 mm / 315g
Wi-Fi 2.4/5GHz 2T2R Connection | - Support 802.11 ac/a/b/g/n - Data rate up to 866Mbps
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240VAC input, 5V/2A DC output
Safety Certification | BSMI / NCC certification
5
Chipset | Memory
AML S905D Quad-core 64bit ARM Cortex-A53 up to 2.0 GHz, Penta-cores Mali-450 up to 750MHz | 2 GB DDR3 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.0b @ 4Kp60 output x1, HDCP 2.2 HDMI input x 2 up to 1080i resolution USB 2.0 Host Type A x1 RJ-45 x1; 10Mbps / 100Mbps LED for power on/off indication Reset button IR extender (3.5mm phone jack) DC jack for 5V @ 2A DC input | Main stream box for HEVC/4K video HLS/MS Smooth Streaming/MPEG-DASH, 4K 60fps decoding Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade Android TV certificated Netflix NTS certificated
Networking | Remote Control
Wi-Fi 802.11 ac/a/b/g/n 2x2 dual band 10/100 Base-T Ethernet Bluetooth 4.1 w/ BLE | BT4.0 or IR based RCU
Multimedia | Operating System
Decode H.265 HEVC MP-10@L5.1 4Kp60 H.264 AVC HP@L5.1 up to 4Kp30 VP9 profile 2 4Kp60 Encode H.264 1080p60 | Android 7.1 Widevine Level 1/PlayReady DRM support Dolby AC3 support
Notes: 1. 一組 S/PDIF
2. 兩組 USB
3. 一組 Composite
5

## Slide 6
Dimension | - 167 × 111 × 35mm
Wi-Fi 2.4/5GHz 2T2R Connection | - Support 802.11 ac/a/b/g/n - Data rate up to 866Mbps
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240VAC input, 12V/2A DC output
Safety/ Cert. | TBD
6
Chipset | Memory
Realtek RTD1611 | 2 GB DDR4 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.0b @ 4Kp60 output x1, HDCP 2.2 USB3.0 Host Type A x 2 RJ-45 x1; 10/ 100 Mbps AV output (3.5mm phone jack) x 1 F-type CON x1; DVB-C Full-Band captured tuner x 1 7-Segment Display x 1 DC jack for 12V @ 2A DC input | Main stream box for HEVC/4K video HLS/MPEG-DASH/HDR 10/ HLG Google casting support BT Voice control Preload apps for TV services Over-The-Air image upgrade Android TV certificated Netflix NTS (optional) PVR
Networking | Remote Control
Wi-Fi 802.11 ac/a/b/g/n 2x2 dual band 10/100 Base-T Ethernet Bluetooth 5.0 w/ BLE | BT4.2 BLE
Multimedia | Operating System
Decode 4Kp60 10b H.265, VP9 Profile 2 1080p60 H.264 BP@L3, MP/HP@L 4.2 Encode H.264 BP/MP/HP@ L4.2 1080p60 | ATV (Android Q) Widevine Level 1/PlayReady DRM support
Reference 5: DVB-C 4K Hybrid OTT Specification
4K Hybrid Box
Technical Specification
Highlight

## Slide 7
Project | Reference 1 | Reference 2 | Reference 3 | Reference 4 | Reference 5
Country / Market | Japan | Japan | Taiwan | Korea, Taiwan, Hong Kong | Taiwan
B2B or B2C | B2C | B2C | B2C | B2C | B2C
(Planned) Launched date | EVT only | 2018/4 | 2018/1 | 2016/12 | 2020/4
Quantity of production | N/A | 20K | 10K | 250K in total | 30K
Reference 1~3 are products similar to the requested one.
Reference 4~5 are other products supporting Ethernet and WiFi.

## Slide 8
MINI BOX
Proposal

## Slide 9: Mini Box Specification
OTT Box ID
Highlight
Dimension | - 97.2mm x 45.5mm x 17.48mm
Wi-Fi 5GHz 2T2R Connection | - Support 802.11 ac/a/n
Operation environment | Temperature 0 ~ 40°C Humidity 10% ~ 90% relative humidity
Power adapter | 100~240VAC input, 5V/2A DC output
Safety/ Cert. | TBD
9
Chipset | Memory
AML S905X3 | 3 GB LPDDR4 8 GB eMMC flash (MLC type)
Interface | Features
HDMI 2.1 @ 4Kp60 output x1, HDCP 2.2 RJ-45x1; 10/100/1000 Mbps LED for power on/off indication Micro-USB for 5V @ 1A DC input | Main stream box for HEVC/4K video Google casting support Preload apps for TV services Over-The-Air image upgrade Android TV pre-certified Netflix NTS (optional)
Networking | 
10/100/1000 Base-T Ethernet Wi-Fi 802.11 ac/a/n 2x2 dual band Bluetooth 5.0 w/ BLE | 
Operating System | 
ATV (Android Q) Widevine Level 1/PlayReady DRM support | 
Technical Specification
Notes: 9

## Slide 10
S905X3 OTT Stick Block Diagram
S905X3
SoC
LPDDR4
SDRAM
3GB
32bits
eMMC
Flash
8GB
8bits
Crystal
24MHz
Front Panel
Wi-Fi 11ac/ BT 5.0
2T2R Chipset
RTL8822CS
UART
SDIO
Chip
Antenna *2
Crystal
40MHz
Back Panel
Power Block
DC-DC
5V
VDD_EE
VDD_CPU
VCC_3.3V
DDR_1.1V
VCC_1.8V
RGB LED*1
Micro USB
(USB2.0)
USB OTG D+/D-
TMDS/DDC_I2C/CEC/HPD
HDMI Female
Connector
eFuse
GPIO
Button*2
GPIO
Ethernet PHY
RJ45 Connector
RGMII

## Slide 11: PCBA placement-recommended box siz - 97.2mm x 45.5mm x 17.48mm

## Slide 12: The reason why the other placement is not chosen
If the USB and HDMI connectors are placed at 2 sides, the layout trace routing will be more complicated and hence enlarge the length.
Also the Ethernet port restricts the shortening of width.

## Slide 13: Wi-Fi Development Process (1/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
Wi-Fi spec. review
  Transmit power
  Frequency Band
Wi-Fi solution
  Interface : SDIO
  Chipset vendor : REALTEK
Locating Antenna position in STB
  Mechanical drawing
  Simulation(HFSS)
  RF cable path
Schematic and Layout Vendor review

## Slide 14: Design prepare
Mechanical drawing
Simulation (HFSS)
* RF cable path refer to above plot with gray and orange line
Return Loss
Efficiency
ANT1 | 5.15G | 5.35G | 5.55G | 5.85G
Efficiency(%) | 67 | 69 | 70 | 72
ANT2 | 5.15G | 5.35G | 5.55G | 5.85G
Efficiency(%) | 68 | 67 | 67 | 68
* Above is reference data, need to use actual PCB to test
OTT BOX

## Slide 15: Wi-Fi Development Process (2/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
802.11a/n/ac Spec. verification
  Transmit power measurement
  Transmitter spectral mask test
  Transmitter spectral Flatness
  Local Oscillator suppression & Center frequency tolerance
  Transmit Center Frequency Error
  Transmit Power On and Power Down Ramp
  Transmit modulation accuracy (EVM)
  Receiver minimum input level sensitivity
  Receiver maximum input level
  Adjacent channel rejection and Non-adjacent channel rejection
Chipset vendor review Conducted performance

## Slide 16: Conducted test
Test diagram
Test Step
DUT install RF test tool of module
Control PC connect IQxel or others equipment via Ethernet
Connect DUT and IQxel by 50 ohm cable and Ipex4 to SMA cable
Setting parameter by IQxel
Setting parameter by RF test tool and start test
Repeat step4 and step5
 | Q’ty
Control PC | 1
IQxel | 1
Ethernet cable | 1
50 ohm cable | 1
Ipex4 to SMA cable | 1
Test equipment list

## Slide 17: Wi-Fi Development Process (3/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
internal design target
  Frequency 5GHz: 5150 ~ 5350, 5470 ~ 5850MHz
  Directivity: ≥ +3dBi
  Efficiency: ≥ -50%
  VSWR: ≤ 2.0:1
  Return Loss : ≤ -10dB
Antenna passive test with mounting STB
  Antenna position: Simulation by using 3D antenna tool (HFSS)
  Antenna performance measurement in Anechoic chamber
Antenna 3D plot
The reason to reduce peak gain spec from +5dBi to 3dBi
Based on environment of dongle, expected to use chip antenna, but pattern design of chip antenna is fixed and the peak gain can’t be improved by adjusting antenna matching
Based on the design experience in previous project, the peak gain of chip antenna is about +3dBi

## Slide 18: Antenna Test
Test Step
DUT place on test platform
Parameter setting by test tool
Generate antenna gain, efficiency, 2D and 3D plot
DUT
DUT
Antenna Anechoic chamber

## Slide 19: Wi-Fi Development Process (4/5)
RvR(Wi-Fi Throughput Rate vs. Range in TCP) test (FNX: Realtek will provide test report of 8822CS as reference.)
  Test Spec.:
  Test condition
  - In anechoic chamber or shield room
WIFI Throughput Tx/Rx test
- In anechoic chamber
Design prepare
Conducted test
Antenna test
Radiation test
OTA test
Octobox environment setting
- Please refer test diagram , environment and condition to next page

## Slide 20: Radiation test
Actual test environment
Test diagram
5GHz (unit: 866Mbps) |  | Channel 36 | Channel 149 | Channel 161
RCU no pairing | Tx | 268 | 297 | 280
 | Rx | 256 | 256 | 257
RCU pairing | Tx | 265 | 293 | 277
 | Rx | 250 | 248 | 254
5GHz (unit: 866Mbps) |  | Channel 36 | Channel 149 | Channel 161
RCU pairing | Tx | 250 | 262 | 260
 | Rx | 236 | 256 | 237
Test Condition : RCU pairing/RCU non pairing
Test Condition : RCU pairing + Play 4K Video
* Above is reference data, need to use actual PCB to test

## Slide 21: Wi-Fi Development Process (5/5)
Conducted test
Antenna test
Radiation test
Design prepare
OTA test
Indoor OTA test
  Test Spec.: Min. Throughput ≥ 20Mbps @spot No
  Test condition
  - CH36 @5GHz and CH161
  - Test spot on FXN TW office
Outdoor OTA test
  Test Spec.: comparison data for reference sample
  Test condition
  - CH36 @5GHz and CH161
- Test place where is line of sight W/O WLAN AP
MP prepare
  Mass product automation program
  Manufacturing Spec. fix
Please refer test environment and procedure to next page

## Slide 22: OTA test
Indoor
Test Step for Indoor and Outdoor OTA test
DUT install Iperf3 client APK
The AP is placed at the green point in the picture
The DUT is placed at the red point 1 in the picture
Start Rx test
Repeat step 3 and step 4
NLOS - Rental House Test
Live signal without neighbors’ WiFi interference
Outdoor

## Slide 23: Wi-Fi Manufacturing Process (1/4)
Conducted test
Radiation test
Calibration
OBA test
Wi-Fi Calibration equipment
  List up FNX Factory WiFi test equipment for mass production.
Wi-Fi Calibration spec
  List up

## Slide 24: Wi-Fi Manufacturing Process (1/4)
Conducted test
Radiation test
Calibration
OBA test
Wi-Fi Calibration
Wi-Fi Verification(Conducted test)
Using IQxel80 or IQM8W
Description | Unit
PC | 1
IQxel80 or IQM8W | 1
RF connector | 4
RF cable | 5
Attenuator(10dB) | 1
Ethernet cable | 3
Shielding Box(Big) | 1
Fixture | 1

## Slide 25: Wi-Fi Manufacturing Process (1/4)
Conducted test
Radiation test
Calibration
OBA test
Wi-Fi Calibration spec
  List up

## Slide 26: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
WIFI Conducted test
  Test diagram
  Test spec
802.11a/n/ac . Frequency list, Test spec, Calibration & verification or only have verification
  Transmit power measurement
  Transmitter spectral mask test
  Transmit Center Frequency Error
  Transmit Power
  Transmit modulation accuracy (EVM)
  Receiver minimum input level sensitivity
  Receiver maximum input level

## Slide 27: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
WIFI Conducted test
  Test diagram
  Test spec

## Slide 28: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
Throughput test
  Test diagram
  Test spec

## Slide 29: Wi-Fi Manufacturing Process (3/4)
Calibration
Conducted test
Radiation test
OBA test
WIFI Radiation test
  Test diagram
  Test spec
* ALT Comment : Please update mass production test diagram and test environment
* FXN : It’s the same with WIFI throughput test

## Slide 30: Wi-Fi Manufacturing Process (4/5)
Calibration
Conducted test
OBA test
Radiation test
WIFI OBA test
  Test diagram
  Test spec->Connect internet and play YouTube content
* ALT Comment : Please update mass production test diagram and test environment

## Slide 31: Wi-Fi Manufacturing Process (2/4)
Calibration
Radiation test
Conducted test
OBA test
WIFI Conducted test (FXN: Please check if this is needed in MP production.)
  Test diagram
  Test spec
Throughput test
  Test diagram
  Test spec
* ALT Comment : Please update mass production test diagram and test environment

## Slide 32: Wi-Fi Manufacturing Process (3/4)
Calibration
Conducted test
Radiation test
OBA test
WIFI Radiation test
  Test diagram
  Test spec
* ALT Comment : Please update mass production test diagram and test environment
* FXN : It’s the same with WIFI throughput test

## Slide 33: Wi-Fi Manufacturing Process (4/5)
Calibration
Conducted test
OBA test
Radiation test
WIFI OBA test
  Test diagram
  Test spec->Connect internet and play YouTube content
* ALT Comment : Please update mass production test diagram and test environment

## Slide 34
Development schedule
Refer to the EXCEL file

## Slide 35: Reliability Test Plan

## Slide 36: Reliability Test Plan-Cont’

## Slide 37: Reliability Test Plan-Cont’

## Slide 38: Reliability Test Plan-Cont’

## Slide 39: S905X3 OTT Stick Power Consumption Chart
5V/611mA
DCDC
VDD_EE
0.84V/688mA
Efficiency = 90%
5V/128.4mA
5V/82.4mA
DCDC
Efficiency = 90%
VDDCPU
0.84V/441.6mA
DCDC
5V/233.2mA
Efficiency = 90%
3.3V/25mA
1.8V/160mA
VDDIO_BOOT/AVDD18/VDDIOX
DCDC
5V/88mA
Efficiency = 90%
LPDDR4 3GB
1.1V/360mA
3.055W
3.3V/280mA
1.8V/67mA
1.8V/83mA
RGB LED
5V/15mA
8GB eMMC
BT/WiFi chip
Ethernet
PHY
3.3V/13mA
3.3V/318mA
DCDC
●
1.8V/10mA
5V/64mA