## Slide 1
- On 12/28/2022, ALT customer feedback that they found out 1pcs has UHD(4K) Channel noise.
FATP can’t cover this failure by old test program
- On 03/09/2023, RD provided the video to verify at factory SW NG board occur noise when play video at factory SW.
Compare between old and new test Program
Summary:
- Based on HEVC standard video provided by RD/customer and using golden sample video to check.
Applied new test program on 03/09/2023 at FT1 station can cover this issue on FATP.
- From 03/09 to now, BFX-AT100 model produced 7838pcs and didn’t find any defective product relate to UHD(4K) noise issue.
Items | Difference test items | Remark | Log test
Old test program | - Items[12]:Check HDMI VP9 Video - Items[13]:Check HDMI H265 Video | Follow test plan | 
New test program | - Items[12]:Check HDMI VP9 Video - Items[13]:Check HDMI H265 Video - Items[14]:Check HDMI HEVC HDR10+ Video | Follow test plan and add test items “Check HDMI HEVC HDR10+ Video” |