## Slide 1
Report For Dec-2022 Mass Production Inspection

## Slide 2
Problems Description
#1
Issue Description | 
When | 2022.10.01
Who | ALT customer
Where | Korean
What | ALT customer request to analyze 5 RMA units, no boot issue
Why | The root cause is P3V3 power was shorted with GND
How | Product can not boot
How many | Total 5pcs and detail as table below:
No# | NG1 sample | NG2 sample | NG3 sample | NG4 sample | NG5 sample
MAC | 38D57AD8588B | 38D57ADA242B | 4CD577FFEFFF | 38D57ADA046F | 38D57AD810F4
SN | 2149688001202201093490 | 2149688001202201206149 | 2149688001202201069841 | 2149688001202201204082 | 2149688001202201072761
Production Date | 2022.02.10 | 2022.04.22 | 2022.01.07 | 2022.04.02 | 2022.01.22
Issue | No boot | No boot | No boot | No boot | No boot

## Slide 3
RMA Analysis Plan
Step | Items | Contents | Owner | Status | Result
1 | Visual inspection | Inspect appearance of housing | PD: Van Anh | Done | No damaged or any abnormal
2 | Baking | Baking 24h at 450C | PD: Van Anh | Done | N/A
3 | Re-test OBA function | Re-test function at OBA station | OBA: Tu | Done | 5/5 units can not boot
4 | Open housing & VI PCBA | Open housing and inspect PCBA | PE: Nam | Done | 4 units aren’t abnormal. 1 unit (NG5 sample) was burnt at R823, R824,R825, R826 locations. Therefore, can not further repair and analyze.
5 | Take X-ray | Take X-ray focus on: U1, U602, U801, U1101, U1001 locations | ME: Hugo | Done | PASS
6 | Failure Analysis of NG1~NG4 samples | Retest FATP | PE: Nam | Done | 4/4pcs no boot from UK station
 |  | Double check history record production data | PE: Nam | Done | No found abnormal
 |  | Measure impedance, voltage all power supplies | PE: Nam | Done | - For NG1+NG2: P3V3 (3.3V) and ETH_DVDD10 (1V) power supplies was shorted with GND. - NG3+NG4: P3V3 (3.3V) power supply was shorted with GND.
 |  | - For NG1+NG2 sample: Remove and measure impedance + VF of U801 location then compare with OK sample. - For NG3+NG4 sample: Remove & measure impedance + VF of U1 then compare with OK sample. | PE: Nam | Done | - For NG1+NG2: pins of U801 component relate to ETH_DVDD10 and P3V3 power supplies was shorted. - For NG3+NG4: all pins of U1 component relate to P3V3 supply was shorted.
 |  | - For NG1+NG2 sample: Changed new U801 (RTL8211F) then check boot up status. - For NG3+NG4 sample: Changed new U1 (S905X2 ) then check boot up status. | PE: Nam | Done | 4 units boot up normal.
7 | FATP | Re-test 4 RMA units at all test stations after changed new U801 and U1 material. | PD: Van Anh | Done | 4 units passed all test station.
8 | OBA test | Test function at OBA station. | OBA: Tu | Done | 4 units passed functional test at OBA station.
#2

## Slide 4
Visual Inspection
#3
Result: No found any damaged or abnormal.
Check appearance of housing
Visual Inspection Outside Housing |  |  |  |  | 
 | NG1 | NG2 | NG3 | NG4 | NG5
Top side |  |  |  |  | 
Bot side |  |  |  |  | 

## Slide 5
Re-test OBA Function
#4
Baking 5pcs RMA 24h at 450C.
Re-test function at OBA station.
Can not boot up
Result:
Baking 5pcs RMA 24h in 450 (Done).
5pcs can not boot up when re-testing at OBA station.

## Slide 6
Open housing and inspect PCBA, detail as table below:
NG sample | NG1 | NG2 | NG3 | NG4 | NG5
Top side |  |  |  |  | 
Bot side |  |  |  |  | 
VI Result | Pass | Pass | Pass | Pass | Burn at R823, R824, R825, R826 locations
PCBA Visual Inspection
#5

## Slide 7
Due to NG5 sample was burnt at R823,R824, R825, R826 locations  Therefore, can not further repair and analyze.
#5
Burnt locations
Result:
NG1 to NG4 samples is normal.
NG5 sample was burnt at 4 location, so can not further analyze..
PCBA Visual Inspection

## Slide 8
Take X-ray
#6
Take X-ray 5 locations : U1, U602, U1101, U1001, U801 of 5 NG samples, detail images as below:
NG# | Image
NG1 | 
NG2 | 
NG3 | 
NG4 | 
NG5 | 
U801
U1001
U1101
U602
U1
U801
U1001
U1101
U602
U1
U801
U1001
U1101
U602
U1
U801
U1001
U1101
U602
U1
U801
U1001
U1101
U602
U1
Result: No found any abnormality.

## Slide 9
Failure Analysis
#7
1.Auto copy flash by Burning Tool
(2’80 s)
UK
I
FT
FT1
RC
RC1
RC2
7.1 Re-test 5 NG samples at all test stations follow normal process.
5 NG samples can not boot from first station.
 Test station can cover 100% no boot issue
Result:
5 NG sample can’t boot at test station.
Test station can cover 100% this issue.