## Slide 1
Report
for Aug 2020 MP
BFX - AT100
Date : 15- Jan-2021
Prepared by: Heng Ruan

## Slide 2
Issue Description
5 June 2020, ALT customer complain [BFX-AT100] May 2020 Mass production issue.
Defect Total:
1. HDMI output noise (Critical ) : 2/500pcs (0.4%)
2. Can not google login with RCU (Critical) 1/500pcs (0.2%)
3. SET label print is not completely (Major) : 1/500pcs (0.2%)
4. Ethernet cable packing NG (Major) : Not counted (20%)

## Slide 3
Issue Description | Root Cause | Actions | Owner | Due Date | Status
Phenomenon: No HDMI output. Type: Critical Q’ty : 2/500pcs DR: 0.4% SN:2149688001202005107167 | 1. Checked history: This unit was passed all stations smoothly. 2. Re-Check at factory: Failed Function. - Retest FT station: Result FAIL (HDMVID:HDMI Video 4K60Hz test fail). - Retest FT1 station: Result FAIL (AU4K05: HDMI AUDIO 4K Value is High). 3. Visual inspection: did not find out abnormal. 4. X-ray did not find out abnormal as attached file: 5. Use multi-meter to check power P5V, P1V2, P2V5,P3V3, P1V8_eMMC P2V5,VDDCPU and VDDEE no issue found. 6. Check power when HDMI cable connect U1_J41( HDMI_TX0+), U1_J43( HDMI_TX0-) had abnormal. 7. Measuring impedance pin 1, pin 3 of J1401 find out U1_C43( HDMI_TX2+), U1_C45( HDMI_TX2-) had abnormal. 8. Check console information did not see abnormal. Please see attached file for detail measurement: Suspect U1(BGA) component issue. | 1. Measuring impedance pin 1, pin 3 of J1401 find out U1_C43( HDMI_TX2+), U1_C45( HDMI_TX2-) had abnormal. 2. Change new U1 (BGA) then pass. U1(BGA) component issue. 3. FXN SQE was responsible to inform for vendor this issue. 4. Vendor’s FA report, conclusion is that ESD caused HDMI pin leakage issue. 5. Fii production line ESD control for more improvement ESD at some risk station of ALT product. ( Att file ) 6. Every shift TE Engineer to check ESD status of all power cable, HDMI cable for test station and line leaders check regularly ion fan at all stations to prevent ESD issue during production. Please see attached file for more detail: | PE-Loc TE-Allan SQE-Khoa | 15-Jan | 
1. No HDMI output
FIL1401 FIL1402
U1

## Slide 4
Issue Description | Root Cause | Actions | Owner | Due Date | Status
Phenomenon: No HDMI output. Type: Critical Q’ty : 2/500pcs DR: 0.4% SN:2149688001202005131536 | 1. Checked history: This unit was passed all stations smoothly. 2. Re-Check at factory: Failed Function. - Retest FT station: Result FAIL (HDMVID:HDMI Video 4K60Hz test fail). - Retest FT1 station: Result FAIL (AU4K05: HDMI AUDIO 4K Value is High). 3. Visual inspection: did not find out abnormal. 4. X-ray did not find out abnormal as attached file: 5. Use multi-meter to check power P5V, P1V2, P2V5,P3V3, P1V8_eMMC P2V5,VDDCPU and VDDEE no issue found. 6. Check power HDMI cable connect did not find out abnormal. 7. Measuring impedance pin 1, pin 3 of J1401 find out U1_C43( HDMI_TX2+), U1_C45( HDMI_TX2-) had abnormal. 8. Check console information did not see abnormal. Please see attached file for detail measurement: Suspect U1(BGA) component issue. | Measuring impedance pin 1, pin 3 of J1401 find out U1_C43( HDMI_TX2+), U1_C45( HDMI_TX2-) had abnormal. 2. Change new U1 (BGA) then pass. U1(BGA) component issue. 3. FXN SQE was responsible to inform for vendor this issue.( SQE send NG material to Vendor for future analysis 07-Dec-2020 ) 4. Vendor’s FA report, conclusion is that ESD caused HDMI pin leakage issue. 5. Check all process in production line from SMT to packing station all control ESD strictly is normal. 6. . Fii apply special check ESD control for more improvement ESD at some risk station of ALT product. Please see attached file for more detail: | PE-Loc TE-Allan SQE-Khoa | 15-Jan | 
1. No HDMI output
FIL1401 FIL1402
U1

## Slide 5
Issue Description | Root Cause | Actions | Owner | Due Date | Status
Can not google login with RCU Type: Critical Q’ty : 1/500pcs DR: 0.2% SN:2149688001202005119978 | 1. Check production data no found abnormal issue. 2. Check log test history data of device. - RC1 & RC2 test station log (Date: 28/7/2020): Check App version: 15.513.10; Check DUT version: 20200130. 3. Visual inspection: did not find out abnormal. 4. Visual inspection & X-ray U1 did not find out abnormal. 5. Check the power: P5V, P3V3, P1V8, P1V8_EMMC, P1V2, P2V5,VDDCPU and VDDEE did not found abnormal. Suspect Flash (U602), U1 (BGA) components issue. | 1. Write MAC by hand and update correctly FW: 15.513.10 for this device. 2. Re-checked at OBA test station: FAIL Found out can not login Google Issue . 3. Suspect Flash(U602) component issue, replace new eMMC (U602), write Mac by hand and update FW 15.513.10=> FAIL: device still can not login google. - Suspect U1(BGA) component issue, replace new U1, write Mac by hand and update FW 15.513.10. => PASS: Device logins google normally. U1(BGA) component issue. Swapping U1 component to another normal device => Fail - Check console log information no information and boot up failure. 4. SQE sent material for vendor. However, because After two times Fii swapped failure lead to copper pad scrapped, so vendor can not analyze U1(BGA). 5. If the same defect happens in the future, will work with vendor for FA and request the vendor to monitor the issue. | PQE-Hang PE: Loc | 15-Dec | 
2. Can not google login with RCU
FIL1401 FIL1402
U1

## Slide 6
Issue Description | Root Cause | Actions | Owner | Due Date | Status
Phenomenon: SET label print is not completely Type: Major Q’ty : 1/500pcs DR: 0.2% | Root cause: - This is maybe the technical errors. Make print out content text not full, as customer info. Escaped cause : - OP printer label and Op visual inspection don’t careful check print content. | 1. Add NG picture to SOP printer label and visual inspection station. 2. Training OP online by quality Alert issue. 3. Line leader often check and monitor all operators at all stations to make sure their operating comply with SOP. | IE: Huyen PD: Dung IT:Phuc | 01-Sep | 
3. SET label print is not completely
Print label
Check after print
Paste label on housing

## Slide 7
Issue Description | Root Cause | Actions | Owner | Due Date | Status
Phenomenon: Ethernet cable packing NG Type: Major Q’ty : 1/500pcs DR: 0.2% | Vendor root cause: The Ethernet have 2 kind packing method, Normal the cable have to tie maximum is 120 (+-10 ) mm, but the NG Ethernet cable is 150mm. This is cause incoming material have 2 kind mix together in carton box. Escaped cause (at FXN): IQC inspection incoming material follow AQL 0.4 , So no defect this issue. All accessory no test function online, just test OBA follow AQL 0.65. - Online production this is accessory material , packing inside PE bag, no any notice from QA, no reject this issue. | FXN SQE was responsible for inform to vendor this issue, remark this issue on vendor side, Waiting sorting result from vendor. FXN action: - Remark from IQC new coming material inspection this issue, - Showed NG sample and re-trained operator at put accessory station for checking requirement. - Line leader often check and monitor all operators at all stations to make sure their operating co mply wsith SOP. | SQE-Khoa IQC: Long PD:Dung | 22-Aug | 
4. Ethernet cable packing NG