## Slide 1
FOXCONN CPEG JBD_VN
Mar 15, 2023
Report for BFX-AT100 - Dec 2022 Mass Production Inspection

## Slide 2
Establish the Team
Team Leader
Team Member
Foxconn
  MFG Manager : David Yin
  QA Manager : Toney Tu/ CB Lin
PE: Michael, Nam
ME: Cheng Lun, Hugo
PM: An Tran, Yuri
PD: Wen Yong
QA: Ken, Robert
TE: Mark, Jones
IE: Hai Ly, Heng Ruan

## Slide 3
On Feb 23, 2023 ALT customer feedback about Mass Production Inspection for shipment lots in Feb-2023 Detail as below:
Description of Problems
Issue Description

## Slide 4
Failure Analysis Report
1. Foreign object on DC connector
Issue Description | Root cause | Actions | Status
Symptom: No power when fully inserted DC connector. Defect Q’ty : 1/1600pcs Defect rate : 0.06% SN : 2149688001202301025302 | During inspection process, ALT customer detected one unit was no power due to have foreign object inside DC connector, after customer removed foreign object this unit operates normal. Fii check production data: this unit passed all test stations smoothly. Fii check testing tools: head of power cord to insert in DC connector is made from sliver (white color) but the foreign object inside DC connector is yellow color. Maybe foreign object got in DC connector after Fii shipped. | Add NG picture in SOP at VI station and re-train OP to inspect careful at DC connector location. (Done) | Monitor
NG
Foreign object
Fii power cord

## Slide 5
Issue Description | Root cause | Actions | Status
Symptom: LED light leakage when operation Defect Q’ty : 1/1600pcs Defect rate : 0.06% SKB SN: SN :2149688001202301034831 | Occur Root Cause : After ALT customer was opened housing and detected The gasket was missing, ALT Re-attached gasket then assembled again, didn’t find LED light leakage issue. Therefore, it maybe due to operator when assembly forgot attach the gasket. Escape Root Cause : Test program in production line can not cover LED light leakage issue. | Action for occur: Add notice in SOP and Re-train operators, “Must check the gasket was attached well before assembly the top case”. (Done) Action for Escape: Improve test program to enhance test coverage. (Owner : TE/Mark Due date : Mar-30) | On- going
Failure Analysis Report
2. LED light leakage

## Slide 6
Issue Description | Root cause | Actions | Status
Symptom: Physical damage on USB connector area Defect Q’ty : 1/1600pcs Defect rate : 0.06% SN: 2149688001202301024991 | Occur Root Cause : When start the testing process the test fixture will keep the device on test fixture to move to the power ports was fixed on test machine for test. However, operator putted device was misalign with test fixture, (device did not fix full 100% with test fixture due to Op putted misalign). Therefore, when start testing, the power port on test machine will touch with housing at USB connector area due to the device on test fixture was putted misalign by operator, it leads to physical damage on housing at USB connector area. Escape Root Cause : VI operator did not detect this issue. | Action for occur: Add one notice on test program before start testing to remind OP check the device was placed correct on test fixture or not. (Done) Add notice in SOP and Re-train operators, “Must inspect careful at the connector positions”. (Done) | Open
Failure Analysis Report
3. Top housing damaged
OK
NG

## Slide 7
Issue Description | Root cause | Actions | Status
Symptom: Makes a noise sound when the bottom cover is pressed Defect Q’ty : 1/1600pcs Defect rate : 0.06% SKB SN: SN:2149688001202301017824 | During inspection process, ALT customer detected one unit had a noise sound when the bottom cover is pressed. After customer re-assemble bottom cover, didn’t find the noise sound when the bottom cover is pressed again. It maybe due to OP didn’t fix correct 100% when assembling top cover with bottom cover. | Re-train OP and request OP at VI station must press bottom cover whether happen noise sound or not. (Done). | Monitor
Failure Analysis Report
4. Bottom cover noise sound