## Slide 1
Prepared by : PE Long
Date : 2023/10/18
T99X171.00 DOA Product Reboot/ Hang Up
FA Report

## Slide 2
Establish the Team
PE: Michael, Long
ME: Cheng Lun, Hugo
PM: An Tran, Roisy
PD: Wen Yong
QA: Ken, Robert
TE: Allan, Jones
IE: Hai Ly, Heng Ruan
Foxconn
  MFG Director: David Yin
  QA Manager : CB Lin, Toney
Team Leader
Team Member
#1
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 3
Problems description
#2
Issue Description (5W2H) | 
When | 2023/07/27
Who | ALT customer
Where | SK networks warehouse, Anseong, Korea.
What | ALT customer feedback that they found out 1/1000pcs has Reboot/ Hang Up.
Why | Follow SoC material (P/N: 002.02753.005. DC: 2309, Vendor: AMLOGIC)
How | Abnormal reboot after system hangup (Unstable).
How many | 1/1000pcs ( F/R: 0.1%) as table below.
No | Description Issue | S/N | MAC | Fail rate
1 | Abnormal reboot after system hangup. | 2149688001202301146495 | BCF4D4F91707 | 0.1%
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 4
#3
Background Information
On 07/27, T99X171.00 model, ALT customer feedback that they found out 1/1000pcs has hang-up/ reboot.
Defect rate: 1/1000 =1000 DPPM
Fail symptom: NG board hang up/reboot issue
Summary:
Abnormal reboot after system hangup.
Console SW customer
Screen hang-up or reboot
Console SW factory
Notes: 5.26891E-07 4.96855E-07

## Slide 5
System level
1. Recheck production data record.
2. Recheck test log
Dot level
T level
No# | Station | Status
1 | UK | Pass
2 | FT | Pass
3 | FT1 | Pass
4 | RC | Pass
5 | RC1 | Pass
6 | RC2 | Pass
Summary:
- Recheck production data record and test log  Did not find out any abnormal.
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 6
1. Check visual inspection and take X-ray NG sample, result as below:
Board level- 1
Summary:
Don’t find out any abnormality at top/bottom side of NG boards.
Don’t find out process issue such as: Solder short ... on board .
Item | Top side | Bottom side
Visual inspection |  | 
Item | SoC | DDR | eMMC
X-Ray |  |  | 
#5
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 7
Board level- 2
#6
2. SW verification:
Re-update factory image: k000b-523r06_SD_fac-20220118 and check power on
 NG board still auto reboot after booting about 5-20 minutes:
Summary:
Auto reboot still happen on factory image
Because NG board reboot after about 5-20minutes booting (unstable)) then after next is hang up/reboot FATP so can’t cover 100% this issue.
Notes: 5.26891E-07 4.96855E-07

## Slide 8
#7
Summary:
- Because NG board auto reboot after about 5-20minutes booting (unstable) then after next is hang up/reboot so FATP can’t cover this issue.
3. Re-test at FATP
Board level- 3
Retest NG board on FATP |  |  |  |  | 
Station | FT | FT1 | RC | RC1 | RC2
Seconds times | 31s | 120s | 100s | 4s | 4s
Result | PASS | PASS | PASS | PASS | PASS
Notes: 5.26891E-07 4.96855E-07

## Slide 9
Board level- 4
#8
4. Check Vout noise of PCBA NG, result as table below:
Summary:
 Don’t find out abnormal. Vout noise of NG board their value meet the spec
Item | P1V2_Vout Spec (1.14V-1.26V) | P3V3_Vout Spec (3.135-3.465V) | VDDCPU_Vout Spec (0.73V-1.01V) | VDDEE_Vout Spec (0.68V-0.96V) | ETH_DVDD10_Vout Spec (~1.00V)
Compare Vout |  |  |  |  | 
0.86V
3.31V
0.738V
1.20V
1.00V
Item | Y401 | Y801
Compare Crystal |  | 
25Mhz
23.98Mhz
Notes: 5.26891E-07 4.96855E-07

## Slide 10
5. Swap SoC and retest:
- RD Cooper suggest us swap SoC U1 verify:
 Result : This issue follow SoC component.
Board Level- 5
Summary:
- This issue follow SoC (P/N: 002.02753.005, DC: 2309,Vendor: AMLOGIC) material have issue.
#9
Run-in product 10hours + check Power ON/OFF 5times | 1 | 2
OK board + OK SoC | PASS | PASS
NG board + NG SoC | Fail | Fail
OK board + NG SoC | Fail | Fail
NG broad + OK SoC | PASS | PASS
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 11
Conclusion
#10
Root cause:
Occur cause: Follow SoC material (P/N: 002.02753.005. DC: 2309, Vendor: AMLOGIC)
Escape cause: FATP can’t cover this issue
Action:
Recheck data on Y2023 produce q’ty 250000pcs, OBA tested 4195pcs not find out the same issue
PE suggest add run-in and power ON/OFF station on next buid.
Send FA report and NG SoC material to vendor AMLOGIC for futher analyzing. Owner: SQE Naomi.
Due date: 10/21
RD co-work with AMLOGIC taking action for this issue. Owner: RD Cooper. Due date: ASAP
Notes: MA5800-X7#display cable modem <MAC> detail