## Slide 1
Prepared by : PE Long
Date: 2023/11/20
T99X171.00 UI screen broken FA Report

## Slide 2
Establish the Team
PE: Michael, Long
ME: Cheng Lun, Hugo
PM: An Tran, Roisy
PD: Wen Yong
QA: Ken, Robert
TE: Allan, Jones
IE: Hai Ly, Heng Ruan
Foxconn
  MFG Director: David Yin
  QA Manager : CB Lin, Toney
Team Leader
Team Member
#1
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 3
Issue Description ( 5W2H) | 
When | 2023/07/27
Who | ALT customer
Where | SK networks warehouse, Anseong, Korea.
What | ALT customer feedback that they found out 1/1000pcs has UI screen is unstable (broken). Defect rate: 1/1000 = 1000 DPPM
Why | Follow SoC material (P/N: 002.02753.005. DC: 2309, Vendor: AMLOGIC)
How | UI screen is unstable (broken).
How many | Total 1pcs (Defect rate: 1/1000 = 1000 DPPM) as below table.
No | Description Issue | S/N | MAC | Fail rate
1 | UI screen is unstable (broken) | 2149688001202301117565 | BCF4D4F8BF3B | 1000 DPPM
Problems description -1
#2
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 4
Problems description -2
UI screen is unstable (broken).
Summary:
- UI screen is unstable (broken).
#3
Note: Please watching video
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 5
Data checking
1. Recheck production data record.
2. Recheck test log
Dot level
T level
No# | Station | Status
1 | UK | PASS
2 | FT (test HDMI) | PASS
3 | FT1(test HDMI) | PASS
4 | RC | PASS
5 | RC1 | PASS
6 | RC2 | PASS
Summary:
- Recheck production data record and test log  Did not find out any abnormal.
#4
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 6
#5
1. Retest NG sample at OBA station.
OBA + FATP verify
Summary: The fail symptom same as customer feedback.
- Retest NG sample at FT, FT1 station  Pass normally.
 FATP station can’t cover this issue
UI screen is unstable (broken).
2. Upgrade again factory FW and test NG sample at FT, FT1 station, the result as below:
No. | Station | Result
1 | FT | Pass
2 | FT1 | Pass
Screen broken
Note: Please watching video
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 7
1. Check Visual inspection and take X-ray NG sample, result as below:
Board Level -1
Summary:
- Check visual inspection and take X-ray  Result: No abnormality
Item | Top side | Bottom side | Result
Visual inspection |  |  | No abnormality
Item | SoC | eMMC | HDMI Connector | Filter | Result
X-ray |  |  |  |  | No abnormality
#6
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 8
2. Measure impedance /VF on board HDMI connector of NG sample and compare with OK sample, result as table below:
Board Level -2
Summary: Did not find out abnormal with impedance of NG sample
Impedance/VF measurement on board HDMI Connector |  |  |  |  |  | 
Pin No | Pin Name | Description | NG sample |  | OK sample | 
 |  |  | Impedance (Ω) | VF | Impedance (Ω) | VF
1 | TX2+ | HDMI TMDS data2 negative output | 3.21M | 0.683 | 3.2M | 0.68
2 | TX2_shield | System Ground | 0 | 0 | 0 | 0
3 | TX2- | HDMI TMDS data2 positive output | 3.226M | 0.68 | 3.2M | 0.68
4 | TX1+ | HDMI TMDS data1 positive output | 3.224M | 0.68 | 3.2M | 0.68
5 | TX1_shield | System Ground | 0 | 0 | 0 | 0
6 | TX1- | HDMI TMDS data1 negative output | 3.221M | 0.68 | 3.2M | 0.68
7 | TX0+ | HDMI TMDS data0 positive output | 3.220M | 0.68 | 3.2M | 0.68
8 | TX0_shield | System Ground | 0 | 0 | 0 | 0
9 | TX0- | HDMI TMDS data0 negative output | 3.221M | 0.68 | 3.2M | 0.68
10 | TXC+ | HDMI TMDS clock positive output | 3.215M | 0.68 | 3.2M | 0.68
11 | TXC_shield | System Ground | 0 | 0 | 0 | 0
12 | TXC- | HDMI TMDS clock negative output | 3.21M | 0.68 | 3.2M | 0.68
13 | CEC | General purpose input/output bank H signal 3 | 2.4M | 0.69 | 2.2M | 0.69
14 | NC | Not Connect | NA | NA | NA | NA
15 | SCL | General purpose input/output bank H signal 1 | 1.2M | 0.61 | 1.2M | 0.62
16 | SDA | General purpose input/output bank H signal 0 | 1.11M | 0.61 | 1.01M | 0.61
17 | GND | System Ground | 0 | 0 | 0 | 0
18 | 5V | HDMI_PW | 1.12M | 0.50 | 1.2M | 0.55
19 | HPD | General purpose input/output bank H signal 2 | 110K | 0.69 | 110K | 0.69
#7
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 9
3. Change component of HDMI block and retest screen TV. :
- Change new SoC
 Result: Pass 5/5 times. This issue follow SoC component.
Board Level - 3
Summary:
- This issue follow SoC (P/N: 002.02753.005, DC: 2309,Vendor: AMLOGIC) material have issue.
TV screen OK
#8
Note: Please watching video
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 10
1. Removed SoC and measure HDMI block pin, result as table below:
Component level - 1
Summary: Measure impedance/VF HDMI pins of NG SoC  Did not find out any abnormality
SoC-U1 HDMI pin impedance measurement |  |  |  |  | 
SoC_PIN NAME | Description | OK SoC Sample |  | NG SoC sample | 
 |  | Impedance | VF | Impedance | VF
C43 | HDMI TMDS data2 negative output | 8.81MΩ | 0.76 | 8.56MΩ | 0.767
C45 | HDMI TMDS data2 positive output | 8.71MΩ | 0.76 | 8.56MΩ | 0.767
E45 | HDMI TMDS data1 positive output | 8.61MΩ | 0.76 | 8.57MΩ | 0.766
G43 | HDMI TMDS data1 negative output | 8.61MΩ | 0.76 | 8.56MΩ | 0.766
J41 | HDMI TMDS data0 positive output | 8.65MΩ | 0.76 | 8.45MΩ | 0.764
J43 | HDMI TMDS data0 negative output | 8.63MΩ | 0.76 | 8.43MΩ | 0.764
L43 | HDMI TMDS clock positive output | 8.54MΩ | 0.76 | 8.33MΩ | 0.763
L45 | HDMI TMDS clock negative output | 8.64MΩ | 0.76 | 8.33MΩ | 0.763
N41 | General purpose input/output bank H signal 1 | 2.52MΩ | 0.71 | 2.69MΩ | 0.721
N43 | General purpose input/output bank H signal 3 | 2.64MΩ | 0.75 | 2.70MΩ | 0.746
R43 | General purpose input/output bank H signal 0 | 2.49MΩ | 0.71 | 2.655MΩ | 0.724
R45 | General purpose input/output bank H signal 2 | 2.61MΩ | 0.74 | 2.694MΩ | 0.729
AG45 | General purpose input/output bank H signal 4 | 2.91M | 0.78 | 3.182MΩ | 0.788
#9
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 11
#10
2. Reball and do a swap verification SoC
Component level - 2
Summary:
- As analyzed above this issue follow U1-SoC( P/N: 002.2753.005, DC: 2309, Vendor: AMLOGIC ) component.
Check Screen HDMI | 1 | 2
OK board + OK SoC | OK | OK
NG board + NG SoC | NG | NG
OK board + NG SoC | NG | NG
NG broad + OK SoC | OK | OK
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 12
Action
#11
1. RD Jerry and TE Jones have completed the following test verification.
- Use commands to move the selected item in the settings menu to verify this issue.(One per second)
- Use the developed application to optimize item 1 and dynamically adjuset the test frequency. (Dynamically adjust time)
2. The conclusion as below:
- The frequency of this issue does not occur every time.
- It is not in the same location and is dynamically displayed in differnet positions on the screen.
Summary: FATP cannot be checked through software.
Notes: MA5800-X7#display cable modem <MAC> detail

## Slide 13
Corrective Action
#12
Root cause:
- Occur cause: Follow U1 SoC (P/N: 002.02753.005, DC: 2309, Vendor: AMLOGIC) have material issue. - Escape cause: FATP can’t cover issue.
Short term:
Co-work with RD, TE team, how to cover this issue at FATP ,Owner :RD Jerry ,TE Jones. Duedate: 09/28
On 09/27, after verify RD and TE confirm FATP can’t cover issue.
Send FA report and NG SoC material to vendor AMLOGIC for futher analyzing and taking action for this issue. Owner: SQE Naomi. Due date: 20-Nov-2023
Notes: MA5800-X7#display cable modem <MAC> detail