## Slide 1
BlueTool Install and Test Command

## Slide 2: HW Rework
PCB jumper wire Tx、Rx、GND
R1010
(Tx)
R1011
(Rx)
Keep 0ohm of R1010、R1011
Along 0ohm jumper wire

## Slide 3
Important!!!
Must to use USB to TTL module serial converter, and connect Tx、Rx and GND to PCB
GND
Tx(R1010)
Rx(R1011)
Tx
Rx
GND
PCB

## Slide 4: NOTE
If display error message, need to
(1) DUT Reset (power off and then power on again)
(2) Re-plug in USB to TTL dongle
(3) Close BlueTool and open tool again

## Slide 5: A. Install BlueTool
Open Bluetool folder  Install ActivePerl-5.8.4.810-MSWin32-x86
Install BlueTool

## Slide 6
1

## Slide 7: B. Enable Test Mode
Open BlueTool
From the View menu, select Log Window
From the Transport menu, select HCI Control
NOTE！
After power on, need to wait 1 minute
and can start to deliver command

## Slide 8
(1) In Select HCI Control Window Transport, select UART
(2) Key-in COM PORT, the same with device manager
(3) Select baud rate to 115200
(4) Cancel CTS flow control
(5) Click OK
(1)
(2)
(3)
(4)
(5)

## Slide 9: Reset
In the HCI Control Command Window
  Select 7.3 Host Controller & Baseband Command
  In the main body of the window, double-click Reset
  In the log window, the last line reads status = 0x0 (0, "Success")
(1)
(2)
(3)

## Slide 10: Download Firmware
Download Firmware
  From the Transport menu, select Download Firmware
  Device Configuration :
  Import  Select BCM20703A2_Runtime_Ram_Config_Download
(1)
(2)

## Slide 11
2
  (3) Select burn image
  (4) Click Locate  select CYW20704A2_001.002.011.0296.0298.hcd
  Click Execute
  Display Status : Download completed
(3)
(4)
(5)
(6)

## Slide 12
(1) After Load FW  select HCI control window  select HCI protocol active
(2) Click Reset
(3) In the log window, the last line reads status = 0x0 (0, "Success")
(1)
(2)
NOTE！ After complete download firmware, wait at least 40sec,
then click reset
Reset

## Slide 13
Set Event Filter
Success : In the log window, the last line reads status = 0x0 (0, "Success")
Write Scan Enable
  Success : In the log window, the last line reads status = 0x0 (0, "Success")

## Slide 14
Enable Test Mode
Success : In the log window, the last line reads status = 0x0 (0, "Success")

## Slide 15: C. Set Tx Carrier Frequency ARM