## Slide 1
Control Run New Housing(PC mold)
of T99X171.00 Product
Prepare by: ME - Huy
Date: April 24th 2023

## Slide 2
Result : The width, length, height of 9pcs incoming material are in Spec.
New top case ASS'Y 95.05*95.05 (PN: 441.00896.035)
Inside the top case of new housing don’t have sponge, so need to paste sponge (P/N: 484.00300.005) on the housing as old housing (PN: 441.00896.015).
Measure the width, length, height of new housing (PC mold)
Control Run new housing of T99X171 product
P/N |  | Logo | In Housing | Material
441.00896.025 | New mold |  |  | MABS
441.00896.035 | PC mold |  |  | MABS
Top cover Samples | Width 95.05±0.2mm | Length 95.05±0.2mm | Height 25±0.15mm
#1 | 95.06 | 95.00 | 24.96
#2 | 95.11 | 95.02 | 24.93
#3 | 95.03 | 95.02 | 24.98
#4 | 95.13 | 95.08 | 24.96
#5 | 95.08 | 94.96 | 25.04
#6 | 95.09 | 95.11 | 25.02
#7 | 95.11 | 95.07 | 25.05
#8 | 95.12 | 95.06 | 24.93
#9 | 94.98 | 94.98 | 25.01

## Slide 3
Measure the width, length of new housing (New mold)
Bottom cover Samples | Width 90.79±0.2mm | Length 90.79±0.2mm
#1 | 90.80 | 90.86
#2 | 90.75 | 90.81
#3 | 90.75 | 90.74
#4 | 90.78 | 90.77
#5 | 90.84 | 90.82
#6 | 90.81 | 90.84
#7 | 90.83 | 90.82
#8 | 90.79 | 90.85
#9 | 90.81 | 90.80
Bottom case 90.79*90.79*7.49 (PN: 442.00630.015)
P/N |  | Top side | Bottom side | Material
442.00630.015 | New mold |  |  | ABS
Result : The width, length of 9pcs incoming material are in Spec.
Control Run new housing of T99X171 product

## Slide 4
Result : 10pcs are assembled normal. The Gap between bottom case and top case is in Spec.
New top case ASS'Y 95.05*95.05 (PN: 441.00896.035)
Old bottom case ASS'Y 90.79*90.79*7.49 (PN: 442.00630.015)
Measure the gap between bottom case and top case of 10 samples units
Control Run new housing of T99X171 product
Sample | Side 1 | Side 2 | Side 3 | Side 4 | Spec
#1 | 0.1mm | 0.2mm | 0.2mm | 0.1mm | =/<0.4mm
#2 | 0.1mm | 0.2mm | 0.15mm | 0.15mm | 
#3 | 0.15mm | 0.15mm | 0.2mm | 0.1mm | 
#4 | 0.1mm | 0.15mm | 0.15mm | 0.1mm | 
#5 | 0.15mm | 0.2mm | 0.2mm | 0.1mm | 
#6 | 0.15mm | 0.15mm | 0.2mm | 0.15mm | 
#7 | 0.1mm | 0.2mm | 0.15mm | 0.1mm | 
#8 | 0.1mm | 0.15mm | 0.2mm | 0.15mm | 
#9 | 0.15mm | 0.2mm | 0.2mm | 0.1mm | 
#10 | 0.1mm | 0.2mm | 0.15mm | 0.1mm | 
Side 1
Side 3
Side 4
Side 2

## Slide 5
Summary : 10pcs are assembled normal. The gap between housing and connection ports is in Spec.
Measure the gap between top case and connection ports of 10 samples units
Control Run new housing of T99X171 product
Sample | GAP LAN | GAP HDMI | GAP USB | GAP DC | Spec
#1 | 0.25 | 0.2 | 0.2 | 0.25 | 0.5mm
#2 | 0.2 | 0.2 | 0.2 | 0.2 | 
#3 | 0.2 | 0.2 | 0.25 | 0.2 | 
#4 | 0.25 | 0.25 | 0.25 | 0.2 | 
#5 | 0.25 | 0.2 | 0.2 | 0.25 | 
#6 | 0.2 | 0.2 | 0.25 | 0.2 | 
#7 | 0.25 | 0.25 | 0.25 | 0.25 | 
#8 | 0.25 | 0.25 | 0.2 | 0.2 | 
#9 | 0.2 | 0.25 | 0.2 | 0.2 | 
#10 | 0.2 | 0.2 | 0.2 | 0.25 | 
New top case ASS'Y 95.05*95.05 (PN: 441.00896.035)
LAN, HDMI, USB, DC ports

## Slide 6
Result : No found any visual inspection issue..
Visual inspection 100pcs control run on production line.
Control Run new housing of T99X171 product
Model | Visual inspection Q’ty | Pass Q’ty | Failure Q’ty | Result
T99X171 | 100 | 100 | 0 | Pass

## Slide 7
IQC measure the width, length, height of 9pcs of incoming material: Pass
IQC measure the width, length of 9pcs of incoming material: Pass
ME measure the gap between bottom case and top case of 10 samples units: Pass
ME measure the gap between top case and connection ports of 10 samples units: Pass
Visual inspection 100pcs control run on production line: Pass
Result: the control run result is PASS, we can use new housing of NWE.
Conclusion