## Slide 1
T99X171.00 comparison table of different FW CPU Loading
Cooper.Kung
2022.12.20

## Slide 2
T99X171.00 comparison table of different FW CPU Loading(Test condition: 4K Video on local + iperf 50Mbps) | 
1.FW Version: 15.502.13(r13 DVT1) | 1.FW Version: 15.523.06(Remove Shield CAN)
2.Command: vmstat | 2.Command: vmstat
3.CPU Load = 100-id=80% | 3.CPU Load = 100-id=27%
4.Cause of high CPU loading: logcat will continue output error message, It will cause high load on system server | 
5. Summary: 15.502.13(r13 DVT) FW will logcat output error message continuously when Ethernet connected. It will also causes high CPU load and leads to poor thermal test results. | 

## Slide 4: ALT Test result
TestFW : r13 dvt1 (15.502.13) image link , https://drive.google.com/file/d/1RVL-z53myPbXWknuy9KDweLcFAWfF_i8/view?usp=share_link

## Slide 5: ALT Test result
Running Youtube(4K) and iperf3 at the same time

## Slide 6: ALT Test result
The connectivity log is observed every 2 minutes and 11 seconds

## Slide 7: Re-test by Foxconn
TestFW : r13 dvt1 (15.502.13) image link , https://drive.google.com/file/d/1RVL-z53myPbXWknuy9KDweLcFAWfF_i8/view?usp=share_link

## Slide 8: Re-test by Foxconn
Success log in

## Slide 9: Re-test by Foxconn
Running Youtube(4K) and iperf3 at the same time

## Slide 10: Re-test by Foxconn
logcat will continue output error message, It will cause high load on system server(CPU Loading~90%)