## Slide 1: SKB Serial number
By. ALT SH, SON

## Slide 2: 1. SKB Requirement
SKB Serial number(= SKB Asset number) requirement.
This requirement is mandatory for SKB
  SKB first registered SKB serial number in SKB DB and notify this number.
  Manufacture should be followed the SKB Serial number when the production
  Only the registered SKB number can be put on the SKB where house.
  Ex.) PO 1K -> e, Asset number per STB
  : sequential number : 000001~001000

## Slide 3: 2. Manufacturing process flow.
AS IS : FXN Factory Manufacturing process flow
  All serial numbers (FXN, SKB, MAC) are matched.
PCBA process :
use PCBA FXN S/N
Attached Label
With SKB S/N
S/N | MAC | SKB S/N | PCBA S/N
1231231231 | aa:bb:cc:dd:ee | 1231231231231 | Abcdefg
1231231232 | aa:bb:cc:dd:ed | 1231231231232 | abcedfh
Already assigned and matched S/N and Mac and SKB S/N each Lot
(example)
Print SET label
With SKB S/N

## Slide 4: 3. Problems
ALT will notice the each lot serial number range
  example
FXN should be match each lot unit serial number range.
If not matched serial number, will be rejected form SKB.
Currently FNX VN factory MES system is not ready this SKB requirement.
P/O No. | Model | Q'ty(LOT) | Date* | S/N (The start no.) | S/N (The last no.) | S/N Issue date (To FXN)
ALT190320‐STB | BFX-AT100 | 1,000 | Jun 19th, 2019 | 2149688001201904000001 | 2149688001201904001000 | Apr 25th, 2019
 | BFX-AT100 | 9,000 | Jul 26th 2019 | 2149688001201904001001 | 2149688001201904010000 | Apr 25th, 2019
 | BFX-AT100 | 10,000 | Aug 26th 2019 | 2149688001201904010001 | 2149688001201904020000 | Apr 25th, 2019
P/O Total |  | 20,000 |  |  |  | 

## Slide 5: 4. Suggest Manufacturing process flow
All production proceed based on FXN number
FXN SET serial number should be no effect Google CTS requirements.
Add the customer material at BOM “SKB S/N barcode”. And include this item at gift packing station.
When gift packing station, upload SKB S/N by barcode scanner and matched each packed FXN S/N
Find a way to be meet the SKB requirement on FXN MES System

## Slide 6: 5. Reference
Other process
Label station
Print the SKB S/N label
This number will be noticed by ALT
SMT
DIP
UK
PT
Assembly
FT
Burning
Production - OEM S/N with temporary label
- MES db example
SKB Temp Label
Customer material, (temporary use)
S/N | MAC | SKB S/N | PCBA S/N
1231231231 | aa:bb:cc:dd:ee |  | Abcdefg
1231231232 | aa:bb:cc:dd:ed |  | abcedfh
Print the SKB Label
. Other SKB Manufacture manufacturing flow

## Slide 7: 5. Reference
Gift packing
Carton packing
Pallet packing
OBA Test
- MES db example
Upload SKB S/N. paring FXN S/N with SKB S/N
Print the SET and Gift label
SKB S/N
S/N | MAC | SKB S/N | PCBA S/N
1231231231 | aa:bb:cc:dd:ee | ~~~20190001 | Abcdefg
1231231232 | aa:bb:cc:dd:ed | ~~~20190002 | abcedfh
Production - OEM S/N
. Other SKB Manufacture manufacturing flow
SKB Temp Label
Customer material,
(temporary use)
SCAN OEM S/N
SCAN SKB S/N
Print SET Label
Attached SET Label
Print Gift Label
Gift packing with attached label
SKB temp label scrap. no more use in production line.
Paring OEM and SKB S/N. Print DEVICE LABEL

## Slide 8: 5. Reference
Gift packing
Carton packing
Repair
OBA Test
SKB Temp Label
Upload SKB S/N. paring OEM S/N with SKB S/N
Print the SET and Gift label
In case of NG OBA Test
- MES db example
S/N | MAC | SKB S/N | PCBA S/N
1231231231 | aa:bb:cc:dd:ee |  | Abcdefg
1231231232 | aa:bb:cc:dd:ed | ~~~20190002 | abcedfh
Test NG
STB
SKB S/N
Remove SET Label.
And unpairing OEM S/N with SKB S/N from db
Use unpaired SKB S/N
Production - OEM S/N
. Other SKB Manufacture manufacturing flow
Attached the OEM S/N label
SKB Temp Label Print

## Slide 9
EOD