## Slide 1
Before error occurred  when an error occurs
Initial CEC data : Error observed
Overview
This is the process of ping from Play1 (STB) to Audio.
In this case, EOM (End Of Message) bit (=0),
An incorrect protocol is generated.
An abnormal waveform is estimated to occur in the CEC Bus
due to the ping(incorrect protocol) reception
Logical Address Discover from Play1 (STB) to Ping. At this time, it is EOM (End of Message) bit (=1), This bit is satisfied with the specifications.
CEC Bus 에 Abnormal
파형 발생
EOM(=1)
Initiator (=STB, 0x4)
Follower (=STB, 0x4)
Content (=Ping)
EOM(=0)
Initiator (=STB, 0x4)
Follower (=Audio, 0x5)
Content (=Ping)
First ping
<Issue Condition> CEC communication waveform when TV Off state STB alone is on
→ ① CEC Bus Error occurred
② CEC CMD transmission delayed for tens of seconds due to Bus Error

## Slide 2
에러 발생 직전  에러 발생 시
초기 구간 CEC 데이터 : 에러 발생
Overview
Play1 (STB) 에서 Audio 로 Ping 하는 과정이다.
이 때는 EOM (End Of Message) bit (=0) 으로,
올바르지 않은 프로토콜을 발생시킨다.
해당 (비규격 프로토콜) Ping 수신에 의하여 CEC Bus 에 비정상적인 Bus Timing Error 를 유발하는 파형이 발생하는 것으로 추정됨
Play1 (STB) 에서 Ping 으로 Logical Address Discover 하는 과정.
이 때는 EOM (End Of Message) bit (=1) 로,
규격에 부합한다.
CEC Bus 에 Abnormal
파형 발생
EOM(=1)
Initiator (=STB, 0x4)
Follower (=STB, 0x4)
Content (=Ping)
EOM(=0)
Initiator (=STB, 0x4)
Follower (=Audio, 0x5)
Content (=Ping)
최초 Ping 동작 시
<불량 재현 조건> TV Off 상태 STB 단독 On 시의 CEC 통신 파형
→ ① CEC Bus Error 발생함
② Bus Error 에 의하여 대부분의 유의미한 CEC CMD 전송이 수십초간 딜레이 됨