## Slide 1
LED and Button Scenario for BFX-AT100
ALT
2019. 2. 26

## Slide 2
Rivision History
Revision No. | Release Date | Description
0.1 | 2019/1/23 | First Release
0.2 | 2019/2/26 | Change LED Scenario

## Slide 3
Button Scenario
Short Press time duration : less than 3 secs. Long Press time duration : more than 3 secs.
Press duration | Buttons | Action | Android Key Event
Short Press | ∧ | Channel Up | KEYCODE_CHANNEL_UP
 | ∨ | Channel Down | KEYCODE_CHANNEL_DOWN
Long Press | ∧ | Display Pairing Screen of OKSSU/Btv Plus App | KEYCODE_SKB_FUNC_19
 | ∨ | Find RCU function Run | KEYCODE_SKB_FUNC_18
 | Power ON +∧+∨ | Start Emergency update | Start to run OTA in bootloader
Emergency update : User turn on power while user press two buttons simulateous, then Bootloader runs OTA function. It is for C/S, not for user.

## Slide 4
LED Scenario
STB Status | LED Color | Blanking
During the boot | Green | 
During Voice Recognition | Green blinking | 
Normal operation | Blue always on | 
During RCU Pairing | Blue blinking | 
Active Standby mode | Red always on | 
When there is network problems | Red blinking | 
STB Status | LED Color | Comments
Power off | Off | 
Check STB | White blinking | During Boot
Running STB Service script | White blinking | 
STB Home(After UI Poster ~) / Watching | Normal Network : White blinking Network abnormal : Orange blinking | 
STB Sleep | Green | 
RCU Key reception | White blink once |