## Slide 1: SKB ATV Development Guide for Foxconn (v1.0)
Form TVSTORM
(2019.1.15)

## Slide 2: HW control API Guide
1
HAL library for controlling Front LED and MIC
  Front LED control
    1 RGB LED
    Operation: set status(off/on/blink), change color(red/blue/green)
    Ex) SetLedState (int id, int state);
    SetLedColor (int id, int color);
  MIC control
    Operation: set status(on/off), get/set mic input volume and echo level(0~100)
    Ex) SetMicOnOff(bool onoff);
    GetMicVolume();
    SetMicVolume(int vol);
    GetMicEchoLevel();
    SetMicEchoLevel(int echo);
HAL Guide Documents
  TVS-ANDROID-TVP-DOC-002_TVSystemService HAL Porting.docx
    HAL porting guide document
  TVSystemService_HAL_template.tar.gz
    HAL skeleton code
  TVSystemService_jnidoc.tar.gz
    HAL API jnidoc

## Slide 3: HDCP on/off and version setup (for debug)
2
Forced HDCP off (for debug)
  Function for debugging
  If “data/btv_home/moded” file is present, should set HDCP off
Configuration of each version of HDCP
  Debugging and functionality for specific users
  hdcp 2.x mode is set as default
  Automatically set to 1.x or 2.x depending on the hdcp mode supported by the connected TV
  "/data/btv_home/hdcp_version_1x“: if the file exists, it works as hdcp 1.x
    - Even if the connected TV is supported by hdcp2.x, STB side is set to hdcp1.x

## Slide 4: Auto Reset Guide
3
Ability to cold boot the STB without knowing the user in a specific situation (decided by App)
The TV screen should not come out from the bootloader, the TV should not be turned on by CEC control. STB must be in standby mode when booting is completed.
Operation
  App issues the reboot command
    “system_reset” command is inserted in reboot command as below
    reboot system_reset
  The Boot loader from manufacturer checks “system_reset”
    If it is confirmed to be an auto reset, do not display the TV screen from the bootloader.
    Set "sys.skb.auto_reset" to true in the System property when amlogic driver is loading.
  Middleware checks sys.skb.auto_reset to disable cec.
  UI App checks sys.skb.auto_reset property to switch STB to standby mode, and initializes sys.skb.auto_reset value

## Slide 5: Console enable (for debug)
4
Console enable feature
  Enables console for debugging in User mode
  The manufacturer enables console if system property "persist.sys.console.enable" is "SK8r0@d8@nd"

## Slide 6: Key (for SKB special feature key)
5
Start recovery mode
  Pressing the channel up and down key at the same time on front panel makes to enter into the recovery mode during STB cold booting.
RCU info key
  STB power, TV power, RCU Info key is transmitted when the integrated power key is input
  If linux scancode in KEYCODE_MANNER_MODE is transmitted according to the RCU, middleware transforms and obtains the maker and version of RCU (* save as system property: dev.rcu.manu, dev.rcu.ver)
  If new RCU which has new button(s) is added, manufacturer has to apply new keys.
SKB key list
    Refer to the “RCU Info” sheet which was already sent to ALT. (SKB_ATV_STB_Key_Code_20181016_v2.8.xlsx)
KeyEvent Name will be changed/updated
  KEYCODE_BUTTON_0~A, KEYCODE_F1~F12, some SKB special feature keys assigned to KEYCODE_MANNER_MODE will be newly added and replaced