## Slide 1
2019.09.19
㈜HM Solution
STB ATT Communication Protocol(Ver7.2)

## Slide 2
[Revion History]
Ver. | Date | Page | Revision Contents
V7.0 |  |  | 
V7.1 | 2019-07-29 | p23 | ㆍ 2.4.8 COMPLETE : Define meaning of items of Result
 |  | p27, p28 | ㆍ 3.2 STB Information communication Protocol : Add “Test Url sample in Web Browser”
V7.2 | 2019-09-19 | P8 | ㆍ 2.2 Scenario for sending/receiving Information – 4/4
 |  | p15 | ㆍ 2.4.2 COMMAND 2/2
 |  | p32 | ㆍ 4.3 Major issues

## Slide 3
STB ATT program is installed on PC for aging test. And STB Deamon is installed on each STBs for test. STB and Aging PC should be able to configure the network environment and connect to each other so that they can access.
STB ATT controls and monitors STBs through STB Deamon via network.
1. System Configuration of STB ATT
1.1 STB Deamon
· · ·
[STB #1]
[STB #n]
STB Deamon
STB ATT Program
[Aging PC]
ATT Server
Send Mac, IP and
Step information
Receive STB IP and
Step information
via MAC
Command
Report results
of command
and Status
information
STB deamon is installed on each STBs
STB ATT Program is installed on Aging PC

## Slide 4
Install using USB
and STB turns On
Start option and authentication information
The STB daemon is started when the STB is booted, and when the STB obtains the IP, it sends the information to the server and waits until the STB ATT program is connected.
The STB status information is transmitted when STB ATT program is connected periodically or when an event occurs. The command is executed when it is received.
2. STB Deamon communication scenario
2.1 STB Deamon
Revoke authentication and Unlock Parental control.
Prohibit auto-upgrade,
Setup dynamic IP,
Check SDCard/USB
Reboot
Connect Management Server
(MAC, IP, Step Flag(1))
Receive setting information
Authentication and send result
Test STB button and IR reception
Realtime broadcast/VoD
Revoke Authentication
Reboot/Factory Default
END
Connect Management Sever
(MAC, IP, Step Flag(2))
Connect Management Sever
(MAC, IP, Step Flag(3))
Check ATT STB program and Delete it in STB.
Check Deamon deletetion
It should be deleted deamon that it installed before 24 hours ago.(It is for prevention that it runs in customer house)
Update channels
Reboot
It may change how to install demon.
* After completing each step, it is necessary to modify the step information based on reboot status.

## Slide 5
2.2 Scenarion for sending/receiving Information – 1/4
STB ATT Program
STB Deamon
Management
Server
Connect USB
2. STB Deamon communication Scenario
STB On
(Install Deamon)
Ready to Test
Mac, IP,
Authetication, Step(1)
Ack
Request IP & Ver. Inform. using MAC as a key
Ack(IP, Update Date, Authentication)
Create STB IP Inform.
Connect TCP socket(Port : 10000)
Connect Socket
Send Monitoring option
Option
Refer to 3.2
It should include whether Patch run and reboot or not
#It should run the following functions itself when STB deamon starts#
1. Revoke Authentication : Reboot
2. Unlock Parental control
3. Prohibit auto upgrade
4. Set Dynamic IP
5. Check SDCard/USB

## Slide 6
2. STB Deamon communication Scenario
STB Inform.(Device, Ver. Inform.)
Ack
Authentication result(True, False)
Ack
STB Authen.
STB Infrom.
Authentication
Channel Update command(RCU Scenario)
Update channels
2.2 Scenarion for sending/receiving Information – 2/4
STB ATT Program
STB Deamon
Management
Server

## Slide 7
2. STB Deamon communication Scenario
Start VoD Service(VoD code)
Check VoD
Broadcast
Change realtime broadcast channel(Channel)
Check realtime Broadcast
·
·
·
Realtime / VoD service aging test according to broadcast aging schedule
Reboot
Mac, IP,
Authentication,
Step(2)
Ack
Create STB IP Inform.
Refer to 3.2
Start Button test
Test
Button/
RCU
Send button click / RCU Code
Stop button test
…
2.2 Scenarion for sending/receiving Information – 3/4
STB ATT Program
STB Deamon
Management
Server
Request IP using MAC as a key
Ack(IP, Update Date, Authentication)

## Slide 8
2. STB Deamon communication Scenario
Connect TCP socket
Connect Socket
Mac, IP, Authentication,
Step(3)
Ack
Create STB IP Inform.
Refer to 3.2
Revoke Authentication(Manager code)
Revoke Authentication
Reboot
Result of revoke authentication(True, False)
Ack
Complete message(TRUE or FALSE)
Complete Process
Delete command of Program(CMD-EXIT)
Factory Reset
(Delete Daemon)
2.2 Scenarion for sending/receiving Information – 4/4
STB ATT Program
STB Deamon
Management
Server
Request IP and ver. Inform. using MAC as a key
Ack(IP, Update Date, Authentication)
Reboot

## Slide 9
2.3 Concept of STB Deamon communication Protocol
The communication protocol defines the TCP / IP socket communication rule between the STB ATT program and the STB daemon.
Basically, the communication protocol configuration is consist a header and a data area. The header can have several fields. The each field is separated by <CR> <LF>. The header and data area are separated by empty line that field has only <CR> <LF>.
There are several fields in the header, and each field is separated by <CR> <LF>. The length of the header is not defined specifically, but is recognized as a header area until an empty line with <CR> <LF>, and the rest of it is recognized as a data area. Some commands can communicate using only header without data area. The length of data area is defined in header. So data can be read as long as the length of data is. Data for communication uses only text, so there is always NULL (0x00) as the last part of data. You can check where is the last part of data even if you don’t check the data length in the header. <NULL> doesn’t include the length of data.
<CR> means 0x0D.
<LF> means 0x0A.
<NULL> means 0x00.
Header
Data
<CR><LF>
<NULL>
MSG-KIND:STATUS<CR><LF>
DATA-LENGTH:4<CR><LF>
test
<CR><LF>
<NULL>
[Example]
2. STB Deamon communication Scenario

## Slide 10
2.3.1 Communication Protocol Type 1/2
Direction | MSG-KIND | Contents | Header/Data
PC->STB | OPTION | Image types(jpg or bmp) Image resolution도(640 * 480 등) Image transfer interval(Sec.) | Data : IMAGE-KIND:JPG<CR><LF> IMAGE-RESOLUTION:640-480<CR><LF> IMAGE-CYCLE:1<CR><LF> CITIZEN-NUMBER:1234567<CR><LF> LOGIN-NUMBER:1234567<CR><LF> MANAGER-CODE:92393484884<CR><LF> PARTIAL-PATCH:1<CR><LF>
 | COMMAND (Add “COMMAND-KIND” in header) | User control | Header : COMMAND-KIND:USER-CONTROL Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Channel update | Header : COMMAND-KIND:CHANNEL-UPDATE Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Partial Patch | Header : COMMAND-KIND:PARTIAL-PATCH Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Change realtime broadcast channels | Header : COMMAND-KIND:CHANNEL Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Start VoD Service | Header : COMMAND-KIND:VOD Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Stop VoD Service | Header : COMMAND-KIND:VOD-STOP Data : RCU control scenario is in there 1C,1000<CR><LF> 20,500<CR><LF>
 |  | Revoke Authentication | Head : COMMAND-KIND:LOGOUT Data : N/A
 |  | Start Test of Button/RCU | Head : COMMAND-KIND:HW-TEST-START Data : N/A
 |  | Stop Test of Button/RCU | Head : COMMAND-KIND:HW-TEST-STOP Data : N/A
 |  | Terminate STB deamon | Head : COMMAND-KIND:EXIT Data : N/A
2. STB Deamon communication Scenario
*Deleted content is not used by the daemon, but is delivered as part of the protocol.
2.3 Concept of STB Deamon communication Protocol

## Slide 11
Direction | MSG-KIND | Contents | Header/Data
STB->PC | STATUS | Video Time Stamp, Audio Time Stamp, Type of played video, error code, etc… | Data : VIDEO-TSTAMP:12321321 AUDIO-TSTAMP:3243324 VIDEO-KIND:2 ERROR-CODE;0 etc….
 | INFO | Version Information Device information | SW-UPDATE-DATE:2012-02-12 CHANNEL-VER:3.4 CHANNEL-UPDATE-DATE:2012-01-12 HDD:30,21.23
 | LOGIN | Complete message of authentication | TRUE or FALSE
 | LOGOUT | Complete message of revoke authentication | TRUE or FALSE
 | REBOOT | Reboot message | 2 or 3
 | IMAGE | Captured Image | Image BINARY
 | HW-TEST-BUTTON | STB Button test | ##RCU Code#### Send one of the following codesCODE:01 // 전원 CODE:0A // 채널 Up CODE:0B // 채널 Down CODE:0C // 볼륜 Up CODE:0D // 볼륨 Down
 |  | RCU Button test | ##RCU Code#### Send one of the following codes CODE:09 // MUTE
 | COMPLETE | Complete message | TRUE or FALSE
Common | ACK | Reception | 
2. STB Deamon communication Scenario
2.3.1 Communication Protocol Type 2/2
2.3 Concept of STB Deamon communication Protocol

## Slide 12
MSG-KIND is an option that the STB ATT program sends to STB daemon after TCP connections. The STB daemon uses that information to decide the image generation cycle and format. It also includes additional information needed for STB daemon to execute functions within the STB.
Information | Data type | Data
Image Type | IMAGE-KIND | JPEG or BMP
Image Resolution | IMAGE-RESOLUTION | ORIGINAL or 640-480
Image transfer Interval | IMAGE-CYCLE | Seconds(1 or 2 or ….)
Resident registration number | CITIZEN-NUMBER | Resident registration number for authentication(070718)
Authentication number | LOGIN-NUMBER | Number for authentication (100601010123)
Manager code | MANAGER-CODE | Code for revoke authentication (1239)
Partial Patch execution or not | PARTIAL-PATCH | 0 or 1(1 means patch execution)
Partial Patch 후 STB 데몬의 재부팅 수행 여부 | PATCH-REBOOT-FLAG | 0 or 1(1 means that deamon executes reboot)
Latest S/W version | LATEST-SW-VER | Version(3.2.5)
Latest Partial version | LATEST-PARTIAL-VER | Version(3.2.6)
Items | Contents
Direction of transmission | PC -> STB
Transmission time | Once after TCP connection between STB ATT program and STB deamon
Transmission Interval | Once (for the first time)
2.4.1 OPTION 1/2
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol
There is no Partial Patch policy any more. So above items are not used, but protocol is in it.
Use for STATUS
transmission Interval

## Slide 13
MSG-KIND:OPTION<CR><LF>
DATA-LENGTH:?<CR><LF>
IMAGE-KIND:JPG<CR><LF>
IMAGE-RESOLUTION:640-480<CR><LF>
IMAGE-CYCLE:1<CR><LF>
CITIZEN-NUMBER:1234567<CR><LF>
LOGIN-NUMBER:1234567<CR><LF>
MANAGER-CODE:92393484884<CR><LF>
PARTIAL-PATCH:1<CR><LF>
PATCH-REBOOT-FLA:1<CR><LF>
LATEST-SW-VER:1.1.1<CR><LF>
LATEST-PARTIAL-VER:1.0.0<CR><LF>
<CR><LF>
<NULL>
[Example for OPTION transport packet]
2.4.1 OPTION 2/2
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 14
MSG-KIND is the command that the STB ATT program ask STB deamon to execute its function. When using this syntax, the "COMMAND-KIND" entry should be added in the header.
Information | Data type | Data
User Control | USER-CONTROL | It contains RCU control scenario to execute these commands. 1C,1000<CR><LF> 20,500<CR><LF> 21,500<CR><LF> 22,500<CR><LF> 23,500<CR><LF> 12,500<CR><LF>
Channel Update | CHANNEL-UPDATE | 
Partial Patch | PARTIAL-PATCH | 
Realtime broadcast channel change | CHANNEL | 
Start VoD Service | VOD | 
Stop VoD Service | VOD-STOP | 
Revoke Authentication | LOGOUT | N/A
Start Button/RCU Test | HW-TEST-START | N/A
Stop Button/RCU Test | HW-TEST-STOP | N/A
Terminate STB Deamon | EXIT | N/A
MSG-KIND:COMMAND<CR><LF>
COMMAND-KIND:LOGOUT<CR><LF>
DATA-LENGTH:0<CR><LF>
<CR><LF>
<NULL>
[Example for config. of LOGOUT command transport packet]
Items | Contents
Direction of transmission | PC -> STB
Transmission time | When the STB ATT program decide that each STEP is the start point.
Transmission Interval | Once for each command
2.4.2 COMMAND 1/2
2. STB Deamon communication Scenario
MSG-KIND:COMMAND<CR><LF>
COMMAND-KIND:EXIT<CR><LF>
DATA-LENGTH:0<CR><LF>
<CR><LF>
<NULL>
[Example for config. of EXIT command transport packet]
2.4 STB Deamon Communication Detail Protocol

## Slide 15
For user control, channel update, partial patch, realtime broadcast and VoD broadcast, and VoD stop, IR control scenarios of the customer are transmitted in the data area.
MSG-KIND:COMMAND<CR><LF>
COMMAND-KIND:VOD<CR><LF>
DATA-LENGTH:123<CR><LF>
1C,1000<CR><LF>
20,500<CR><LF>
21,500<CR><LF>
22,500<CR><LF>
23,500<CR><LF>
12,500<CR><LF>
<CR><LF>
<NULL>
[Example of VOD command transport packet config.]
2.4.2 COMMAND 2/2
2. STB Deamon communication Scenario
#define HWM_KEY_POWER 0x0001
#define HWM_KEY_HOME 0x0002
#define HWM_KEY_TUNER 0x0003
#define HWM_KEY_MENU 0x0004
#define HWM_KEY_HISTORY 0x0005
#define HWM_KEY_CANCEL 0x0006
#define HWM_KEY_LOCK 0x0007
#define HWM_KEY_BREAK 0x0008
#define HWM_KEY_MUTE 0x0009
#define HWM_KEY_CHUP 0x000A
#define HWM_KEY_CHDOWN 0x000B
#define HWM_KEY_VOLUP 0x000C
#define HWM_KEY_VOLDOWN 0x000D
#define HWM_KEY_UP 0x000E
#define HWM_KEY_DOWN 0x000F
#define HWM_KEY_RIGHT 0x0010
#define HWM_KEY_LEFT 0x0011
#define HWM_KEY_ENTER 0x0012
#define HWM_KEY_PLAY 0x0013
#define HWM_KEY_STOP 0x0014
#define HWM_KEY_FASTFORWARD 0x0015
#define HWM_KEY_REWIND 0x0016
#define HWM_KEY_PAUSE 0x0017
#define HWM_KEY_FORWARD_SKIP 0x0018
#define HWM_KEY_BACKWARD_SKIP 0x0019
#define HWM_KEY_RESERVATION 0x001A
#define HWM_KEY_RECORD 0x001B
#define HWM_KEY_SEARCH 0x001C
#define HWM_KEY_CAPTION 0x001D
#define HWM_KEY_ADDITIONAL_SERVICE 0x001E
#define HWM_KEY_JOY 0x001F
#define HWM_KEY_0 0x0020
#define HWM_KEY_1 0x0021
#define HWM_KEY_2 0x0022
#define HWM_KEY_3 0x0023
#define HWM_KEY_4 0x0024
#define HWM_KEY_5 0x0025
#define HWM_KEY_6 0x0026
#define HWM_KEY_7 0x0027
#define HWM_KEY_8 0x0028
#define HWM_KEY_9 0x0029
#define HWM_KEY_POUND 0x002B
#define HWM_KEY_COLOR_RED 0x0031
#define HWM_KEY_COLOR_GREEN 0x0032
#define HWM_KEY_COLOR_YELLOW 0x0033
#define HWM_KEY_COLOR_BLUE 0x0034
Click the Search button and wait for 1000 ms.
Click 0 and wait for 500 ms
Click 1 and wait for 500 ms
Click 2 and wait for 500 ms
Click 3 and wait for 500 ms
Click the OK(Enter) button and wait for 500ms
2.4 STB Deamon Communication Detail Protocol

## Slide 16
STATUS information is STB status information that STB daemon sent to STB ATT program regularly (optional). It send only during realtime and VoD aging test
Information | Data type | Data
Video Timestamp | VIDEO-PTS | 23123123
Audio Timestamp | AUDIO-PTS | 33124234
Current Video Type | VIDEO-KIND | 0 : None, 1 : Realtime Broadcast, 2 : VoD, 3 : ADV
Error code | ERROR-CODE | STB error status checked by STB daemon (requires definition of error type and code) E0000(OK),E0001, E0002…
The others |  | It may be added
MSG-KIND:STATUS<CR><LF>
DATA-LENGTH:231<CR><LF>
VIDEO-PTS:1234123<CR><LF>
AUDIO-PTS:1234112<CR><LF>
VIDEO-KIND:2<CR><LF>
ERROR-CODE:E0000<CR><LF>
<CR><LF>
<NULL>
[Example for configuration of STATUS Transport Packet]
Items | Contents
Direction of transmission | STB -> PC
Transmission time | At the start of realtime and VoD Aging test.
Transmission Interval | Periodic(using the transmission interval of OPTION): It will be set to 1 sec.
2.4.3 STATUS
**In case of smart STB, if the Audio PTS is not available, insert and use the Video PTS value into the Audio PTS.
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 17
STB daemon sends information to the STB ATT program about STB device information and whether measurement readiness is enabled.
Information | Data type | Data
S/W last update date | SW-UPDATE-DATE | 2012-02-12
Channel version | CHANNEL-VER | 3.4
Channel last update date | CHANNEL-UPDATE-DATE | 2012-01-12
Total/Available capacity(G) | HDD | 30,21.23(Gigabytes)
Self-authentication revocation status | SETUP-LOGOUT | TRUE or FALSE
Unlock Self-parental control | SETUP-CHILDREN-LIMIT | TRUE or FALSE
Set Self-auto upgrade prohibit | SETUP-AUTOUPGRADE-PROHIBITION | TRUE or FALSE
Set Self-Dynamic IP | SETUP-DHCP | TRUE or FALSE
Is SDCARD inserted ? | SDCARD | TRUE or FALSE
Is USB inserted ? | USB | TRUE or FALSE
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Once after TCP connection between STB ATT program and STB deamon
Transmission Interval | Once
2.4.3 INFO 1/2
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 18
MSG-KIND:INFO<CR><LF>
DATA-LENGTH:156<CR><LF>
STB-MODEL:TD910H<CR><LF>
SW-VER:2.4<CR><LF>
SW-UPDATE-DATE:2012-02-12<CR><LF>
CHANNEL-VER:3.4<CR><LF>
CHANNEL-UPDATE-DATE:2012-01-12<CR><LF>
HDD:30,21.23<CR><LF>
SETUP-LOGOUT:TRUE<CR><LF>
SETUP-CHILDREN-LIMIT:FALSE<CR><LF>
SETUP-AUTOUPGRADE-PROHIBITION:TRUE<CR><LF>
SETUP-DHCP:TRUE<CR><LF>
SDCARD:TRUE<CR><LF>
USB:TRUE<CR><LF>
<CR><LF>
<NULL>
[Example for configuration of INFO transport packet]
2.4.3 INFO 2/2
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 19
STB daemon sends an authentication complete message to the STB ATT program.
Information | Data type | Data
Authentication success ? | RESULT | TRUE or FALSE
MSG-KIND:LOGIN<CR><LF>
DATA-LENGTH:13<CR><LF>
RESULT:TRUE<CR><LF>
<CR><LF>
<NULL>
[Example for configuration of LOGIN transport packet]
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Once after authentication complete
Transmission Interval | Once
2.4.4 LOGIN
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 20
STB daemon sends authentication revoke message to the STB ATT program.
Information | Data type | Data
Authentication revoke success ? | RESULT | TRUE or FALSE
MSG-KIND:LOGOUT<CR><LF>
DATA-LENGTH:13<CR><LF>
RESULT:TRUE<CR><LF>
<CR><LF>
<NULL>
[Example for configuration of LOGOUT transport packet]
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Once after authentication revoke complete
Transmission Interval | Once
2.4.5 LOGOUT
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol

## Slide 21
If a reboot is required, the STB daemon informs the STB ATT program which step of reboot is in.
Information | Data type | Data
Reboot step | REBOOT-STEP | 2 or 3
MSG-KIND:REBOOT<CR><LF>
DATA-LENGTH:15<CR><LF>
REBOOT-STEP:2<CR><LF>
<CR><LF>
<NULL>
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Once before reboot
Transmission Interval | Totally twice
2.4.6 REBOOT
2. STB Deamon communication Scenario
2.4 STB Deamon Communication Detail Protocol
[Example for configuration of REBOOT transport packet]

## Slide 22
STB daemon captures video periodically after authentication and delivers captured image using STB ATT program.
Information | Data type | Data
Captured Image | N/A | 
Items | Contents
Direction of transmission | STB -> PC
Transmission time | After the authentication is success, periodical(optional) from the video play start time to the authentication revoke time.
Transmission Interval | Periodic(using Transmission interval of OPTION) : Expect 2 sec.
MSG-KIND:IMAGE<CR><LF>
DATA-LENGTH:20480<CR><LF>
DLKFJOWEIR230RUWEFKLSDFJ23R9FJSDJFDKFJS;DFJSDF;SDFJK;J;SDFJ;SDJFWEOIFJS;DKFJ;SDFJ;SDJF;SDFJWEJF;JSDFJKSD;JKFJ;SDF;KFJ;SDFJKLDFDDFSSDFSD
<CR><LF>
<NULL>
2.4.7 IMAGE
2. STB Deamon communication Scenario
[Example for configuration of IMAGE transport packet]
2.4 STB Deamon Communication Detail Protocol

## Slide 23
After last reboot, STB daemon sends complete message when it connects to STB ATT program
Information | Data type | Data
Success ? | RESULT | TRUE or FALSE TRUE : Success to revoke authenticaiton FALSE : Fail to revoke authentication
MSG-KIND:COMPLETE<CR><LF>
DATA-LENGTH:13<CR><LF>
RESULT:TRUE<CR><LF>
<CR><LF>
<NULL>
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Once after last reboot
Transmission Interval | Once
2.4.8 COMPLETE
2. STB Deamon communication Scenario
[Example for configuration of COMPLETE transport packet]
2.4 STB Deamon Communication Detail Protocol

## Slide 24
STB deamon sends HW TEST Button message when the STB deamon receives a STB Button or RCU signal in HW Test step.
Information | Data type | Data
Detected signal code | CODE | 01 // Power 0A // Channel Up 0B // Channel Down 0C // Volume Up 0D // Volume Down 09 // MUTE
MSG-KIND: HW-TEST-BUTTON<CR><LF>
DATA-LENGTH:9<CR><LF>
CODE:0C<CR><LF>
<CR><LF>
<NULL>
Items | Contents
Direction of transmission | STB -> PC
Transmission time | Send the received code immediately when STB button or RCU signal is detected in HW-TEST STEP(Button/RCU Test)
Transmission Interval | Once
2.4.9 HW-TEST-BUTTON
MSG-KIND: HW-TEST-BUTTON<CR><LF>
DATA-LENGTH:9<CR><LF>
CODE:09<CR><LF>
<CR><LF>
<NULL>
When STB detects Volume up button in STB button
When STB detects MUTE button signal in
2. STB Deamon communication Scenario
[Example for configuration of
HW-TEST-BUTTON transport packet (Button)]
2.4 STB Deamon Communication Detail Protocol
[Example for configuration of
HW-TEST-BUTTON transport packet (RCU)]

## Slide 25
ACK is sent to confirm that the message was received correctly when it was sent and received by the STB ATT program or STB Deamon
Items | Contents
Direction of transmission | PC -> STB deamon
Transmission time | As soon as message is received
Transmission Interval | Once
They type of MSG-KIND that should send a response
INFO
LOGIN, LOGOUT
MSG-KIND:ACK<CR><LF>
DATA-LENGTH:0<CR><LF>
<CR><LF>
<NULL>
2.4.10 ACK
* No ACK sent by STB deamon to STB ATT program
2. STB Deamon communication Scenario
[Example for configuration of ACK transport packet]
2.4 STB Deamon Communication Detail Protocol

## Slide 26
3.1 Management Server communication Overview
STB daemon reports IP and authentication status of STB to the management server when STB is booting for IP Information Management of the STB.
The STB ATT program uses MAC information from STB inputted by the administrator to obtain STB IP information from the management server for network access to STB.
Mac, IP,
Authentication,
Step
Ack
Request IP based on Mac as a Key
Ack(IP, Update Date, Authentication)
Create STB IP
Inform.
Name of column | Data type | Description
UPDATE_DATE | Varchar(20) | Time when IP information updated (This inform. is self-generated by the management server when data is received.)
STB_MAC | Varchar(18) | STB MAC Address(Data classification Key)
STB_IP | Varchar(16) | STB IP Address
AUTHENTICATION | Number(1) | STB initial boot Authentication status
REBOOT_STEP | Number(1) | 1 ~ 3
STB_SW-VER | Varchar(16) | SW version(1.5.3.1)
STB_PARTIAL_VER | Varchar(16) | Partial Patch version(5.2.3.4)
STB_MODEL | Varchar(16) | STB Model Name(TG4256)
STB IP management DB Table
3. Management Server Communication
STB ATT Program
STB Deamon
Management
Server

## Slide 27
3.2 STB Information communication Protocol(1/2)
3. Management Server Communication
The STB Deamon and STB ATT program use the ASP Post query method for communication with Management server.
① STB Deamon Communication
Item | Description
Contents | STB Daemon registers STB's IP information in the management server when STB is connected to a network.
ASP | http://Management server IP:Port No./STBInfo_Insert_new2.asp
Included Information | STB_MAC:001122334455 STB_IP:111.222.111.111 AUTHENTICATION:0(0 : No authentication, 1 : Authentication) REBOOT_STEP:1(1 ~ 3) STB_SW_VER:1.1.1.1 STB_PARTIAL_VER:0.0.0.1 STB_MODEL:TD0202 DAEMON_VER:160614 * Data Classification: &
Query method | POST
Managem. server resp. | SUCCESS : Succeed to update FAILURE : Fail to update
https://www.hmit.co.kr/control/stbinfo_insert_test.asp?STB_MAC=001122334455&STB_IP=111.222.111.111&AUTHENTICATION=0&REBOOT_STEP=1&STB_SW_VER=1.1.1.1&STB_PARTIAL_VER=0.0.0.1&STB_MODEL=AAA-AI600&DAEMON_VER=190614
♣ Sample of Test Url in Web Browser
: Transmit STB information

## Slide 28
3. Management Server Communication
Item | Description
Contents | The STB ATT program queries IP information of STB from the management server in order to access STB over the network.
ASP | http://Management server IP:Port No./STBInfo_Query_new.asp
Included Information | STB_MAC:001122334455
Query method | POST
Managem. server resp. | NOTFIND : No information with that MAC (No Information) SUCCESS : There is information with that MAC(Include Information) STB_MAC:001122334455 STB_IP:111.222.111.111 AUTHENTICATION:0(0 : No authentication, 1 : Authentication) UPDATE_DATE:2012-02-28 13:21:21 REBOOT_STEP:2 STB_SW_VER:1.1.1.1 STB_PARTIAL_VER:0.0.0.1 STB_MODEL:TD0202 * Data Classification: ,
② STB ATT Program communication
3.2 STB Information communication Protocol(2/2)
https://www.hmit.co.kr/control/stbinfo_query_test.asp?STB_MAC=001122334455
♣ Sample of Test Url in Web Browser
: Search transmitted STB information

## Slide 29
4.1 Process for screen adjustment
4. Additional Information
Smart STB display the menu that requests screen adjustment when booting after factory reset or full batch. STB daemon has a "screen adjustment scenario" in text form, and it is loaded when it runs. And it receives LOGIN messages from ATT programs when it runs. After run the screen adjustment scenario, authentication process will be run.
Full Patch
STB and ATT Agency
Screen Adjustment
Or
Authentication screen
STB Deamon
Screen adjustment
STB Deamon Installation
ATT preparation
Run Screen adjustment process
When receiving LOGIN commands from ATT program, run screen adjust-ment scenario, and then run authentication.
Perform the screen adjust-ment scenario, even if the authentication window is opened
Allow screen adjust-ment menu to be opened when ATT is ran and reset
12,1000
12,1000
12,1000
12,1000
12,1000
12,1000
12,1000
12,1000
Screen Adjustment Scenario
(STB deamon has text file)
The screen adjustment menu should be displayed when it installed in the customer's house.
Run ATT
Run ATT

## Slide 30
4.2 Middleware support for daemon(1/2)
4. Additonal Information
Item | Deamon Functions | MW Support
Deamon installation | When you boot from a USB port with a flash drive, Specific script files on flash drive should be able to run, and the scripts performed should be able to copy and execute daemons to specific areas of STB. | 
Deamon deletion | 1. When ATT is finished normally, 2. When STB boots, daemons must be deleted if the date on which they are installed is more than 24 hours old. | 
Revoke Authentication | 1. When installing daemon, 2. When you receive an order to revoke authen- tication from the ATT program, you must revoke the STB's certification. | Provide how revoke the authentication(Remove file ?)
Basic setting function | When Deamon are installed, the settings below should be set automatically. 1. Authenticate. 2. Release the children's watch restriction 3. Upgrade prohibited 4. Dynamic IP Settings | File control or support script
Collection basic information | SW update date Channel version Channel update date HDD or Memory information | Provide information collection location
PTS Collection | Collect video and audio PTS value | Provide information collection location
Collection Button/RCU signal inform. | Identify Buttons and RCU signal | Provide information collection location
Run RCU Scenario | Requires the function that can run RCU scenarios from the ATT program on the STB interface *Scenario consists of RCU key and latency time | 
Display ‘*’, when authentication number is entered | Set System property and notify ATT boot (sys.skb.hidecert) | Load System property and Display '*' when authenticating in ATT Mode. (UI development Company) # system properties System property value: sys.skb.hidecert ->1, then display '*' and 0 or NULL, then processes normally

## Slide 31
Item | Deamon Functions | MW Support
LED Control | To indicate completion of daemon installation, flash three LEDs (status, network, power) in STB every 0.5 seconds. | Provide how to control LED
Check USB Port | If the Deamon installation is complete, the LED is blinked and the status of the USB port should be checked periodically. If all USB ports are off, then proceed to the next step. | Provide how to check USB Port status
Check HDMI Port | The daemon transmits the connection status to the ATT program when the HDMI is connected at a certain stage. * Features to be added | Provide how to check HDMI Port
4. Additonal Information
4.2 Middleware support for daemon(2/2)

## Slide 32
Item | Description
Install Deamon | # Start when STB Power is off. Connect USB to STB. Turn on STB Deamon is installed when USB has deamon file during the boot During the Deamon run, authentication should be revoked not to update SW. After install Daemon, LED should be blink every 0.5s. User can pulls out the USB from the STB when LED blink. Before user pulls out the USB, STB show authentication screen.) Daemon inputs basic settings and reboot after user pulls out USB from STB. The basic settings are include the setting that user input authentication code with “*”, not real number. STB Deamon should wait to connect with ATT program after sending Step information(include IP and MAC etc) to ATT Server. ATT program connect STB Deamon and start to send command.
4. Additonal Information
4.3 Major issues